## Slide 1
JVET-P0175
AHG16/Non-CE4: A clean-up to merge list generation by removing shared merge list
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
In current VTM6.0, shared merge list is used to solve the tight cycle budget issue for 4x4 sized IBC, wherein candidate list generation may only have the budget of 12 cycles which is tight for a typical use case(400MHZ, 4K video)
Illustration of virtual cycle counts for IBC candidate list generation of VTM6.0 (actual case may be different)

## Slide 3
Introduction
By using shared merge list only for IBC mode, CU location and size information need to be stored before CU split. Consequently, a decoder needs duplicated memory to store CU shape information (location and size) as illustrated in Figure 1.
(1) CU information after splitting for usual processing
(2) CU information before splitting for shared merge list
Illustration of addition memory and logic for shared merge list

## Slide 4
Proposal
The storage cost may not be very significant. But it is unnecessary to have a specific tool with unnecessary duplicate logic and memory used only for IBC mode.
It is desired to clean up current VTM6.0 design by using an alternative method to reduce number of cycles of 4x4 IBC candidate list generation process as below:
Directly add HMVP candidate to candidate list without pruning when current CU is 4x4 IBC block.
Directly update HMVP table without pruning when current CU is 4x4 IBC block.
Remove shared merge list.
Illustration of virtual cycle counts for IBC candidate list generation of proposal(actual case may be different)

## Slide 5
Simulation results
 | All Intra Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | 0.06% | 0.10% | 142% | 97%
Class A2 | -0.79% | -0.94% | -0.91% | 144% | 95%
Class B | -0.79% | -0.66% | -0.86% | 160% | 98%
Class C | -0.27% | -0.29% | -0.25% | 161% | 99%
Class E | -1.23% | -1.31% | -1.29% | 162% | 100%
Overall | -0.62% | -0.61% | -0.64% | 155% | 98%
Class D | -0.58% | -0.69% | -0.71% | 149% | 99%
Class F | 0.02% | -0.09% | 0.01% | 100% | 101%
TGM | 0.14% | 0.13% | 0.10% | 98% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.13% | 0.02% | 0.24% | 104% | 98%
Class A2 | -0.06% | -0.12% | -0.07% | 105% | 99%
Class B | -0.14% | -0.12% | -0.34% | 108% | 100%
Class C | 0.21% | 0.09% | -0.03% | 111% | 99%
Class E |  |  |  |  | 
Overall | 0.02% | -0.03% | -0.09% | 108% | 99%
Class D | 0.07% | -0.29% | -0.34% | 111% | 99%
Class F | 0.05% | 0.04% | 0.01% | 144% | 147%
TGM | 0.10% | 0.06% | 0.03% | 96% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.09% | 0.10% | 113% | 98%
Class C | 0.03% | 0.14% | 0.03% | 117% | 100%
Class E | 0.04% | 0.46% | 0.38% | 111% | 99%
Overall | 0.02% | 0.20% | 0.15% | 114% | 99%
Class D | 0.06% | 0.30% | 0.10% | 120% | 101%
Class F | 0.11% | 0.04% | 0.60% | 96% | 97%
TGM | 0.01% | 0.17% | 0.12% | 94% | 98%
Anchor: VTM6.0
Test: IBC on + proposed method

## Slide 6
6
Conclusion
It is proposed to remove shared merge list for clean-up of IBC merge list generation. Doing so clean up the design and also reduces hardware cost by avoiding duplicate memory and logic and also simplifies specification text.

## Slide 7
7
Thank Dji for cross-check