## Slide 1
JVET-P0255
CE5-related: Bilateral filter with SAO band offset
K. Abe, T. Toma
Panasonic Corporation

## Slide 2
Introduction
The combination of bilateral filter and SAO is proposed by CE5-3.1(JVET-P0073).
It has good trade off between gain and complexity.
BIF
SAO
(BO or EO)
+
)
Current Sample
Reference Samples

## Slide 3
Introduction
 | SAO (Band Offset) | SAO (Edge Offset) | BIF
apply to | Luma + Chroma | Luma + Chroma | Luma
on / off | CTU | CTU | CTU
sample reference | 1 pixel | 3x3 pixel | 3x3 pixel
padding | no | no | yes
Offset derivation | signaling 4 offsets, select one using band of sample value | signaling 4 offsets, select one using 2 neighboring differences | no signaling, derive using LUT and 8 neighboring differences
Analysis
SAO BO is useful for subjective improving, and there is no tool which has same functionality.
The effectiveness of SAO EO and BIF is particularly overlapped.
SAO EO for chroma has not enough benefit for subjective and objective performance.
Comparison of SAO and BIF

## Slide 4
Proposal
BIF
SAO
(BO or EO)
+
Remove SAO edge offset, but still keep SAO band offset.
Both BifOffset and SaoOffset are used for the output.
coding_tree_unit( ) { | 
…. | 
if( pps_bilateral_filter_flag ) | 
bif_ctu_flag | 0: none, 1: BIF
if( slice_sao_enabled_flag) { | 
for( cIdx = 0; cIdx < 3; cIdx++ ) { | 
if( cIdx == 0 ) | 
sao_type_idx_luma | 0: none, 1: SAO BO
else if( cIdx == 1 ) | 
sao_type_idx_chroma | 0: none, 1: SAO BO
…. | 
} | 

## Slide 5
Simulation results
 | All Intra Main10 (over VTM-6.0) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.31% | 0.27% | 0.22% | 105% | 105%
Class A2 | -0.39% | 0.18% | 0.12% | 108% | 103%
Class B | -0.34% | 0.24% | 0.23% | 108% | 105%
Class C | -0.53% | 0.07% | 0.23% | 104% | 102%
Class E | -0.44% | 0.26% | 0.16% | 103% | 103%
Overall | -0.40% | 0.20% | 0.20% | 106% | 104%
Class D | -0.47% | 0.08% | 0.06% | 104% | 102%
Class F | -0.55% | -0.03% | -0.07% | 106% | 104%
TGM | -0.38% | -0.02% | 0.00% | 104% | 105%
CE5-3.1
 | Random Access Main10 (over VTM-6.0) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.34% | 0.11% | 0.00% | 102% | 107%
Class A2 | -0.42% | 0.13% | 0.21% | 102% | 99%
Class B | -0.43% | 0.43% | 0.28% | 104% | 102%
Class C | -0.53% | 0.38% | 0.35% | 103% | 101%
Overall | -0.44% | 0.29% | 0.23% | 103% | 102%
Class D | -0.61% | 0.12% | 0.26% | 103% | 101%
Class F | -0.51% | 0.05% | 0.06% | 104% | 101%
TGM | -0.30% | -0.04% | -0.03% | 103% | 103%
 | Low delay B Main10 (over VTM-6.0) |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.19% | 0.62% | 0.46% | 103% | 102%
Class C | -0.50% | 0.63% | 0.68% | 101% | 102%
Class E | -0.28% | 0.81% | 1.15% | 102% | 102%
Overall | -0.32% | 0.67% | 0.71% | 102% | 102%
Class D | -0.75% | 0.93% | 1.15% | 103% | 100%
Class F | -0.33% | 0.65% | 0.86% | 103% | 100%
TGM | -0.43% | -0.02% | -0.11% | 102% | 101%
All Intra Main10 (over VTM-6.0) |  |  |  | 
Y | U | V | EncT | DecT
-0.34% | 0.49% | 0.35% | 108% | 103%
-0.38% | 0.50% | 0.32% | 109% | 101%
-0.32% | 0.32% | 0.42% | 109% | 103%
-0.56% | 0.39% | 0.68% | 111% | 109%
-0.42% | 0.23% | 0.16% | 108% | 110%
-0.40% | 0.38% | 0.41% | 109% | 105%
-0.48% | 0.19% | 0.20% | 109% | 109%
-0.25% | 0.33% | 0.45% | 106% | 105%
1.51% | 0.53% | 0.61% | 104% | 103%
Random Access Main10 (over VTM-6.0) |  |  |  | 
Y | U | V | EncT | DecT
-0.31% | 0.37% | 0.23% | 102% | 109%
-0.31% | 0.55% | 0.46% | 103% | 101%
-0.34% | 0.63% | 0.73% | 105% | 106%
-0.53% | 0.64% | 0.65% | 104% | 110%
-0.38% | 0.56% | 0.55% | 103% | 106%
-0.74% | 0.13% | 0.23% | 103% | 114%
-0.10% | 0.46% | 0.51% | 105% | 110%
1.61% | 0.52% | 0.53% | 104% | 104%
Low delay B Main10 (over VTM-6.0) |  |  |  | 
Y | U | V | EncT | DecT
-0.05% | 1.45% | 2.08% | 105% | 107%
-0.47% | 1.07% | 1.52% | 105% | 106%
-0.18% | 0.29% | 1.03% | 105% | 108%
-0.22% | 1.03% | 1.63% | 105% | 107%
-0.79% | 1.32% | 1.60% | 106% | 106%
0.29% | 0.55% | 1.38% | 105% | 105%
1.87% | 1.05% | 1.16% | 103% | 100%
All Intra Main10 (over VTM-6.0) |  |  |  | 
Y | U | V | EncT | DecT
-0.34% | 0.20% | -0.10% | 106% | 104%
-0.36% | 0.14% | 0.11% | 106% | 102%
-0.34% | 0.26% | 0.26% | 107% | 104%
-0.52% | 0.06% | 0.23% | 106% | 102%
-0.43% | 0.24% | 0.17% | 106% | 104%
-0.40% | 0.18% | 0.15% | 107% | 103%
-0.48% | 0.11% | 0.12% | 105% | 103%
-0.55% | -0.03% | -0.12% | 105% | 104%
-0.44% | -0.04% | -0.02% | 104% | 105%
Random Access Main10 (over VTM-6.0) |  |  |  | 
Y | U | V | EncT | DecT
-0.32% | 0.17% | 0.09% | 103% | 103%
-0.33% | 0.21% | 0.21% | 103% | 101%
-0.37% | 0.41% | 0.30% | 104% | 102%
-0.52% | 0.40% | 0.34% | 104% | 101%
-0.39% | 0.32% | 0.25% | 104% | 102%
-0.68% | 0.06% | 0.37% | 103% | 101%
-0.48% | 0.04% | 0.03% | 103% | 102%
-0.32% | -0.03% | -0.05% | 103% | 103%
Low delay B Main10 (over VTM-6.0) |  |  |  | 
Y | U | V | EncT | DecT
-0.17% | 0.82% | 0.71% | 104% | 103%
-0.47% | 0.49% | 0.37% | 104% | 101%
-0.21% | 0.63% | 1.10% | 101% | 101%
-0.28% | 0.66% | 0.70% | 103% | 102%
-0.82% | 0.85% | 0.96% | 104% | 99%
-0.25% | 0.11% | 0.30% | 103% | 101%
-0.44% | -0.14% | -0.12% | 103% | 104%
CE5-3.1 disabling SAO
Proposal

## Slide 6
6
Conclusions
On top of bilateral filter, remove SAO EO, but still keep SAO BO.
We propose to adopt either method into VVC.
The gain is similar to bilateral filter with SAO (CE5-3.1).
-0.40%, -0.39%, -0.28% for AI, RA, LDB on VTM-6.0.
SAO BO is a useful tool especially for SCC even when bilateral filter is enabled.

## Slide 7
7
Thanks Ericsson for cross-checking of the proposal.
Acknowledgments