## Slide 1
JVET-P0256
AHG15: 16x16 base scaling matrix for 64x64 TU
T. Toma, K. Abe
Panasonic Corporation

## Slide 2
2
Introduction
Currently, maximum size of base scaling matrix is 8x8.
8x8 base scaling matrix is up-sampled by 8 times to generate scaling matrix for 64xN / Nx64 TU.
Up-sampling is done by duplicating elements of base scaling matrix, so granularity of controlling quantization scale gets lower for 64xN / Nx64 TU.
Also, maximum up-sampling ratio of base scaling matrix is 4 times in HEVC.

## Slide 3
3
Proposal
16x16 base scaling matrix is used for 64xN / Nx64 TU.
Signalling and up-sampling methods are the same as those of 8x8 base matrix for 64xN / Nx64 TU.
  8x8 elements of right-bottom region of 16x16 matrix are not signalled
  Up-sampling is done by duplicating elements
Size of quantization matrix | Size of corresponding base scaling matrix
2x2 (chroma only) | 2x2
4x4 | 4x4
8x8 | 8x8
16x16 | 8x8
32x32 | 8x8
64x64 (luma only) | 16x16

## Slide 4
4
Simulation results
BD-rate is slightly lost in AI in which scaling matrices are signaled in each picture.
Scaling matrices ON (VTM 6.0)
Scaling matrices ON (Proposed)
 |  | All Intra |  |  | 
 |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 9.11% | 18.47% | 8.61% | 102% | 104%
Class A2 | 8.51% | 13.27% | 12.16% | 95% | 104%
Class B | 11.05% | 8.08% | 7.84% | 100% | 108%
Class C | 12.92% | 10.78% | 10.82% | 90% | 116%
Class E | 12.81% | 8.62% | 9.83% | 100% | 109%
Overall | 11.01% | 11.37% | 9.68% | 97% | 109%
Class D | 18.59% | 14.71% | 15.59% | 89% | 136%
Class F | 7.84% | 11.25% | 11.85% | 97% | 107%
 |  | Random access |  |  | 
 |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 5.55% | 14.68% | 7.93% | 100% | 103%
Class A2 | 4.91% | 12.02% | 11.06% | 96% | 103%
Class B | 8.47% | 8.64% | 7.94% | 98% | 106%
Class C | 8.93% | 10.71% | 10.28% | 96% | 122%
Class E |  |  |  |  | 
Overall | 7.30% | 11.08% | 9.19% | 97% | 109%
Class D | 10.33% | 10.26% | 10.78% | 95% | 169%
Class F | 5.78% | 12.00% | 13.22% | 99% | 116%
 |  | Low delay B |  |  | 
 |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 8.58% | 5.67% | 3.36% | 98% | 106%
Class C | 9.38% | 9.59% | 9.30% | 95% | 122%
Class E | 6.59% | -2.21% | -1.51% | 99% | 120%
Overall | 8.35% | 5.01% | 4.12% | 97% | 114%
Class D | 9.45% | 7.32% | 7.68% | 95% | 169%
Class F | 5.51% | 11.83% | 12.48% | 99% | 118%
 |  | All Intra |  |  | 
 |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 9.27% | 18.65% | 8.77% | 102% | 105%
Class A2 | 8.60% | 13.37% | 12.25% | 97% | 105%
Class B | 11.31% | 8.33% | 8.09% | 101% | 109%
Class C | 13.57% | 11.39% | 11.45% | 90% | 119%
Class E | 13.63% | 9.37% | 10.59% | 100% | 111%
Overall | 11.41% | 11.74% | 10.06% | 98% | 110%
Class D | 20.40% | 16.41% | 17.34% | 89% | 141%
Class F | 8.44% | 11.85% | 12.45% | 98% | 109%
 |  | Random access |  |  | 
 |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 5.57% | 14.70% | 7.95% | 99% | 104%
Class A2 | 4.93% | 12.04% | 11.07% | 96% | 104%
Class B | 8.52% | 8.69% | 7.99% | 98% | 107%
Class C | 9.05% | 10.83% | 10.41% | 96% | 125%
Class E |  |  |  |  | 
Overall | 7.35% | 11.13% | 9.24% | 97% | 110%
Class D | 10.70% | 10.63% | 11.16% | 94% | 176%
Class F | 6.03% | 12.26% | 13.49% | 99% | 119%
 |  | Low delay B |  |  | 
 |  | Over VTM-6.0 |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 8.59% | 5.68% | 3.37% | 98% | 108%
Class C | 9.39% | 9.60% | 9.31% | 95% | 125%
Class E | 6.63% | -2.17% | -1.48% | 99% | 124%
Overall | 8.37% | 5.02% | 4.14% | 97% | 117%
Class D | 9.48% | 7.35% | 7.71% | 95% | 175%
Class F | 5.55% | 11.86% | 12.52% | 100% | 121%
Custom matrices in JCTVC-F362 is used in both cases.

## Slide 5
5
Conclusion
16x16 base scaling matrix is used instead of 8x8 for 64xN and Nx64 TU so that maximum up-sampling ratio of base scaling matrix is 4 times.
It is proposed to adopt this method into VVC test model.

## Slide 6
6
Thanks MediaTek for cross-checking of the proposal.
Acknowledgments