## Slide 1: JVET-P0281 Non-CE4: Corrections on parameter calculation for PROF and BDOF
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Introduction
To correct the parameter calculation for PROF/BDOF, 3 solutions are proposed.
  Remove the bit-depth factor on parameter calculation
  Reduce the truncation error
  Prevent the 16-bit overflow

## Slide 3: Proposed method I
The bit-widths of the PROF parameters according to the input bit-depth.
  Refinement offset is calculated with gradient and motion vector difference.
    Refinement offset = (gradientH[ x ][ y ] * diffMv[ x ][ y ][ 0 ] + gradientV[ x ][ y ] * diffMv[ x ][ y ][ 1 ] + 1) >> 1
  Gradient has fixed bit-width even though it has high correlation.
    gradientH[ x ][ y ] = ( predSamples[ x + 2 ][ y ] >> shift1 ) − ( predSamples[ x ][ y ] >> shift1 )
    gradientV[ x ][ y ] = ( predSamples[ x ][ y + 2 ] >> shift1 ) − ( predSamples[ x ][ y ] >> shift1 )
  Bit-width of the motion vector difference is decided according to the input bit-depth even though it has no correlation with bit-depth.
    diffMv[ x ][ y ][ i ] = Clip3( −dmvLimit, dmvLimit − 1, diffMv[ x ][ y ][ i ])
 | predSample |  | Gradient |  |  | diffMV |  |  | Refinement offset | 
bitDepth | Min | Max | shift1 | Min | Max | dmvLimit | Min | Max | Min | Max
8 | -23268 | 23204 | 6 | -725 | 725 | 6 | -64 | 63 | -46399 | 45675
10 | -23313 | 23297 | 6 | -728 | 728 | 6 | -64 | 63 | -46591 | 45864
12 | -23324 | 23320 | 6 | -728 | 728 | 6 | -64 | 63 | -46591 | 45864
14 | -93308 | 93304 | 8 | -728 | 728 | 8 | -256 | 255 | -186367 | 185640
16 | -373244 | 373240 | 10 | -728 | 728 | 10 | -1024 | 1023 | -745471 | 744744
shift1 = Max( 6, BitDepthY − 6 )
dmvLimit = 1 << Max( 6, BitDepthY − 6 )
< For 10bit bit-depth, Min : ((86 * (-22) * 1023) + (86 * (-22) * 1023)) >> 8, Max : ((86 * 86 * 1023) + ((-22) * (-22) * 1023)) >> 8 >

## Slide 4: Proposed method I
Remove bit-depth factor on parameter calculation
  Shift1 for gradient and dmvLimit for motion vector difference are fixed.
  There is no change for input bit-depth 8 ~ 12.
  The bit-width of the refinement offset for input bit-depth 14 and 16 are not changed.
 | predSample |  | Gradient |  |  | diffMV |  |  | Refinement offset | 
bitDepth | Min | Max | shift1 | Min | Max | dmvLimit | Min | Max | Min | Max
8 | -23268 | 23204 | 6 | -725 | 725 | 6 | -64 | 63 | -46399 | 45675
10 | -23313 | 23297 | 6 | -728 | 728 | 6 | -64 | 63 | -46591 | 45864
12 | -23324 | 23320 | 6 | -728 | 728 | 6 | -64 | 63 | -46591 | 45864
14 | -93308 | 93304 | 8 | -728 | 728 | 8 | -256 | 255 | -186367 | 185640
 |  |  | 6 | -2914 | 2914 | 6 | 64 | 64 | -186495 | 183582
16 | -373244 | 373240 | 10 | -728 | 728 | 10 | -1024 | 1023 | -745471 | 744744
 |  |  | 6 | -11662 | 11662 | 6 | -64 | 64 | -746367 | 734706
Variable shift1 is set equal to Max( 6, BitDepthY − 6 ).  6
dmvLimit = 1 << Max( 6, BitDepthY − 6 )  6

## Slide 5: Proposed method I
Removing bit-depth factor on parameter calculation is extended to BDOF.
  shift1, shift2, shift3, and mvRefinedThres(Th) are fixed.
  There is no change for input bit-depth 8 ~ 12.
  The bit-width of the refinement offset for input bit-depth 14 and 16 are not changed.
 | predSample |  | Gradient |  |  | diff |  |  | tempH, tempV |  |  | diffMV |  |  | Refinement offset | 
bitDepth | Min | Max | shift1 | Min | Max | shift2 | Min | Max | shift3 | Min | Max | Th | Min | Max | Min | Max
8 | -25022 | 24958 | 6 | -779 | 779 | 4 | -3122 | 3122 | 1 | -779 | 779 | 5 | -32 | 31 | -49856 | 48298
10 | -25071 | 25055 | 6 | -782 | 782 | 4 | -3131 | 3131 | 1 | -782 | 782 | 5 | -32 | 31 | -50048 | 48484
12 | -25083 | 25079 | 6 | -782 | 782 | 4 | -3134 | 3134 | 1 | -782 | 782 | 5 | -32 | 31 | -50048 | 48484
14 | -100347 | 100343 | 8 | -782 | 782 | 6 | -3134 | 3134 | 3 | -195 | 195 | 7 | -128 | 127 | -200192 | 198628
 |  |  | 6 | -3134 | -3134 | 4 | -12542 | 12542 | 1 | -3134 | -3134 | 5 | -32 | 31 | -200576 | 194308
16 | -401403 | 401399 | 10 | -782 | 782 | 8 | -3134 | 3134 | 5 | -48 | 48 | 9 | -512 | 511 | -800768 | 799204
 |  |  | 6 | -12542 | 12542 | 4 | -50174 | 50174 | 1 | -12542 | 12542 | 5 | - 32 | 31 | -802688 | 777604
The variable shift1 is set to equal to Max( 6, bitDepth − 6 ).  6
The variable shift2 is set to equal to Max( 4, bitDepth − 8 ).  4
The variable shift3 is set to equal to Max( 1, bitDepth − 11 ).  1
The variable mvRefineThres is set equal to 1 << Max( 5, bitDepth − 7 ).  1<< 5

## Slide 6: Experimental results
Simulation results (TEST1 in JVET-P0281)
  Proposed Method I : Remove the bit-depth factor on parameter calculation for PROF/BDOF
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 99% | 101% |  |  |  |  | 
Class A2 | 0.00% | 0.00% | 0.00% | 99% | 100% |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 98% | 102% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class C | 0.00% | 0.00% | 0.00% | 96% | 96% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 99% | 103%
Overall | 0.00% | 0.00% | 0.00% | 98% | 100% | 0.00% | 0.00% | 0.00% | 99% | 101%
Class D | 0.00% | 0.00% | 0.00% | 94% | 91% | 0.00% | 0.00% | 0.00% | 98% | 100%
Class F | 0.00% | 0.00% | 0.00% | 96% | 98% | 0.00% | 0.00% | 0.00% | 99% | 103%

## Slide 7: Proposed method II
  Reduce the truncation error
  Right-shift (6 for 10-bit input) operation at gradient calculation stage make truncation error.
  Reduce the truncation error, right-shift operation is performed at final offset calculation stage.
Variable shift1 is set equal to Max( 6 7, BitDepthY – 6 5 ).
Variable gradLimit is set equal to 1 << Max( 15, BitDepth + 3 )
For x =0..sbWidth − 1, y =0..sbHeight − 1, the following ordered steps apply:
The variables gradientH[ x ][ y ] and gradientV[ x ][ y ] are derived as follows:
gradientH[ x ][ y ] = Clip3 ( -gradLimit , gradLimit – 1, ( predSamples[ x + 2 ][ y ] >> shift1 ) − ( predSamples[ x ][ y ] >> shift1 ) ) (8‑796)
gradientV[ x ][ y ] = Clip3 ( -gradLimit , gradLimit – 1, ( predSamples[ x ][ y + 2 ] >> shift1 ) − ( predSamples[ x ][ y ] >> shift1 ) ) (8‑797)
The variable dI is derived as follows:
dI = (gradientH[ x ][ y ] * diffMv[ x ][ y ][ 0 ]) >> shift1 + (gradientV[ x ][ y ] * diffMv[ x ][ y ][ 1 ]) >> shift1 (8‑798)
Prediction sample value at location ( x, y ) in the subblock is derived as follows:
pbSamples[ x ][ y ] = predSamples[ x + 1 ][ y + 1 ] + ( ( dI + 1 ) >> 1 ) (8‑799)
 | Current design | Proposed design
gradientH/V | >> 6 | Clipping
dI | - | >> 7
Final offset | >> 1 | X

## Slide 8: Proposed method II
Extension to BDOF
Reduce the truncation error, right-shift operation is performed at final offset calculation stage.
 | Current design | Proposed design
gradientHLX/VLX (shift1) | >> 6 | Clipping
tempH/V (shift3) | >> 1 | >> 7
bdofOffset | >> 1 | >> 7
bdofOffset = ( vx * ( gradientHL0[ x + 1 ][ y + 1 ] − gradientHL1[ x + 1 ][ y + 1 ] ) ) >> 1 shift1 (8‑819) + ( vy * (gradientVL0[ x + 1 ][ y + 1 ] − gradientVL1[ x + 1 ][ y + 1 ] ) ) >> 1 shift1
tempH[ x ][ y ] = (gradientHL0[ x ][ y ] + gradientHL1[ x ][ y ] ) >> shift3 (8‑808)
tempH[ x ][ y ] = (gradientHL0[ x ][ y ] >> shift3)+ (gradientHL1[ x ][ y ] >> shift3) (8‑808)
tempV[ x ][ y ] = (gradientVL0[ x ][ y ] + gradientVL1[ x ][ y ] ) >> shift3 (8‑809)
tempV[ x ][ y ] = (gradientVL0[ x ][ y ] >> shift3) + (gradientVL1[ x ][ y ] >> shift3) (8‑809)
gradientHL0[ x ][ y ] = Clip3 ( -gradLimit , gradLimit – 1 , ( predSamplesL0[ hx + 1 ][vy] >> shift1) − ( predSampleL0[ hx − 1 ][ vy ] ) >> shift1)) (8‑803)

## Slide 9: Experimental results
Proposed Method II : Reduce the truncation error
TEST2 in JVET-P0281 shows the results of the Method II for PROF
TEST8 in JVET-P0281 shows the results of the Method II for BDOF
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.03% | -0.01% | 99% | 101% |  |  |  |  | 
Class A2 | 0.01% | 0.04% | 0.07% | 99% | 100% |  |  |  |  | 
Class B | -0.01% | 0.11% | -0.02% | 97% | 100% | -0.02% | 0.13% | -0.01% | 99% | 100%
Class C | 0.01% | 0.03% | 0.02% | 95% | 96% | -0.03% | 0.09% | 0.03% | 98% | 99%
Class E |  |  |  |  |  | -0.05% | 0.09% | 0.14% | 98% | 101%
Overall | 0.00% | 0.06% | 0.01% | 97% | 99% | -0.03% | 0.11% | 0.04% | 99% | 100%
Class D | -0.02% | -0.05% | -0.05% | 94% | 91% | -0.04% | 0.62% | 0.35% | 98% | 100%
Class F | 0.00% | 0.03% | -0.02% | 96% | 97% | 0.09% | 0.24% | 0.30% | 98% | 100%
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B |  |  |  |  |  |  |  |  |  | 
Class C |  |  |  |  |  |  |  |  |  | 
Class E |  |  |  |  |  |  |  |  |  | 
Overall |  |  |  |  |  |  |  |  |  | 
Class D |  |  |  |  |  |  |  |  |  | 
Class F |  |  |  |  |  |  |  |  |  | 

## Slide 10: Proposed method III
Prevent the 16-bit overflow for PROF
  Prediction samples are in [-23313, 23297] range.
  Refinement offsets are in [-46591, 45864] range.
  Refined prediction samples are in [-69904, 69161] range.
  To prevent the 16-bit overflow, refinement offsets are restricted to [-8192, 8191]
Extension to BDOF
  Prediction samples are in [-25071, 25055] range.
  Refinement offsets are in [-50048, 48484] range.
  Refined prediction samples are clipped to 16-bit range.
  To reduce the effect of the refinement offset, refinement offsets are restricted to [-4096, 4095]

## Slide 11: Experimental results
TEST9 in JVET-P0281 shows the results of the Method III for BDOF
Proposed Method III : Prevent the 16-bit overflow
TEST3 in JVET-P0281 shows the results of the Method III for PROF
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | 0.00% | 99% | 99% |  |  |  |  | 
Class A2 | 0.00% | 0.00% | 0.00% | 99% | 99% |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 98% | 99% | 0.00% | -0.01% | -0.01% | 100% | 99%
Class C | 0.00% | 0.00% | 0.00% | 96% | 96% | 0.00% | 0.00% | 0.00% | 99% | 100%
Class E |  |  |  |  |  | 0.00% | 0.00% | 0.00% | 99% | 99%
Overall | 0.00% | 0.00% | 0.00% | 98% | 98% | 0.00% | 0.00% | 0.00% | 99% | 99%
Class D | 0.00% | 0.00% | 0.00% | 94% | 92% | 0.00% | 0.00% | 0.00% | 98% | 98%
Class F |  |  |  |  |  | 0.07% | 0.20% | 0.00% | 99% | 98%
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.00% | -0.01% | 100% | 100% | 0.00% | 0.00% | -0.01% | 100% | 100%
Class A2 | 0.00% | 0.01% | 0.01% | 100% | 100% | 0.00% | 0.01% | 0.01% | 100% | 100%
Class B | 0.00% | 0.05% | 0.01% | 99% | 99% | 0.00% | 0.05% | 0.01% | 99% | 99%
Class C | -0.01% | 0.00% | 0.00% | 97% | 97% | -0.01% | 0.00% | 0.00% | 97% | 97%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.00% | 0.02% | 0.00% | 99% | 99% | 0.00% | 0.02% | 0.00% | 99% | 99%
Class D | 0.00% | -0.03% | 0.05% | 95% | 92% | 0.00% | -0.03% | 0.05% | 95% | 92%
Class F | 0.00% | 0.03% | -0.02% | 96% | 97% | 0.00% | 0.03% | -0.02% | 96% | 97%

## Slide 12: Conclusion
Thanks to InterDigital (JVET-xxx) for crosscheck
To correct the parameter calculation for PROF/BDOF, 3 solutions are proposed.
  Remove the bit-depth factor on parameter calculation
  Reduce the truncation error
  Prevent the 16-bit overflow
The experimental results reportedly show negligible changes in BD-rate and run-time
It is recommended to consider this method in the next VTM.