## Slide 1: JVET-P0282 Non-CE4: Block size alignment between PROF and BDOF
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Proposed methods
In VTM6.0, block size constraint between PROF and BDOF is different
To align with BDOF, block size aligning methods for affine mode are proposed.
  Method I: Block size restriction on PROF  PROF is performed at same size with BDOF, Block size for AFFINE mode is not modified.
  Method II: Block size restriction on AFFINE MERGE  PROF is performed at same size with BDOF, Both AFFINE MERGE and PROF is not performed when the block size is 8x8.
  Method III: Block size restriction on AFFINE INTER and AFFINE MERGE  PROF is performed at same size with BDOF, Both AFFINE INTER and MERGE have same condition. (8xN and Nx8 (N != 8))
 |  | AFFINE INTER | AFFINE MERGE | PROF | BDOF
VTM6.0 |  | w>=16 && h>=16 | w>=8 && h>=8 | - | w>=8 && h>=8 && w*h>=128
Proposal | Method I | w>=16 && h>=16 | w>=8 && h>=8 | w*h>=128 | w>=8 && h>=8 && w*h>=128
 | Method II | w>=16 && h>=16 | w>=8 && h>=8 && w*h>=128 | - | w>=8 && h>=8 && w*h>=128
 | Method III | w>=8 && h>=8 && w*h>=128 | w>=8 && h>=8 && w*h>=128 | - | w>=8 && h>=8 && w*h>=128

## Slide 3: Proposed methods
Proposed spec changes
  Method I: Block size restriction on PROF
If one or more of the following conditions are true, cbProfFlagLX is set equal to FALSE. sps_affine_prof_enabled_flag is equal to 0. fallbackModeTriggered is equal to 1. numCpMv is equal to 2 and cpMvLX[ 1 ][ 0 ] is equal to cpMvLX[ 0 ][ 0 ] and cpMvLX[ 1 ][ 1 ] is equal to cpMvLX[ 0 ][ 1 ]. numCpMv is equal to 3 and cpMvLX[ 1 ][ 0 ] is equal to cpMvLX[ 0 ][ 0 ] and cpMvLX[ 1 ][ 1 ] is equal to cpMvLX[ 0 ][ 1 ] and cpMvLX[ 2 ][ 0 ] is equal to cpMvLX[ 0 ][ 0 ] and cpMvLX[ 2 ][ 1 ] is equal to cpMvLX[ 0 ][ 1 ]. cbHeight * cbWidth is less than 128. Otherwise, cbProfFlagLX set equal to TRUE.

## Slide 4: Proposed methods
Proposed spec changes
  Method II: Block size restriction on AFFINE MERGE
merge_data( x0, y0, cbWidth, cbHeight, chType ) { | Descriptor
…… | 
if( MaxNumSubblockMergeCand > 0 && cbWidth >= 8 && cbHeight >= 8 && (cbWidth * cbHeight) >= 128 ) | 
merge_subblock_flag[ x0 ][ y0 ] | ae(v)
if( merge_subblock_flag[ x0 ][ y0 ] = = 1 ) { | 
if( MaxNumSubblockMergeCand > 1 ) | 
merge_subblock_idx[ x0 ][ y0 ] | ae(v)
} else { | 
…… | 
} | 

## Slide 5: Proposed methods
Proposed spec changes
  Method III: Block size restriction on AFFINE INTER and AFFINE MERGE
coding_unit( x0, y0, cbWidth, cbHeight, cqtDepth, treeType, modeType ) { | Descriptor
……. | 
if( slice_type = = B ) | 
inter_pred_idc[ x0 ][ y0 ] | ae(v)
if( sps_affine_enabled_flag && cbWidth >= 16 && cbHeight >= 16 cbWidth >= 8 && cbHeight >= 8 && (cbWidth * cbHeight) >= 128) { | 
inter_affine_flag[ x0 ][ y0 ] | ae(v)
if( sps_affine_type_flag && inter_affine_flag[ x0 ][ y0 ] ) | 
cu_affine_type_flag[ x0 ][ y0 ] | ae(v)
} | 
…… | 
} | 
merge_data( x0, y0, cbWidth, cbHeight, chType ) { | Descriptor
…… | 
if( MaxNumSubblockMergeCand > 0 && cbWidth >= 8 && cbHeight >= 8 && (cbWidth * cbHeight) >= 128 ) | 
merge_subblock_flag[ x0 ][ y0 ] | ae(v)
if( merge_subblock_flag[ x0 ][ y0 ] = = 1 ) { | 
if( MaxNumSubblockMergeCand > 1 ) | 
merge_subblock_idx[ x0 ][ y0 ] | ae(v)
} else { | 
…… | 
} | 

## Slide 6: Experimental results
Simulation results
  Method I
  Method II
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.09% | 0.01% | 100% | 101% |  |  |  |  | 
Class A2 | 0.05% | 0.01% | 0.04% | 101% | 101% |  |  |  |  | 
Class B | -0.01% | 0.05% | 0.00% | 100% | 102% | 0.00% | 0.04% | -0.05% | 101% | 99%
Class C | 0.02% | 0.04% | 0.06% | 100% | 101% | -0.03% | -0.14% | 0.10% | 100% | 100%
Class E |  |  |  |  |  | 0.00% | 0.59% | 0.88% | 100% | 102%
Overall | 0.01% | 0.05% | 0.03% | 100% | 101% | -0.01% | 0.12% | 0.23% | 100% | 100%
Class D | -0.01% | -0.03% | 0.03% | 101% | 103% | 0.01% | 0.16% | -0.13% | 100% | 99%
Class F | 0.01% | 0.00% | 0.00% | 101% | 101% | -0.02% | -0.25% | 0.25% | 100% | 101%
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.02% | -0.03% | 100% | 100% |  |  |  |  | 
Class A2 | 0.02% | 0.01% | 0.02% | 101% | 100% |  |  |  |  | 
Class B | 0.01% | 0.11% | 0.11% | 100% | 101% | 0.02% | -0.14% | -0.27% | 100% | 100%
Class C | 0.02% | 0.04% | 0.12% | 99% | 100% | -0.04% | 0.13% | 0.06% | 99% | 100%
Class E |  |  |  |  |  | -0.12% | 0.38% | 0.08% | 100% | 101%
Overall | 0.02% | 0.05% | 0.06% | 100% | 100% | -0.04% | 0.08% | -0.07% | 100% | 100%
Class D | 0.00% | -0.04% | 0.03% | 100% | 101% | 0.05% | 0.33% | 0.13% | 99% | 99%
Class F | 0.01% | 0.01% | 0.04% | 101% | 103% | 0.06% | -0.11% | 0.59% | 100% | 103%

## Slide 7: Experimental results
Simulation results
  Method III
  Method III + encoder modification
    In Encoder, affine block is selected when cost of the affine block is lower than cost of the normal block * lambda. In here, lambda is adjusted to 1.25 from 1.05.
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.03% | 102% | 100% |  |  |  |  | 
Class A2 | 0.01% | -0.02% | 0.01% | 103% | 101% |  |  |  |  | 
Class B | -0.04% | 0.04% | -0.02% | 103% | 101% | 0.00% | -0.02% | -0.30% | 106% | 100%
Class C | -0.11% | -0.05% | -0.02% | 104% | 101% | -0.11% | 0.05% | -0.04% | 107% | 100%
Class E |  |  |  |  |  | -0.03% | 0.47% | 0.21% | 105% | 102%
Overall | -0.04% | -0.01% | -0.02% | 103% | 101% | -0.05% | 0.13% | -0.09% | 106% | 101%
Class D | -0.20% | -0.03% | -0.11% | 105% | 103% | -0.15% | -0.04% | 0.24% | 106% | 99%
Class F | -0.11% | -0.09% | 0.01% | 103% | 102% | -0.05% | -0.16% | 0.14% | 104% | 100%
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Over VTM-6.0 |  |  |  |  | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -0.01% | 0.04% | 0.01% | 102% | 101% |  |  |  |  | 
Class A2 | -0.02% | -0.04% | 0.02% | 103% | 100% |  |  |  |  | 
Class B | -0.06% | -0.06% | -0.06% | 101% | 101% | 0.01% | 0.02% | 0.02% | 106% | 100%
Class C | -0.11% | -0.02% | 0.03% | 100% | 97% | -0.09% | -0.11% | -0.03% | 106% | 99%
Class E |  |  |  |  |  | 0.02% | 0.76% | 0.50% | 104% | 102%
Overall | -0.05% | -0.03% | -0.01% | 101% | 100% | -0.02% | 0.16% | 0.13% | 105% | 100%
Class D | -0.21% | -0.02% | 0.00% | 99% | 92% | -0.18% | -0.33% | 0.29% | 105% | 100%
Class F | -0.11% | -0.11% | -0.06% | 99% | 98% | -0.10% | -0.01% | 0.73% | 104% | 102%

## Slide 8: Conclusion
Thanks to Sharp (JVET-P0870) for crosscheck
To align with BDOF, block size aligning methods for affine mode are proposed.
  Method I: Block size restriction on PROF
  Method II: Block size restriction on AFFINE MERGE
  Method III: Block size restriction on AFFINE INTER and AFFINE MERGE
For Method I and II, the experimental results reportedly show negligible BD-rate changes without no changes in run-time.
For Method III, the experimental results reportedly show 0.04%(0.05%) gain in RA(LB).
It is recommended to consider this method in the next VTM.