## Slide 1: JVET-P0316
Johannes Sauer
RWTH Aachen University

## Slide 2: Uncoded areas for non-compact cubemap face arrangement
Non-compact (4x3) face arrangement
Allows usage of reference sample wrap-around
6 continous face boundaries (compact layout has only 4)
0
4
3
5
1
2
uncoded
uncoded

## Slide 3: Other applications of uncoded areas
Additional reference pictures
  Encoder needs to code different motion vector
Multi layer coding
Scalable coding
360°: Providing buffer space which can be used for high-level geometry padding
Issues:
  Dependencies of slices on other slices
Reference picture
Additional reference (empty tile)
Base layer
Upsampled base layer (empty tile)
Enhancement layer
Unused

## Slide 4: Uncoded areas using empty tiles
Allow uncoded slices, which do not hold any CTUs
Partition picture using tiles.
  Group uncoded areas/tiles into slices
  Omit corresponding slices from bitstream
  Add signaling in PPS indicating uncoded areas at tile granularity
Slices
sdf
Omitted from bitstream
Omitted from bitstream

## Slide 5: Uncoded areas using empty tiles
Allow uncoded slices, which do not hold any CTUs
Partition picture using tiles.
  Group uncoded areas/tiles into slices
  Omit corresponding slices from bitstream
  Add signaling in PPS indicating uncoded areas at tile granularity
slice_header( ) { | Descriptor
slice_pic_parameter_set_id | ue(v)
if( rect_slice_flag ¦ ¦ NumBricksInPic > 1 ¦ ¦ allow_uncoded_areas_flag ) | 
slice_address | u(v)
… | 
byte_alignment( ) | 
} | 

## Slide 6: Uncoded areas using empty tiles
Allow uncoded slices, which do not hold any CTUs
Partition picture using tiles.
  Group uncoded areas/tiles into slices
  Omit corresponding slices from bitstream
  Add signaling in PPS indicating uncoded areas at tile granularity
pic_parameter_set_rbsp( ) { | Descriptor
pps_pic_parameter_set_id | ue(v)
pps_seq_parameter_set_id | ue(v)
output_flag_present_flag | u(1)
single_tile_in_pic_flag | u(1)
if( !single_tile_in_pic_flag ) { | 
uniform_tile_spacing_flag | u(1)
if( uniform_tile_spacing_flag ) { | 
tile_cols_width_minus1 | ue(v)
tile_rows_height_minus1 | ue(v)
} else { | 
num_tile_columns_minus1 | ue(v)
num_tile_rows_minus1 | ue(v)
for( i = 0; i < num_tile_columns_minus1; i++ ) | 
tile_column_width_minus1[ i ] | ue(v)
for( i = 0; i < num_tile_rows_minus1; i++ ) | 
tile_row_height_minus1[ i ] | ue(v)
} | 
allow_uncoded_areas_flag | u(1)
if( allow_uncoded_areas_flag ) { | 
for( i = 0; i < NumTilesInPic; i++ ) { | 
tile_is_coded_flag[ i ] | u(1)
} | 
} | 
brick_splitting_present_flag | u(1)
… | 
rbsp_trailing_bits( ) | 
} | 

## Slide 7: Results #1
VTM 5.2
360CTC (HEC, face size 1280, QP 22…37, no padding)
Tested: Non-compact with reference sample wrap-around. Two face row slices. Unused regions not encoded.
Anchor: Compact layout. Single slice.
 | End-to-end WS-PSNR |  | 
 | Y | U | V
Class S1 | 0.19% | 0.48% | 0.11%
Class S2 | -0.27% | -1.25% | -1.83%
Overall | 0.01% | -0.21% | -0.66%

## Slide 8: Results #2
VTM 5.2
360CTC (HEC, face size 1280, QP 22…37, no padding)
Tested: Non-compact with reference sample wrap-around. Two face row slices. Unused regions not encoded.
Anchor: Compact layout. Two face row slices.
 | End-to-end WS-PSNR |  | 
 | Y | U | V
Class S1 | -0.23% | 0.29% | 0.09%
Class S2 | -0.65% | -1.06% | -1.29%
Overall | -0.40% | -0.25% | -0.46%

## Slide 9: Results #3
VTM 5.2
360CTC (HEC, face size 1280, QP 22…37, no padding)
Tested: Non-compact without reference sample wrap-around. Two face row slices. Unused regions not encoded.
Anchor: Compact layout. Single slice.
 | End-to-end WS-PSNR |  | 
 | Y | U | V
Class S1 | 0.29% | 0.68% | 0.33%
Class S2 | -0.10% | -0.69% | -1.36%
Overall | 0.13% | 0.13% | -0.35%

## Slide 10: Results #4
VTM 5.2
360CTC (HEC, face size 1280, QP 22…37, no padding)
Tested: Non-compact with reference sample wrap-around. Two face row slices. Unused regions are encoded.
Anchor: Compact layout. Single slice.
 | End-to-end WS-PSNR |  | 
 | Y | U | V
Class S1 | 0.84% | 1.09% | 0.91%
Class S2 | 0.15% | -0.52% | -0.97%
Overall | 0.56% | 0.44% | 0.16%

## Slide 11: Impact for moving camera sequences
Increased number of continuous face boundaries
Average gains of the moving camera sequences in WS-PSNR are 0.25% (Y), 0.78% (U) and 1.24% (V)
Likely also has subjective benefits
Usage of reference sample wraparound:

## Slide 12: Problems
Increased buffer space (twice of compact layour)
  Implementation issue, since empty regions are never used
Interference with padding
  potentially reduces number of continuous face boundaries
0
4
3
5
1
2
2
3

## Slide 13: Conclusion
Further study of non-compact cube face arrangement using uncoded areas
Exploration of other applications of uncoded areas
Recommendation
  Add support for uncoded areas to VVC