## Slide 1
Non-CE4: BCW clean-up for weight signalling
JVET-P0317
The 16th JVET Meeting
Oct. 2019
Dohyeon Park, Yong-Uk Yoon, Jihoon Do, Jae-Gon Kim (KAU)
Jinho Lee, Jungwon Kang (ETRI)

## Slide 2: I. Introduction
BCW weights are restricted depending on
  indicates if there is no future picture in the display order among the reference pictures
Issues on the parsing of bcw_idx
  Normative restriction on the possible weights can violate the decoding flexibility
  NoBackwardPredFlag may cause a dependency
bcw_idx | Weights | Code word (NoBackwardPredFlag == 1) | Code word (NoBackwardPredFlag == 0)
0 | 4 | 0 | 0
1 | 5 | 10 | 10
2 | 3 | 110 | 11
3 | 10 | 1110 | Not allowed
4 | -2 | 1111 | Not allowed

## Slide 3: II. Proposed Simplification
Proposed clean-up
  Removing the condition check of NoBackwardPredFlag at the parsing of bcw_idx ()
  The adjustment on the number of available weights could be handled non-normatively
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
bcw_idx[ ][ ] NoBackwardPredFlag = = 0 | 0 | bypass | na | na | na | na
bcw_idx[ ][ ] NoBackwardPredFlag = = 1 | 0 | bypass | bypass | bypass | na | na

## Slide 4: III. Experimental Results
Anchor: VTM6.0 with CTC, Test: anchor + proposed method
The algorithm for weight searching in VTM6 is not changed
  3 weights are searched in RA (the same as in VTM6)
 | Random access |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | 0.05% | 0.04% | 100% | 101%
Class A2 | 0.04% | 0.06% | 0.06% | 100% | 101%
Class B | 0.02% | 0.08% | -0.04% | 100% | 101%
Class C | 0.02% | 0.09% | 0.03% | 100% | 102%
Class E |  |  |  |  | 
Overall | 0.02% | 0.07% | 0.02% | 100% | 101%
Class D | -0.01% | -0.06% | 0.12% | 100% | 102%
Class F | 0.01% | 0.02% | 0.01% | 100% | 101%
 | Low delay B |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.00% | 0.00% | 101% | 97%
Class C | 0.00% | 0.00% | 0.00% | 100% | 99%
Class E | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 99%
Class D | 0.00% | 0.00% | 0.00% | 99% | 98%
Class F | 0.00% | 0.00% | 0.00% | 100% | 95%

## Slide 5: IV. Conclusions
The proposed clean-up
  It presents a clean-up design for the syntax of BCW which removes the condition check of NoBackwardPredFlag at the parsing of bcw_idx
  It resolves the flexibility and latency issues of BCW with negligible loss
Experimental results show that 0.02% and 0.00% luma BD-rate performance for RA and LDB, respectively, in the proposed method
It is recommended to consider the proposed method in the next VTM