## Slide 1
CE6-related: LFNST applied to ISP mode
JVET-P0342
F. Le Léannec, K. Naser, F. Galpin, T. Poirier

## Slide 2: Motivation
In VTM-6.0 the only intra mode where LFNST is not applied is ISP
Proposal: unify the design of VVC by allowing LFNST with ISP

## Slide 3: Proposal description
LFNST can be applied in ISP CU with size at least 16 in width and height (same as for LFNST/MIP combination)
If LFNST is applied in an ISP CU, then the primary 2D transform used is always DCT2-DCT2.
The last non-zero position and DC only conditions to code LFNST index are unchanged compared to VTM6
LFNST index first bin uses duplicated CABAC contexts based on the use of ISP in considered CU
If LFNST is active in a given ISP CU, then it applies to every TU in that CU.

## Slide 4: Results
Performances over VTM-6.0

## Slide 5: Method 2 proposed
LFNST can be applied in ISP CU if ISP splitting leads to TU sizes at least equal to 4x4
If LFNST is applied in an ISP CU, then the primary 2D transform used is always DCT2-DCT2.
The last non-zero position and DC only conditions to code LFNST index are unchanged compared to VTM6
LFNST index first bin uses duplicated CABAC contexts based on the use of ISP in considered CU
If LFNST is active in a given ISP CU, then it applies to every TU in that CU.

## Slide 6: Results of method 2
Performances over VTM-6.0

## Slide 7: Conclusion
Proposed to allow the combined use of LFNST and ISP
Unifies the design of VVC w.r.t. LFNST interaction with other tools
Coding efficiency:
  Slight gain in every class in RA, limited impact in AI.
  BD-rate improved in the currently running method 2
  May provide coding efficiency improvement with a better adapted RDO
    See JVET-P0392
Thanks to HHI for cross-checking