## Slide 1: JVET-P0372 CE5-related: Joint chroma cross-component adaptive loop filtering
Hua Yang, Yuwen He, Hongyu Li
Oct 2019

## Slide 2: CCALF
Complexity issue
  ~1% Y BD-rate RA gain, but 50% complexity increase over ALF
The idea
  CCALF is applied on Cb, Cr, separately.
  However, correlation exists between Cb, Cr refinement signals.

## Slide 3: Joint chroma CCALF (JC-CCALF)
The used ALF filter is trained and coded once and used for both Cb and Cr refinement.
SAO Luma
ALF Luma
SAO Cb
SAO Cr
Joint chroma
CC ALF
ALF Chroma
Y
Cb
Cr
w

## Slide 4: JC-CCALF
Weighting factor:
  One per slice
  Sign (1 bit) and index (3 bits)
Encoder fast search:
  Prioritized weight list of all the possible values
  Early termination, if two consecutive weight values give no RD improvement.
  Previous coded same-type slice weight: the 1st to check (i.e. highest priority)
Cb, Cr use two separate block-level on/off control maps
  One same coded control block size for both Cb, Cr
  Encoder iterative ALF coefficient training: a block is included in the current iteration of training, if the previous iteration decision on the block is “on” (i.e. to apply the ALF filtering) for both Cb and Cr.
Index | 1 | 2 | 3 | 4 | 5 | 6 | 7
¦w¦ | 1/4 | 1/2 | 3/4 | 1 | 4 | 2 | 4/3

## Slide 5
5
CCALF CE5-2.1: with chroma gain shifted to luma (Reference)
 | All Intra Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.19% | 5.37% | 3.75% | 104% | 102%
Class A2 | -2.04% | -0.29% | -0.74% | 101% | 102%
Class B | -0.74% | -1.74% | 0.92% | 101% | 102%
Class C | -0.76% | 3.98% | 4.50% | 100% | 101%
Class E | -0.46% | -2.81% | 4.71% | 101% | 102%
Overall | -0.99% | 0.78% | 2.54% | 101% | 102%
Class D | -0.75% | 5.36% | 4.85% | 100% | 100%
Class F | -0.73% | -1.03% | -1.29% | 101% | 102%
Class TGM | -1.13% | -4.80% | -4.59% | 101% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.81% | 5.25% | 4.13% | 102% | 103%
Class A2 | -2.05% | -1.14% | -6.17% | 101% | 103%
Class B | -0.54% | -6.34% | -2.25% | 102% | 102%
Class C | -0.78% | 5.75% | 6.56% | 101% | 101%
Class E |  |  |  |  | 
Overall | -1.16% | 0.24% | 0.59% | 101% | 102%
Class D | -0.64% | 6.08% | 6.42% | 101% | 102%
Class F | -0.92% | 1.86% | 2.34% | 102% | 102%
Class TGM | -1.03% | -3.59% | -4.29% | 102% | 102%
 | Low Delay B Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.54% | -9.26% | -6.60% | 101% | 106%
Class C | -0.73% | 3.86% | 5.44% | 101% | 102%
Class E | -0.24% | -5.62% | 7.60% | 104% | 102%
Overall | -0.53% | -3.98% | 0.96% | 102% | 104%
Class D | -0.56% | 4.90% | 7.37% | 101% | 101%
Class F | -0.84% | -2.82% | -0.28% | 102% | 104%
Class TGM | -1.58% | -5.48% | -5.26% | 103% | 104%

## Slide 6
6
Test 1: JC-CCALF
 | All Intra Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.03% | 5.47% | 2.62% | 103% | 102%
Class A2 | -1.72% | 2.51% | -1.24% | 101% | 101%
Class B | -0.67% | -0.81% | 1.86% | 100% | 101%
Class C | -0.70% | 4.78% | 4.26% | 100% | 101%
Class E | -0.46% | -2.73% | 4.53% | 101% | 101%
Overall | -0.87% | 1.71% | 2.45% | 101% | 101%
Class D | -0.68% | 5.36% | 4.92% | 99% | 99%
Class F | -0.67% | -0.14% | -0.99% | 100% | 100%
Class TGM | -0.84% | -4.42% | -4.85% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.60% | 5.40% | 2.88% | 103% | 103%
Class A2 | -1.76% | -0.64% | -5.98% | 102% | 103%
Class B | -0.42% | -5.36% | -2.91% | 102% | 101%
Class C | -0.67% | 5.46% | 5.15% | 101% | 101%
Class E |  |  |  |  | 
Overall | -0.99% | 0.62% | -0.22% | 102% | 102%
Class D | -0.56% | 5.94% | 6.03% | 101% | 101%
Class F | -0.87% | 2.65% | 2.03% | 103% | 101%
Class TGM | -0.80% | -3.04% | -4.24% | 103% | 101%
 | Low Delay B Main 10 |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.70% | 3.25% | 4.31% | 101% | 100%
Class E | -0.24% | -5.94% | 4.44% | 106% | 100%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.44% | 3.91% | 5.11% | 101% | 100%
Class F | -0.69% | -3.30% | -1.85% | 104% | 102%
Class TGM | -1.44% | -5.17% | -5.31% | 103% | 101%

## Slide 7: Test 2: JC-CCALF + 8-tap filter
8-tap filter
18-tap filter with 14 unique coefficients

## Slide 8
Test 2: JC-CCALF with 8-tap ALF filter (100frms, All Intra)
 | CCALF ( Anchor ) |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.15% | 7.52% | 3.84% | 104% | 102%
Class A2 | -2.02% | -0.28% | -0.33% | 99% | 103%
Class B | -0.76% | -0.20% | 1.59% | 100% | 101%
Class C | -0.74% | 3.75% | 4.57% | 99% | 94%
Class E | -0.49% | -2.68% | 4.75% | 100% | 96%
Overall | -0.99% | 1.54% | 2.83% | 100% | 99%
Class D | -0.72% | 5.09% | 5.81% | 99% | 92%
Class F | -0.72% | -2.38% | -1.70% | 100% | 96%
Class TGM | -1.18% | -4.98% | -4.60% | 100% | 102%
 | JC-CCALF |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.98% | 7.38% | 2.66% | 106% | 104%
Class A2 | -1.71% | 1.70% | -0.77% | 100% | 101%
Class B | -0.65% | 0.95% | 1.93% | 101% | 103%
Class C | -0.69% | 4.57% | 4.20% | 100% | 100%
Class E | -0.50% | -2.84% | 4.48% | 101% | 101%
Overall | -0.87% | 2.32% | 2.53% | 101% | 102%
Class D | -0.67% | 4.78% | 6.07% | 100% | 99%
Class F | -0.69% | -1.07% | -1.21% | 100% | 100%
Class TGM | -0.85% | -4.54% | -4.88% | 101% | 102%
 | JC-CCALF with 8-tap filter |  |  |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.01% | 7.48% | 3.40% | 104% | 102%
Class A2 | -1.70% | 2.04% | -0.35% | 99% | 101%
Class B | -0.67% | 1.24% | 2.48% | 100% | 102%
Class C | -0.72% | 5.08% | 4.34% | 100% | 101%
Class E | -0.52% | -2.80% | 4.62% | 100% | 100%
Overall | -0.88% | 2.59% | 2.93% | 101% | 101%
Class D | -0.72% | 5.55% | 6.38% | 100% | 98%
Class F | -0.74% | -0.43% | -0.85% | 100% | 99%
Class TGM | -0.86% | -3.82% | -4.13% | 100% | 101%

## Slide 9: Summary
Propose JC-CCALF with 8-tap filter
  Conduct ALF filtering on input luma signal once and used for both Cb and Cr refinement
  Separate block on/off control for Cb, Cr with the same control block size
  One weighting factor per slice
  8-tap ALF filter
  With 18-tap filter: RA: JC-CCALF: −0.99%/0.62%/−0.22%
  vs CCALF: −1.16%/0.24%/−0.59%
  With 8-tap filter: AI (100frms): JC-CCALF: −0.88%/2.59%/2.93%
  vs CCALF: −0.99%/1.54%/2.83%
Thank Tencent for cross-checking!
(JVET-P0704)