## Slide 1: AHG17/AHG15: On quantization control parameters signalling
R. Chernyak
S. Ikonin, T. Solovyev, M. Sosulnikov, A. Karabutov

## Slide 2
Aspect 1. Problem statement
seq_parameter_set_rbsp( ) {
…
if( ChromaArrayType != 0 ) {
same_qp_table_for_chroma
for( i = 0; i < same_qp_table_for_chroma ? 1 : 3; i++ ) {
num_points_in_qp_table_minus1[ i ]
for( j = 0; j <= num_points_in_qp_table_minus1[ i ]; j++ ) {
delta_qp_in_val_minus1[ i ][ j ]
delta_qp_out_val[ i ][ j ]
}
}
}
…
}
pic_parameter_set_rbsp( ) {
…
pps_cb_qp_offset
pps_cr_qp_offset
pps_joint_cbcr_qp_offset
pps_slice_chroma_qp_offsets_present_flag
cu_chroma_qp_offset_enabled_flag
if( cu_chroma_qp_offset_enabled_flag ) {
cu_chroma_qp_offset_subdiv
chroma_qp_offset_list_len_minus1
for( i = 0; i <= chroma_qp_offset_list_len_minus1; i++ ) {
cb_qp_offset_list[ i ]
cr_qp_offset_list[ i ]
joint_cbcr_qp_offset_list[ i ]
}
}
…
}
slice_header( ) {
…
if( sps_joint_cbcr_enabled_flag )
slice_joint_cbcr_sign_flag
slice_qp_delta
if( pps_slice_chroma_qp_offsets_present_flag ) {
slice_cb_qp_offset
slice_cr_qp_offset
if( sps_joint_cbcr_enabled_flag )
slice_joint_cbcr_qp_offset
}
…
}
JCCR related syntax is being handled differently and redundantly in some cases

## Slide 3
Aspect 1. Proposal
seq_parameter_set_rbsp( ) {
…
if( ChromaArrayType != 0 ) {
same_qp_table_for_chroma
for( i = 0; i < same_qp_table_for_chroma ? 1 : (sps_joint_cbcr_enabled_flag ? 3 : 2); i++ ) {
num_points_in_qp_table_minus1[ i ]
for( j = 0; j <= num_points_in_qp_table_minus1[ i ]; j++ ) {
delta_qp_in_val_minus1[ i ][ j ]
delta_qp_out_val[ i ][ j ]
}
}
}
…
}
pic_parameter_set_rbsp( ) {
…
pps_cb_qp_offset
pps_cr_qp_offset
if( sps_joint_cbcr_enabled_flag )
pps_joint_cbcr_qp_offset
pps_slice_chroma_qp_offsets_present_flag
cu_chroma_qp_offset_enabled_flag
if( cu_chroma_qp_offset_enabled_flag ) {
cu_chroma_qp_offset_subdiv
chroma_qp_offset_list_len_minus1
for( i = 0; i <= chroma_qp_offset_list_len_minus1; i++ ) {
cb_qp_offset_list[ i ]
cr_qp_offset_list[ i ]
if( sps_joint_cbcr_enabled_flag )
joint_cbcr_qp_offset_list[ i ]
}
}
…
}
It is proposed to simply add missed JCCR conditions to SPS and PPS to:
Avoid redundant signaling
Make this part consistent

## Slide 4
Aspect 2. Problem statement
slice_header( ) { | Descriptor
… | 
if( pps_slice_chroma_qp_offsets_present_flag ) { | 
slice_cb_qp_offset | se(v)
slice_cr_qp_offset | se(v)
if( sps_joint_cbcr_enabled_flag ) | 
slice_joint_cbcr_qp_offset | se(v)
} | 
… | 
} | 
slice_cb_qp_offset specifies a difference to be added to the value of pps_cb_qp_offset when determining the value of the Qp′Cb quantization parameter. The value of slice_cb_qp_offset shall be in the range of −12 to +12, inclusive. When slice_cb_qp_offset is not present, it is inferred to be equal to 0.
Do we need to signal and maintain pps_slice_chroma_qp_offsets_present_flag?
Slice QP offsets are signaled as se(v), which allows to signal zero value

## Slide 5
Aspect 2. Proposal
pic_parameter_set_rbsp( ) {
…
pps_joint_cbcr_qp_offset
pps_slice_chroma_qp_offsets_present_flag
cu_chroma_qp_offset_enabled_flag
…
}
slice_header( ) {
…
if( pps_slice_chroma_qp_offsets_present_flag ) {
slice_cb_qp_offset
slice_cr_qp_offset
if( sps_joint_cbcr_enabled_flag )
slice_joint_cbcr_qp_offset
}
…
}
pps_slice_chroma_qp_offsets_present_flag equal to 1 indicates that the slice_cb_qp_offset and slice_cr_qp_offset syntax elements are present in the associated slice headers. pps_slice_chroma_qp_offsets_present_flag equal to 0 indicates that these syntax elements are not present in the associated slice headers. When ChromaArrayType is equal to 0, pps_slice_chroma_qp_offsets_present_flag shall be equal to 0.
slice_cb_qp_offset specifies a difference to be added to the value of pps_cb_qp_offset when determining the value of the Qp′Cb quantization parameter. The value of slice_cb_qp_offset shall be in the range of −12 to +12, inclusive. When slice_cb_qp_offset is not present, it is inferred to be equal to 0.

## Slide 6
Aspect 2. Benefits
Less syntax to be signalled
Less conditions during signalling
Less and cleaner spec text
No redundancy in Slice Chroma QP offsets signalling