## Slide 1: JVET-P0427 AHG17: Bugfixes on constant slice header parameters
​Yao-Jen Chang, Vadim Seregin, Muhammed Coban, Adarsh Ramasubramonian, Marta Karczewicz
​
​Geneva, CH
​Oct. 2019

## Slide 2: Background on constant flag in PPS
Suppose constant_slice_header_params_enabled_flag = 1 (O0238)
  Syntax element can be either signaled in PPS or picture header
    If pps_six_minus_max_num_merge_cand_plus1 = 0, slice_six_minus_max_num_merge_cand is signaled in picture header
    Otherwise, pps_six_minus_max_num_merge_cand_plus1 > 0, then slice_six_minus_max_num_merge_cand is NOT signaled in picture header

## Slide 3: Background on the number of triangular merging candidates
The conformance of slice_max_num_merge_cand_minus_max_num_triangle_cand_plus1 (N0400/0500/0447/0851)
  MaxNumMergeCand >= MaxNumTriangleMergeCand
    If violated, there is no enough candidates in triangle merge list which reuses the regular merge list
  MaxNumTriangleMergeCand shall be larger than or equal to 2
    Triangle merge list requires at least two different merging candidates for two triangle blocks
  MaxNumTriangleMergeCand shall be zero if MaxNumMergeCand is equal to 1

## Slide 4: Issue
PPS cannot understand what the numbers of MaxNumMergeCand are if the values of MaxNumMergeCand are derived in picture headers by slice_six_minus_max_num_merge_cand
MaxNumMergeCand >= MaxNumTriangleMergeCand might be violated if the values of MaxNumMergeCand are derived in picture header, and the value of MaxNumTriangleMergeCand is derived in PPS by pps_max_num_merge_cand_minus_max_num_triangle_cand_plus1

## Slide 5: Proposed 1
Derive MaxNumMergeCand and MaxNumTriangleMergeCand together in either PPS or picture header.
Proposed 1: A conformance to enforce MaxNumTriangleMergeCand derived in picture header if MaxNumMergeCand is derived in picture header
  Infer pps_max_num_merge_cand_minus_max_num_triangle_cand_plus1 to be equal to zero if pps_six_minus_max_num_merge_cand_plus1 is equal to zero

## Slide 6: Proposed 2
Proposed 2: The range of pps_max_num_merge_cand_minus_max_num_triangle_cand_plus1 is changed from “0 to 6 – pps_six_minus_max_num_merge_cand_plus1” to “0 to MaxNumMergeCand − 1”
  Derivation: 6 – (pps_six_minus_max_num_merge_cand_plus1 – 1) = 7 – pps_six_minus_max_num_merge_cand_plus1.

## Slide 7: Proposed 3
MaxNumTriangleMergeCand shall be 2 if MaxNumMergeCand = 2
Proposed 3: Cleanup the syntax by inferring MaxNumTriangleMergeCand = 2 if MaxNumMergeCand = 2
if( sps_triangle_enabled_flag && MaxNumMergeCand >= > 2 && !pps_max_num_merge_cand_minus_max_num_triangle_cand_plus1 ) | 
max_num_merge_cand_minus_max_num_triangle_cand | ue(v)