## Slide 1: JVET-P0460: Non-CE8: Minimum QP for Palette Escape Coding
J. Zhao, S. Paluri S. Kim
LG ELECTRONICS

## Slide 2: Introduction
In July meeting, minimum Allowed QP for Transform Skip Mode (JVET-O0405) was adopted.
In palette mode escape coding, there is no transform. This is similar to transform skip mode.
Proposes to limit the minimum Qp used in escape mode coding as well.

## Slide 3: Background
Currently in VVC 6, when transform skip is used, the QP is derived as
qP = Max( QpPrimeTsMin, Qp′Y )
QpPrimeTsMin, is set as 6* (internalBitDepth – inputBitDepth)) at encoder side, and min_qp_prime_ts_ minus4 is signalled in SPS
QpPrimeTsMin = 4 + min_qp_prime_ts_ minus4
This prevents cases in which the effective quantization step size for transform skip becomes smaller than 1. It also shows coding gain at low Qp.

## Slide 4: Proposed
Palette escape mode does not have transform, escape values are quantized directly, this is similar to transform skip mode.
So propose that that minimum QP limitation should be applied to palette escape coding
For luma, qP = Max( 0 QpPrimeTsMin, Qp′Y )
For Cb, qP = Max( 0 QpPrimeTsMinChroma, Qp′Cb
For Cr, qP = Max( 0 QpPrimeTsMinChroma, Qp′Cr )

## Slide 5: Proposed
QpPrimeTsMinChroma can be signalled and derived in similar ways as QpPrimeTsMin
  Signal min_qp_prime_chroma_ts_minus4 in SPS
  QpPrimeChromaTsMin = 4 + min_qp_prime_chroma_ts_ minus4

## Slide 6: Results ( Low QP Dual Tree Off)
 |  |  | All Intra Main10 |  | 
 | Over VTM6.0 CE8 base |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | 0.08% | -0.94% | -0.98% | 100% | 100%
TGM 720p | 0.03% | -0.30% | -0.30% | 100% | 99%
Animation | 0.00% | -0.01% | -0.01% | 100% | 99%
Mixed content | 0.06% | -0.27% | -0.31% | 101% | 100%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 99%
Overall | 0.04% | -0.36% | -0.38% | 100% | 100%

## Slide 7: Results ( Low QP Dual Tree Off)
 | Random access Main10 |  |  |  | 
 | Over VTM6.0 CE8 base |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.57% | -0.55% | -0.54% | 99% | 99%
TGM 720p | -0.45% | -0.41% | -0.43% | 100% | 98%
Animation | 0.00% | -0.01% | -0.01% | 99% | 99%
Mixed content | -0.41% | -0.38% | -0.40% | 100% | 99%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | -0.33% | -0.31% | -0.32% | 100% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM6.0 CE8 base |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.01% | -0.30% | -0.29% | 100% | 100%
TGM 720p | 0.11% | -0.19% | -0.17% | 100% | 99%
Animation | 0.00% | -0.01% | 0.00% | 100% | 100%
Mixed content | 0.05% | -0.33% | -0.34% | 100% | 100%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.03% | -0.18% | -0.18% | 100% | 100%

## Slide 8: Results ( Low QP Dual Tree On)
 |  |  | All Intra Main10 |  | 
 | Over VTM6.0 CE8 base |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | 0.01% | -0.97% | -0.93% | 100% | 100%
TGM 720p | 0.05% | -0.25% | -0.24% | 100% | 99%
Animation | 0.04% | -0.06% | -0.09% | 100% | 100%
Mixed content | 0.05% | -0.75% | -0.75% | 100% | 100%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.03% | -0.46% | -0.45% | 100% | 100%

## Slide 9: Results ( Low QP Dual Tree On)
 | Random access Main10 |  |  |  | 
 | Over VTM6.0 CE8 base |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.26% | -0.60% | -0.57% | 98% | 98%
TGM 720p | -0.22% | -0.41% | -0.49% | 99% | 98%
Animation | 0.01% | -0.05% | -0.05% | 100% | 99%
Mixed content | -0.24% | -0.35% | -0.34% | 100% | 98%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | -0.16% | -0.33% | -0.34% | 99% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM6.0 CE8 base |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.06% | -0.23% | -0.24% | 99% | 100%
TGM 720p | 0.06% | -0.20% | -0.21% | 100% | 100%
Animation | 0.00% | -0.01% | -0.01% | 100% | 100%
Mixed content | 0.05% | -0.35% | -0.34% | 99% | 100%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 101%
Overall | 0.01% | -0.17% | -0.18% | 100% | 100%

## Slide 10: Conclusion
Propose to limit the minimum QP of palette escape mode similar to transform skip mode minimum Qp
Thanks for ByteDance for cross-checking. (JVET-P0798)