## Slide 1: AHG9: Multiple Convolution Neural Networks For Sequence-Independent Processing (JVET-P0489)
Hujun Yin, Rongzhen Yang, Xiaoran Fang, Zheng Gao and Ruiqi Yang
Oct.1, 2019

## Slide 2: Sequence Independent Multiple CNNs Method
In this contribution, the previous multi-CNNs solution was applied to sequence independent, target to:
  Post filter, the application of CNNs can be optional in the decoding to relax the limitation of complexity, which may be optional enabled in decoder side by using SEI message.
  Multiple CNNs with deeper network structure may explore the higher gain on CTC sequences
One example of 3 CNNs with post filtering:

## Slide 3: Multiple CNNs Method – Single Network Structure
Based on previous design concept, with deep and wider network structure:
  For Luma, 6 channels (packed) input with 4 channels output (367,296 parameters)
  For Chroma, 6 channels (packed) input with 2 channels output (366,144 parameters)

## Slide 4: Training Process for Multiple-CNN
The previous reinforcement training process is tested
The training data sets: DIV2K 800 images (with QP22/27/32/37)
To accelerate the training, the simplified training process is used for some QPs.
Example of One CNN Training in Tensor Board
Example of Multi CNNs training process
Simplified Multiple CNN Training Process

## Slide 5: Experiment Setup - Training
Mandatory | Information in Training Stage |  | 
 | Basic Settings: |  | 
 |  | learning rate: | 0.0003
 |  | optimizer: | ADAM
 |  | batch size: | 512
 |  | epoch: | 512
 |  | loss function: | L1
 |  | training GPU: | GTX Titan V
 |  | training time: | ~48 hours
 |  | framework: | Tensor Flow
offline training based on DIV2K
QP values {22,27,32,37} are used
Training time measured per QP per Luma/Chroma

## Slide 6: Experimental Results on CTC-RA, Post Filter
Overall gain on Post Filter: Y: -1.47%; U: -10.81%; V: -9.29%

## Slide 7: Conclusion
In this contribution:
  Extending the multi-CNNLFs solution to sequence independent method
  Better performance, it can be further optimized with more training data and time
It is recommend the continue study of post filter mode in AHG that may be optional enabled in decoder side by using SEI message.