## Slide 1
JVET-P0529
Non-CE8: QP dependent binarization for palette escape
Hong-Jheng Jhu, Yi-Wen Chen, Xiaoyu Xiu, Tsung-Chuan Ma, Xianglin Wang

## Slide 2: Introduction
In current VVC, the binarization of escape samples is derived by invoking the third order Exp-Golomb binarization process

## Slide 3: The Proposed Methods
Test 1: it is proposed to limit the minimum QP used in escape mode coding to be consistent with Transform skip minimum QP
Test 2: it is proposed to use the fix-length binarization process for escape samples base on Test1
  Length of fix-length binarization : (bitDepth – ((Qp – 4)/6))).
Test 3: QP remapping is introduced base on Test2
  QPesca = ((MAX( 4 , QPcu ) – 2) / 6) * 6 + 4

## Slide 4
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.10% | -0.19% | -0.19% | 99% | 100%
TGM 720p | 0.18% | -0.21% | -0.06% | 97% | 100%
Animation | -0.02% | -0.02% | 0.00% | 97% | 99%
Mixed content | -0.06% | -0.09% | -0.16% | 99% | 99%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 96% | 97%
Overall | 0.01% | -0.12% | -0.09% | 98% | 99%
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.06% | -0.02% | -0.05% | 98% | 99%
TGM 720p | -0.09% | -0.05% | 0.01% | 95% | 100%
Animation | -0.02% | 0.00% | -0.01% | 97% | 99%
Mixed content | 0.01% | -0.01% | -0.03% | 101% | 102%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 97% | 98%
Overall | -0.04% | -0.02% | -0.02% | 98% | 100%
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.13% | -0.13% | -0.14% | 95% | 96%
TGM 720p | 0.00% | -0.13% | -0.21% | 92% | 90%
Animation | 0.13% | 0.05% | 0.07% | 97% | 98%
Mixed content | 0.07% | -0.05% | -0.06% | 97% | 98%
Camera-Captured content | -0.01% | 0.04% | -0.01% | 96% | 99%
Overall | 0.00% | -0.06% | -0.09% | 95% | 96%
Dual Tree On
Dual Tree Off
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.24% | -0.25% | -0.18% | 100% | 100%
TGM 720p | -0.04% | -0.10% | -0.05% | 93% | 92%
Animation | -0.03% | -0.10% | -0.10% | 94% | 97%
Mixed content | -0.08% | -0.01% | -0.30% | 95% | 97%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 99% | 99%
Overall | -0.09% | -0.11% | -0.13% | 96% | 97%
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
TGM 720p | 0.11% | -0.07% | 0.35% | 101% | 102%
Animation | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Mixed content | -0.23% | -0.21% | -0.30% | 96% | 93%
Camera-Captured content | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
TGM 720p | 0.32% | -0.02% | 0.78% | 98% | 101%
Animation | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Mixed content | 0.07% | 0.28% | -0.01% | 98% | 96%
Camera-Captured content | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Test 2 (Normal QP)

## Slide 5
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.33% | -0.46% | -0.52% | 98% | 95%
TGM 720p | 0.04% | -0.08% | -0.22% | 99% | 98%
Animation | -0.04% | -0.04% | -0.07% | 97% | 90%
Mixed content | -0.24% | -0.55% | -0.56% | 95% | 93%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 98% | 97%
Overall | -0.12% | -0.25% | -0.30% | 97% | 95%
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.10% | -0.03% | -0.06% | 100% | 103%
TGM 720p | -0.13% | -0.09% | -0.04% | 95% | 98%
Animation | -0.03% | -0.06% | -0.01% | 101% | 101%
Mixed content | 0.02% | 0.02% | 0.01% | 101% | 99%
Camera-Captured content | -0.01% | 0.04% | 0.00% | 104% | 105%
Overall | -0.06% | -0.03% | -0.02% | 100% | 101%
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.20% | -0.20% | -0.17% | 100% | 100%
TGM 720p | 0.01% | -0.16% | -0.26% | 101% | 99%
Animation | 0.16% | 0.11% | 0.10% | 100% | 100%
Mixed content | 0.03% | 0.01% | 0.05% | 99% | 98%
Camera-Captured content | -0.02% | 0.02% | -0.02% | 98% | 99%
Overall | -0.01% | -0.06% | -0.08% | 100% | 99%
Dual Tree On
Dual Tree Off
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.33% | -0.31% | -0.29% | 101% | 99%
TGM 720p | -0.08% | -0.04% | 0.08% | 99% | 98%
Animation | 0.01% | -0.04% | -0.09% | 98% | 98%
Mixed content | -0.13% | -0.08% | -0.22% | 97% | 98%
Camera-Captured content | 0.00% | -0.01% | 0.00% | 105% | 101%
Overall | -0.12% | -0.11% | -0.11% | 100% | 98%
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.12% | -0.22% | -0.26% | 96% | 96%
TGM 720p | 0.31% | 0.09% | 0.38% | 99% | 96%
Animation | -0.02% | 0.03% | 0.03% | 94% | 92%
Mixed content | -0.11% | -0.36% | -0.22% | 90% | 94%
Camera-Captured content | 0.02% | 0.00% | -0.12% | 101% | 95%
Overall | 0.02% | -0.09% | -0.02% | 96% | 95%
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -0.01% | -0.11% | -0.15% | 102% | 97%
TGM 720p | 0.00% | -0.52% | 0.20% | 95% | 96%
Animation | -0.05% | 0.08% | -0.02% | 94% | 94%
Mixed content | 0.24% | 0.08% | -0.03% | 94% | 92%
Camera-Captured content | 0.00% | -0.01% | 0.01% | 101% | 101%
Overall | 0.03% | -0.13% | 0.00% | 97% | 96%
Test 3 (Normal QP)

## Slide 6
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -2.66% | -3.19% | -3.26% | 96% | 97%
TGM 720p | -0.80% | -1.10% | -1.09% | 97% | 97%
Animation | -0.39% | -0.62% | -0.66% | 97% | 97%
Mixed content | -1.12% | -1.28% | -1.32% | 100% | 97%
Camera-Captured content | 0.00% | 0.00% | -0.01% | 96% | 103%
Overall | -1.15% | -1.43% | -1.46% | 97% | 98%
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.68% | -2.25% | -2.23% | 97% | 98%
TGM 720p | -0.51% | -0.75% | -0.70% | 103% | 101%
Animation | -0.26% | -0.20% | -0.27% | 97% | 96%
Mixed content | -1.36% | -1.58% | -1.63% | 98% | 99%
Camera-Captured content | 0.00% | -0.01% | 0.00% | 103% | 97%
Overall | -0.85% | -1.08% | -1.09% | 99% | 98%
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.40% | -1.77% | -1.76% | 96% | 98%
TGM 720p | -0.60% | -0.48% | -0.62% | 97% | 95%
Animation | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Mixed content | -1.24% | -0.25% | -0.30% | 95% | 95%
Camera-Captured content |  |  |  |  | 
Overall |  |  |  |  | 
Dual Tree On
Dual Tree Off
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -2.57% | -2.37% | -2.42% | 94% | 92%
TGM 720p | -0.89% | -0.81% | -0.97% | 96% | 91%
Animation | -0.37% | -0.27% | -0.33% | 100% | 97%
Mixed content | -1.00% | -0.84% | -0.94% | 95% | 93%
Camera-Captured content |  |  |  |  | 
Overall |  |  |  |  | 
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.16% | -1.25% | -1.27% | 98% | 99%
TGM 720p | -0.10% | -0.42% | -0.35% | 94% | 93%
Animation | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Mixed content | -0.37% | -0.11% | -0.14% | 100% | 102%
Camera-Captured content | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.49% | -1.61% | -1.58% | 97% | 98%
TGM 720p | -0.11% | -0.29% | -0.29% | 95% | 95%
Animation | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Mixed content | -0.20% | -0.43% | -0.54% | 99% | 98%
Camera-Captured content | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Test 2 (Low QP)

## Slide 7
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -3.33% | -4.60% | -4.66% | 101% | 100%
TGM 720p | -0.99% | -1.54% | -1.56% | 98% | 96%
Animation | -0.53% | -0.63% | -0.58% | 96% | 97%
Mixed content | -1.47% | -2.00% | -2.13% | 101% | 100%
Camera-Captured content | 0.00% | 0.00% | 0.00% | 99% | 98%
Overall | -1.46% | -2.03% | -2.06% | 99% | 98%
 |  |  | All Intra |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -2.04% | -3.55% | -3.55% | 96% | 98%
TGM 720p | -0.64% | -1.14% | -1.17% | 94% | 95%
Animation | -0.30% | -0.33% | -0.46% | 96% | 98%
Mixed content | -1.72% | -2.85% | -2.88% | 96% | 97%
Camera-Captured content | 0.01% | -0.02% | -0.01% | 96% | 95%
Overall | -1.05% | -1.77% | -1.81% | 95% | 97%
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.57% | -2.24% | -2.21% | 94% | 95%
TGM 720p | -0.61% | -0.88% | -1.07% | 96% | 93%
Animation | -0.22% | -0.48% | -0.48% | 100% | 97%
Mixed content | -1.40% | -0.47% | -0.53% | 97% | 95%
Camera-Captured content | 0.00% | 0.01% | -0.03% | 97% | 98%
Overall | -0.85% | -0.96% | -1.01% | 97% | 95%
Dual Tree On
Dual Tree Off
 |  |  | Random access |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -2.78% | -2.87% | -2.89% | 96% | 98%
TGM 720p | -0.86% | -1.10% | -1.25% | 101% | 97%
Animation | -0.42% | -0.37% | -0.45% | 97% | 97%
Mixed content | -1.08% | -1.10% | -1.30% | 95% | 94%
Camera-Captured content | 0.01% | -0.01% | 0.01% | 97% | 99%
Overall | -1.19% | -1.27% | -1.36% | 97% | 97%
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.23% | -1.65% | -1.65% | 99% | 99%
TGM 720p | -0.05% | -0.62% | -0.51% | 93% | 91%
Animation | -0.75% | -0.49% | -0.51% | 97% | 97%
Mixed content | -0.46% | -0.93% | -0.89% | 99% | 102%
Camera-Captured content | 0.01% | 0.00% | 0.02% | 96% | 96%
Overall | -0.55% | -0.84% | -0.80% | 97% | 97%
 |  |  | Low delay B |  | 
 | Over VTM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
TGM 1080p | -1.69% | -2.17% | -2.10% | 96% | 100%
TGM 720p | -0.29% | -0.62% | -0.81% | 96% | 97%
Animation | -0.44% | -0.63% | -0.67% | 98% | 98%
Mixed content | -0.64% | -1.61% | -1.78% | 99% | 100%
Camera-Captured content | 0.01% | 0.01% | 0.01% | 100% | 100%
Overall | -0.70% | -1.12% | -1.18% | 97% | 99%
Test 3 (Low QP)

## Slide 8: Summary
The proposed method report improvement compared to anchor
It is recommended to consider adoption the proposed method
Thanks Alibaba for cross-checking

## Slide 9: Thank you