## Slide 1
JVET-P0562
Non-CE8: Transform skip residual coding simplification
Yi-Wen Chen, Xiaoyu Xiu, Xianglin Wang and et al.

## Slide 2: Introduction
In TS residual coding, per-sample adaptive codewords (Golomb Rice) is used for the coding of the level remainder
  The rice parameter is derived from the neighbouring levels
Proposed methods to replace per-sample adaptive codewords
  Fixed codeword (rice parameter is fixed as K)
  Adaptive codeword (rice parameter is determined by the CU QP)

## Slide 3: Summary of Results
Anchor :VTM-6.0
 |  | Standard QPs (22, 27, 32, 37) |  |  | Low QPs (22, 27, 32, 37) |  | 
 |  | AI | RA | LDB | AI | RA | LDB
Fix Rice Parameter (K=1) | F | 0.00% | -0.07% | 0.09% | 0.02% | 0.01% | 0.04%
 | TGM | 0.02% | -0.02% | -0.06% | -0.37% | 0.08% | -0.19%
Fix Rice Parameter (K=2) | F | 0.09% | 0.07% | 0.13% | -0.65% | -0.64% | -0.47%
 | TGM | 0.25% | 0.11% | 0.03% | -2.15% | -1.81% | -1.35%
QP-dependent Rice Parameter* | F | 0.09% | 0.07% | 0.13% | -0.90% | -0.63% | -0.79%
 | TGM | 0.25% | 0.11% | 0.03% | -3.55% | -2.97% | -2.08%
QP value | Qp′Y <4 | Qp′Y <8 | Qp′Y <16 | Qp′Y <32 | Otherwise
cRiceParam (K) | 1 | 2 | 3 | 4 | 5
*QP-dependent rice parameter derivation table:

## Slide 4: Simulation Results
Anchor :VTM-6.0
Test: Anchor + Fix Rice Parameter (K=1)
(DualITree = 0)
(DualITree = 1)

## Slide 5: Simulation Results
Anchor :VTM-6.0
Test: Anchor + Fix Rice Parameter (K=2)
(DualITree = 0)
(DualITree = 1)

## Slide 6: Simulation Results
Anchor :VTM-6.0 (IBC=0)
Test: Anchor + proposed fix
(DualITree = 0)
(DualITree = 1)

## Slide 7: Summary
Propose to fix the un-aligned codewords design of PLT mode
  Fix the physical meaning of prediction mode flag (e.g. 0inter, 1intra)
  Simplify the signaling condition of PLT flag
  Negligible coding performance (minor coding gain)
Recommend to adopt the proposed method into VVC
Thanks for Alibaba being our cross-checker

## Slide 8: Thank you
Standard QPs (22, 27, 32, 37)

## Slide 9
Rice Parameter deriviation in VTM6.0

## Slide 12: Summary of Results
Anchor :VTM-6.0
 |  | Standard QPs (22, 27, 32, 37) |  |  | Low QPs (22, 27, 32, 37) |  | 
 |  | AI | RA | LDB | AI | RA | LDB
Fix Rice Parameter (K=1) | CTC | 0.00% | 0.00% | - | 0.00% | - | 0.00%
 | F | 0.00% | -0.07% | 0.09% | 0.02% | 0.01% | 0.04%
 | TGM | 0.02% | -0.02% | -0.06% | -0.37% | 0.08% | -0.19%
Fix Rice Parameter (K=2) | CTC | 0.00% | 0.00% | - | 0.00% | - | -
 | F | 0.09% | 0.07% | 0.13% | -0.65% | -0.64% | -0.47%
 | TGM | 0.25% | 0.11% | 0.03% | -2.15% | -1.81% | -1.35%
QP-dependent Rice Parameter | CTC | 0.00% | 0.00% | - | 0.00% | - | 0.00%
 | F | 0.09% | 0.07% | 0.13% | -0.90% | -0.63% | -0.79%
 | TGM | 0.25% | 0.11% | 0.03% | -3.55% | -2.97% | -2.08%