## Slide 1: Non-CE7: State-dependent Binarization for Transform Coefficient Levels
H. Schwarz, A.Henkel, D. Marpe, T. Wiegand
JVET-P0619

## Slide 2: Bin-To-Bit Ratio Increase for Dependent Quantization
with current bin limit: cabac_zero_words are present in some of the bitstreams (mostly at low QPs)
weighted bin-to-bit ratio (1 for ctx bins, 0.25 for EP bins)

## Slide 3: State-Dependent Binarization
Variant A
if( state > 1 ) use binarization B else use binarization A
Variant B
if( state > 1 && sumAbsTemplate > 0 ) use binarization B else use binarization A

## Slide 4: Context Modelling (for second binarization)
abs_level_eq1_flag
Same context derivation as for sig_coeff_flag
Total number of context for sig_coeff_flag and abs_level_eq1_flag is the same as in VTM-6
abs_level_gt1_flag (for binarization B)
Same context derivation as for sig_coeff_flag (without dependency on state)
20 additional contexts (12 for luma, 8 for chroma) for variant A
15 additional contexts (9 for luma, 6 for chroma) for variant B

## Slide 5: Summary of Results for CTC
cabac_zero_word’s
not present in any
of the bitstreams
weighted
bin-to-bit ratio
(1, 0.25)

## Slide 6: Summary of Results for low QPs (2, 7, 12, 17)
cabac_zero_word’s
not present in any
of the bitstreams
weighted
bin-to-bit ratio
(1, 0.25)