## Slide 1: Non-CE5: Combination of JVET-P0470 and JVET-P0557 on simplification of CC-ALF (JVET-P0666)
X. Li, X. Zhao, L. Zhao, Y. Du, S. Liu (Tencent)
N. Hu, J. Dong, V. Seregin, M. Karczewicz (Qualcomm)
2019/10

## Slide 2: Introduction
In CE5-2.1, cross-component ALF is proposed
  where denotes chroma offset, indicates luma reconstruction sample, and represents filter coefficient
  10-bit, 8-bit, 18 10-bit by 8-bit multipliers

## Slide 3: Proposed Simplifications
Constrain CC-ALF coefficients to be 0, ±1, ±2, ±4 and ±8
  Multiplications can be replaced by shifts
  4-bit increase of dynamic range, keeping 16-bit dynamic range for up to 12-bit internal bit-depth

## Slide 4: Proposed Syntax Changes
CCALF coefficient signaling
alf_data( ) { | Descriptor
… | 
if ( alf_cross_component_cb_filter_signal_flag ) | 
for ( j = 0; j < 14; j++ ) { | 
alf_cross_component_cb_coeff_nonzeroabs[ j ] | u(1)
if( alf_cross_component_cb_coeff_nonzeroabs[ j ] ){ | 
alf_cross_component_cb_coeff_shift[ j ] | u(2)
alf_cross_component_cb_coeff_sign[ j ] | u(1)
} | 
} | 
if ( alf_cross_component_cr_ filter_signal_flag ) | 
for ( j = 0; j < 14; j++ ) { | 
alf_cross_component_cr_coeff_nonzeroabs[ j ] | u(1)
if( alf_cross_component_cr_coeff_nonzeroabs[ j ] ) { | 
alf_cross_component_cr_coeff_shift[ j ] | u(2)
alf_cross_component_cr_coeff_sign[ j ] | u(1)
} | 
} | 

## Slide 5: Simulation Results
Without gain shifting
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-6 |  |  |  |  | Over CE5-2.1-noshift |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.13% | -3.31% | -3.94% | 104% | 103% | 0.00% | 0.19% | 0.23% | 100% | 100%
Class A2 | 0.09% | -7.44% | -8.19% | 102% | 103% | -0.04% | 1.35% | 0.87% | 100% | 100%
Class B | 0.09% | -10.36% | -8.46% | 102% | 105% | -0.01% | 0.24% | 0.13% | 101% | 101%
Class C | 0.10% | -4.17% | -3.94% | 102% | 103% | -0.02% | 0.01% | -0.03% | 100% | 105%
Class E | 0.16% | -10.04% | -3.48% | 102% | 107% | -0.02% | 0.15% | -0.02% | 101% | 105%
Overall | 0.11% | -7.27% | -5.83% | 102% | 104% | -0.02% | 0.35% | 0.21% | 100% | 102%
Class D | 0.11% | -3.08% | -3.59% | 102% | 104% | 0.00% | -0.35% | -0.31% | 101% | 102%
Class F | 0.17% | -6.37% | -6.53% | 101% | 106% | -0.01% | 0.40% | 0.17% | 100% | 104%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-6 |  |  |  |  | Over CE5-2.1-noshift |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.13% | -5.04% | -5.10% | 103% | 102% | 0.00% | 0.67% | 0.25% | 101% | 100%
Class A2 | 0.21% | -10.54% | -14.68% | 103% | 103% | 0.00% | 1.33% | 1.27% | 101% | 100%
Class B | 0.22% | -17.62% | -14.10% | 102% | 105% | 0.01% | 0.03% | -0.09% | 101% | 102%
Class C | 0.11% | -5.21% | -4.53% | 101% | 103% | 0.02% | -0.18% | -0.18% | 101% | 105%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | 0.17% | -10.38% | -9.86% | 102% | 103% | 0.01% | 0.36% | 0.23% | 101% | 102%
Class D | 0.11% | -5.09% | -4.84% | 102% | 106% | 0.00% | -0.70% | -0.43% | 101% | 103%
Class F | 0.20% | -4.63% | -4.59% | 102% | 104% | 0.01% | 0.16% | 0.05% | 101% | 102%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-6 |  |  |  |  | Over CE5-2.1-noshift |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.19% | -21.01% | -18.97% | 102% | 102% | 0.01% | 0.73% | 0.29% | 100% | 98%
Class C | 0.17% | -8.24% | -6.66% | 102% | 108% | 0.05% | -0.08% | -0.25% | 101% | 101%
Class E | 0.03% | -16.52% | -6.70% | 104% | 107% | -0.21% | -0.95% | -0.36% | 100% | 101%
Overall | 0.14% | -15.63% | -11.80% | 102% | 105% | -0.03% | 0.04% | -0.05% | 100% | 100%
Class D | 0.23% | -8.76% | -6.51% | 101% | 107% | 0.05% | -0.74% | -0.51% | 101% | 107%
Class F | 0.28% | -10.09% | -7.56% | 102% | 106% | 0.15% | 0.47% | -0.04% | 100% | 102%

## Slide 6: Clipping for offsets and No Block on/off and temporal prediction
Without gain shifting – minor improvement
 | All Intra Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-6 |  |  |  |  | Over CE5-2.1-noshift |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.11% | -3.26% | -3.77% | 101% | 102% | -0.02% | 0.24% | 0.41% | 97% | 98%
Class A2 | 0.05% | -7.32% | -7.84% | 100% | 102% | -0.08% | 1.49% | 1.26% | 98% | 99%
Class B | 0.07% | -10.00% | -8.17% | 99% | 101% | -0.03% | 0.67% | 0.50% | 98% | 97%
Class C | 0.08% | -3.92% | -3.81% | 100% | 95% | -0.05% | 0.27% | 0.11% | 99% | 97%
Class E | 0.15% | -9.88% | -3.44% | 100% | 99% | -0.04% | 0.34% | 0.02% | 99% | 97%
Overall | 0.09% | -7.06% | -5.63% | 100% | 100% | -0.04% | 0.59% | 0.44% | 98% | 98%
Class D | 0.09% | -2.81% | -3.26% | 100% | 96% | -0.03% | -0.06% | 0.05% | 99% | 95%
Class F | 0.07% | -5.14% | -5.82% | 99% | 99% | -0.11% | 2.30% | 1.06% | 99% | 96%
 | Random Access Main 10 |  |  |  |  |  |  |  |  | 
 | Over VTM-6 |  |  |  |  | Over CE5-2.1-noshift |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.14% | -4.92% | -4.96% | 100% | 101% | 0.01% | 0.80% | 0.40% | 97% | 99%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.22% | -17.23% | -13.84% | 99% | 100% | 0.01% | 0.54% | 0.34% | 98% | 97%
Class C | 0.11% | -4.86% | -4.21% | 99% | 95% | 0.02% | 0.19% | 0.15% | 98% | 97%
Class E |  |  |  |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.07% | -4.85% | -4.55% | 100% | 100% | -0.04% | -0.45% | -0.09% | 99% | 97%
Class F | 0.14% | -4.25% | -4.33% | 100% | 98% | -0.05% | 0.92% | 0.46% | 98% | 97%
 | Low delay B Main10 |  |  |  |  |  |  |  |  | 
 | Over VTM-6 |  |  |  |  | Over CE5-2.1-noshift |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | 0.12% | -7.27% | -5.68% | 100% | 105% | 0.00% | 1.02% | 0.83% | 99% | 98%
Class E | 0.09% | -16.05% | -5.90% | 101% | 103% | -0.14% | -0.45% | 0.50% | 98% | 97%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.12% | -6.79% | -5.06% | 100% | 98% | -0.06% | 1.46% | 1.09% | 100% | 98%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!

## Slide 7: Conclusions
Simplification of CE5-2.1 is proposed
  Filter coefficients are constrained to 0, ±1, ±2, ±4 and ±8
  Less complexity for both hardware and software