## Slide 1
AHG13: Analysis of the Energy Demand and Time Complexity of Several Coding Tools in VTM-7.0

## Slide 2: Motivation
Online video content: 1% of global greenhouse gas emissions [1]
  Civil aviation has a share of 4%
Mobile devices with limited battery lifetime
[1] M. Efoui-Hess, “Climate Crisis: The Unsustainable Use of Online Video. The Practical Case for Digital Sobriety”, Jul. 2019.

## Slide 3: Outline
Energy Measurement & Test Set
Tool Analysis
Comparison of VTM and HM
Conclusion

## Slide 4: Energy Measurement & Test Set
Measurement of the decoding energy:
  Desktop PC
    Intel i7-8700 CPU
    OS: CentOS 7
  Measurement with integrated power meter of Intel CPU: Running Average Power Limit (RAPL)
Test Set:
  Based on JVET common test conditions for SDR sequences (JVET-N1010)
  Tool-Tests according to JVET-Q0013
  VVC:
    Encoding and decoding with VTM-7.0
    Configuration: intra, lowdelay, randomaccess

## Slide 5: Tool Analysis
Evaluated tools:

## Slide 6: Tool Analysis
Evaluation metrics:
  Bjøntegaard-Delta-Rate (BDR)
  Bjøntegaard-Delta-Decoding-Energy (BDDE) [2]
    Positive value  Higher energy demand if tool is switched off  Usage of tool improves energy-efficiency
  Bjøntegaard-Delta-Decoding-Time (BDDT)
[2] C. Herglotz et al. Decoding-Energy-Rate-Distortion Optimization for Video Coding. IEEE Trans. on Circuits and Systems for Video Technology, Vol. 29(1), 2019.

## Slide 7: Tool Analysis
Analysis of ALF, AMVR, and BDOF:
  ALF increases RD-efficiency at the cost of energy demand
  AMVR increases the RD-efficiency as well as the energy-efficiency

## Slide 8: Evaluation of tool analysis
Evaluation:
 | All Intra Over VTM-7.0 |  | 
 | YUV-BDR [%] | BDDT [%] | BDDE [%]
MIP | 0.51 | 1.16 | 0.80
ISP | 0.54 | -1.34 | -1.82
 | Randomaccess Over VTM-7.0 |  | 
 | YUV-BDR [%] | BDDT [%] | BDDE [%]
AMVR | 1.29 | 2.84 | 2.28
TPM | 0.39 | 2.32 | 2.02
LFNST | 0.73 | 2.09 | 1.63
MTS | 0.61 | 1.69 | 1.38
BDOF | 0.80 | -0.81 | -1.30
DMVR | 0.73 | -0.59 | -1.44
ALF | 4.36 | -7.08 | -6.99

## Slide 9: Summary
Tool analysis showed that all tested tools increase RD-efficiency
Some tools increase energy-efficiency

## Slide 10
Thank you very much!