## Slide 1
On QP Adjustment for Adaptive Color Transform (JVET-Q0098)
T. Tsukuba, K. Kondo, Y. Yagasaki, M. Ikeda, T. Suzuki

## Slide 2: Summary of JVET-Q0098
Introduction
  An issue for QP derivation when adaptive color transform (ACT) is enabled.
  Related contribution: JVET-Q0241, JVET-Q0511
Proposal method
  Clip QP to limit in valid range.
Experiment
Conclusion

## Slide 3: Introduction
In VTM-7.1, the QP adjustment of (-5, -5, -3) for ACT are applied to compensate the dynamic range change of residual signals before and after color transform
  In case of non-TS qP = qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 )
  In case of TS qP = Max( QpPrimeTsMin, qP ) − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 )
However, the new derived qP may violate qP valid range
  qP for non-TS can be less than 0
  qP for TS can be less than QpPrimeMinTS
And, current VTM software doesn’t work when InternalBitDepth is set to 8.

## Slide 4: Proposal
To satisfy the qP range, apply clipping as below:
  In case of non-TS qP = Max( 0, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 ) )
  In case of TS qP = Max( QpPrimeTsMin, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 ) )

## Slide 5: Highlight of Spec changes in 8.7.3 Scaling process for transform coefficients
…
The quantization parameter qP is modified and the variables rectNonTsFlag and bdShift are derived as follows:
If transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0, the following applies:
qP = qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? 5 : 0 ) (1133)
qP = Max(0, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5:3) : 0 ) ) (1133)
rectNonTsFlag = ( ( ( Log2( nTbW ) + Log2( nTbH ) ) & 1 ) = = 1 ) ? 1 : 0 (1134)
bdShift = BitDepth + rectNonTsFlag + (1135) ( ( Log2( nTbW ) + Log2( nTbH ) ) / 2 ) − 5 + pic_dep_quant_enabled_flag
Otherwise (transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1), the following applies:
qP = Max( QpPrimeTsMin, qP ) − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? 5 : 0 ) (1136)
qP = Max( QpPrimeTsMin, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5:3) : 0 ) ) (1336)
rectNonTsFlag = 0 (1137)
bdShift = 10 (1138)
The variable bdOffset is derived as follows:
bdOffset = ( 1 << bdShift ) >> 1 (1139)

## Slide 6: Simulation Results
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.22% | -0.40% | -0.35%
RGB, mixed content, 1440p & 1080p | -0.21% | -0.39% | -0.45%
RGB, Animation, 720p | 0.00% | -0.35% | -0.24%
RGB, camera captured, 1080p | 0.00% | -0.21% | -0.20%
YUV, text & graphics with motion, 1080p & 720p | -0.03% | -0.01% | -0.03%
YUV, mixed content, 1440p & 1080p | -0.03% | 0.02% | 0.02%
YUV, Animation, 720p | -0.02% | 0.02% | -0.02%
YUV, camera captured, 1080p | 0.01% | 0.00% | 0.01%
Enc Time[%] | 101% |  | 
Dec Time[%] | 102% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.13% | -0.19% | -0.09%
RGB, mixed content, 1440p & 1080p | -0.20% | -0.23% | -0.31%
RGB, Animation, 720p | 0.01% | -0.40% | -0.34%
RGB, camera captured, 1080p | -0.01% | -0.18% | -0.32%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.00% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.00% | 0.00% | 0.00%
YUV, Animation, 720p | 0.01% | -0.02% | -0.04%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.00%
Enc Time[%] | 101% |  | 
Dec Time[%] | 101% |  | 
DualITree: OFF
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.35% | -0.36% | -0.34%
RGB, mixed content, 1440p & 1080p | -0.32% | -0.53% | -0.46%
RGB, Animation, 720p | 0.00% | -0.38% | -0.30%
RGB, camera captured, 1080p | 0.00% | -0.23% | -0.25%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.00% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.00% | 0.00% | 0.00%
YUV, Animation, 720p | 0.00% | 0.00% | 0.00%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.00%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
Proposal was implemented on top of VTM-7.1
Simulation for DualITreeOn/DualITreeOff were conducted for RGB444/YUV444 SCC sequences

## Slide 7: Simulation Results
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.20% | -0.40% | -0.34%
RGB, mixed content, 1440p & 1080p | -0.17% | -0.31% | -0.34%
RGB, Animation, 720p | 0.05% | -0.27% | -0.17%
RGB, camera captured, 1080p | -0.05% | -0.18% | -0.22%
YUV, text & graphics with motion, 1080p & 720p | -0.20% | -0.40% | -0.34%
YUV, mixed content, 1440p & 1080p | -0.03% | -0.06% | 0.01%
YUV, Animation, 720p | 0.05% | -0.27% | -0.17%
YUV, camera captured, 1080p | -0.01% | 0.00% | -0.01%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.12% | -0.15% | -0.20%
RGB, mixed content, 1440p & 1080p | -0.09% | -0.25% | -0.29%
RGB, Animation, 720p | -0.06% | -0.40% | -0.34%
RGB, camera captured, 1080p | 0.00% | -0.20% | -0.30%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.00% | -0.01%
YUV, mixed content, 1440p & 1080p | 0.01% | 0.01% | 0.01%
YUV, Animation, 720p | -0.01% | 0.00% | 0.01%
YUV, camera captured, 1080p | 0.00% | -0.20% | -0.30%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p |  |  | 
RGB, mixed content, 1440p & 1080p |  |  | 
RGB, Animation, 720p |  |  | 
RGB, camera captured, 1080p |  |  | 
YUV, text & graphics with motion, 1080p & 720p |  |  | 
YUV, mixed content, 1440p & 1080p |  |  | 
YUV, Animation, 720p |  |  | 
YUV, camera captured, 1080p |  |  | 
Enc Time[%] |  |  | 
Dec Time[%] |  |  | 
Proposal was implemented on top of VTM-7.1
Simulation for DualITreeOn/DualITreeOff were conducted for RGB444/YUV444 SCC sequences
DualITree: ON

## Slide 8: Conclusion
Clip qP after QP adjustment for ACT(Adaptive Color Transform) to keep the qP in valid range:
  In case of qP for non-TS qP = Max( 0, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 ) )
  In case of qP for TS qP = Max( QpPrimeTsMin, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 ) )
It can improve coding efficiency at low QP for SCC444 sequences.
Recommend: Adopt JVET-Q0098 into the next VTM/VVC WD
Thanks Kwai for Crosscheck
 |  | AI |  |  | RA |  |  | LB |  | 
 |  | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
DualITreeOFF | RGB | -0.17% | -0.37% | -0.33% | -0.09% | -0.25% | -0.27% | -0.11% | -0.34% | -0.31%
 | YUV | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | -0.02% | 0.01% | -0.01%
DualITreeON | RGB | 0.00% | 0.00% | 0.00% | -0.06% | -0.25% | -0.29% | -0.09% | -0.29% | -0.27%
 | YUV | 0.00% | 0.00% | 0.00% | 0.00% | -0.05% | -0.07% | -0.05% | -0.19% | -0.13%

## Slide 10: Summary
Clip qP after QP adjustment for ACT(Adaptive Color Transform) to keep the qP in valid range:
  In case of qP for non-TS qP = Max( 0, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 ) )
  In case of qP for TS qP = Max( QpPrimeTsMin, qP − ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? (cIdx<2 ? 5 : 3): 0 ) )
Results show proposal can improve coding efficiency at low QP for SCC444 sequences.
Related contribution: JVET-Q0241, JVET-Q0511
Recommend: Adopt JVET-Q0098 into the next VTM/VVC WD
 |  | AI |  |  | RA |  |  | LB |  | 
 |  | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
DualITreeOFF | RGB | -0.17% | -0.37% | -0.33% | -0.09% | -0.25% | -0.27% | -0.11% | -0.34% | -0.31%
 | YUV | 0.00% | 0.00% | 0.00% | 0.00% | 0.00% | -0.01% | -0.02% | 0.01% | -0.01%
DualITreeON | RGB | 0.00% | 0.00% | 0.00% | -0.06% | -0.25% | -0.29% | -0.09% | -0.29% | -0.27%
 | YUV | 0.00% | 0.00% | 0.00% | 0.00% | -0.05% | -0.07% | -0.05% | -0.19% | -0.13%