## Slide 1
JVET-Q0105:
BCW and SIF derivation for pairwise candidate
A. Robert, T. Poirier, F. Le-Léannec

## Slide 2: BCW and SIF derivation in VTM-7.0 JVET-Q0105
In current VTM-7.0, the pairwise candidate
  Average motion vectors of two input candidates (Cand0, Cand1)
  BCW index is set to:
  BCWPW = default
  SIF flag is derived as:
  SIFPW = (SIFCand0 == SIFCand1) ? SIFCand0 : false
Proposal:
  Unify BCW and SIF derivation

## Slide 3: Unify as BCW index derivation JVET-Q0105
Derive both as actual BCW index
  BCWPW = default
  SIFPW = false
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.11% | 0.09% | 100% | 101%
Class A2 | -0.01% | 0.02% | 0.04% | 100% | 98%
Class B | 0.00% | 0.05% | 0.00% | 100% | 100%
Class C | 0.01% | 0.01% | 0.05% | 100% | 100%
Overall | 0.01% | 0.04% | 0.04% | 100% | 100%
Class D | -0.01% | 0.06% | 0.10% | 100% | 101%
Class F | -0.01% | 0.00% | -0.03% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | -0.01% | -0.08% | -0.07% | 100% | 101%
Class C | -0.02% | -0.16% | -0.02% | 100% | 99%
Class E | 0.02% | 0.12% | -0.28% | 99% | 100%
Overall | -0.01% | -0.06% | -0.10% | 100% | 100%
Class D | 0.03% | 0.14% | 0.18% | 100% | 100%
Class F | 0.05% | 0.00% | 0.02% | 100% | 100%

## Slide 4: Unify as SIF flag derivation JVET-Q0105
Derive both as actual SIF flag
  BCWPW = (BCWCand0 == BCWCand1) ? BCWCand0 : default
  SIFPW = ( SIFCand0 == SIFCand1) ? SIFCand0 : false
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.07% | 0.07% | 100% | 101%
Class A2 | -0.01% | 0.01% | -0.01% | 100% | 98%
Class B | 0.00% | 0.04% | 0.03% | 100% | 100%
Class C | 0.01% | 0.04% | 0.01% | 100% | 102%
Overall | 0.00% | 0.01% | 0.02% | 100% | 100%
Class D | -0.01% | 0.00% | 0.04% | 100% | 101%
Class F | 0.00% | -0.02% | -0.05% | 100% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class B | 0.01% | -0.07% | -0.07% | 101% | 100%
Class C | -0.04% | -0.24% | -0.20% | 100% | 99%
Class E | -0.05% | 0.34% | -0.27% | 99% | 99%
Overall | -0.02% | -0.03% | -0.16% | 100% | 100%
Class D | -0.08% | 0.61% | -0.10% | 100% | 98%
Class F | 0.05% | -0.18% | 0.17% | 100% | 99%

## Slide 5: Conclusion JVET-Q0105
Unification of BCW and SIF derivation for pairwise
  As actual BCW index
    0.01% in RA (with 0.03% in class A1)
    -0.01% in LDB
    With same complexity
  As actual SIF flag
    Keep performances in RA (all classes between -0.01% and 0.01%)
    -0.02% in LDB
    With same complexity
  BCWPW = (BCWCand0 == BCWCand1) ? BCWCand0 : default
  SIFPW = ( SIFCand0 == SIFCand1) ? SIFCand0 : false
  Thanks to Tencent for cross-checking

## Slide 6: Thank you