## Slide 1: JVET-Q0161 On constant shift and offset in MIP
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: Summary
Background
  Floating-point data of MIP was provided by HHI.
    The learning data is used in current MIP design.
  This proposal was considered using the floating-point data.
  Related proposal for this aspect.
    JVET-Q0446 “MIP with constant shifts and offsets”
      The techniques are basically same as this proposal. But, the difference is to be used relearn data.
    JVET-Q0450 “On fixed sW and fO in MIP”
      One of proposals, Test-3 is the same as test-sW5 of this proposal.
Introduce proposed simplifications
Experiment results
Conclusion

## Slide 3: Current MIP design (VTM-7.0)
Weight shift (sW) and offset factor (fO)
  Two tables are defined.
  Depend on mipSizeIdx and modeId of MIP
Need a multiplication for offset factor
p[ 0 ] = pTemp[ 0 ] − ( 1 << ( BitDepth − 1 ) ) p[ x ] = pTemp[ x ] − pTemp[ 0 ] for x = 1..inSize − 1 (256)
oW = ( 1 << ( sW − 1 ) ) − fO * () (257)
predMip[ x ][ y ] = ( ( ( ) + oW ) >> sW ) + pTemp[ 0 ] (258)

## Slide 4: Proposed method, test-sW5
Remove two tables for sW and fO in VVC spec text
  sW=5, fO=48 (represented by shift and adder)
Replace a multiplication with shift and add
Use 7-bit table for weights as same as current design
p[ 0 ] = ( 1 << ( BitDepth − 1 ) ) − pTemp[ 0 ] p[ x ] = pTemp[ x ] − pTemp[ 0 ] for x = 1..inSize − 1 (256)
sum = ()
oW = ( 1 << 4 ) − (sum << 5) − (sum << 4) (257)
predMip[ x ][ y ] = ( ( ( ) + oW ) >> 5 ) + pTemp[ 0 ] (258)

## Slide 5: Proposed method, test-sW6
Remove two tables for sW and fO in VVC spec text
  sW=6, fO=96 (represented by shift and adder)
Replace a multiplication with shift and add
Use 8-bit table for weights to reduce loss
  But, it increases complexity
p[ 0 ] = ( 1 << ( BitDepth − 1 ) ) − pTemp[ 0 ] p[ x ] = pTemp[ x ] − pTemp[ 0 ] for x = 1..inSize − 1 (256)
sum = ()
oW = ( 1 << 5 ) − (sum << 6) − (sum << 5) (257)
predMip[ x ][ y ] = ( ( ( ) + oW ) >> 6 ) + pTemp[ 0 ] (258)

## Slide 6: Experiment results
 |  |  | All Intra |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.07% | -0.10% | 0.14% | 98% | 100%
Class A2 | 0.03% | 0.00% | -0.05% | 99% | 100%
Class B | 0.03% | 0.01% | -0.07% | 100% | 100%
Class C | 0.02% | 0.03% | -0.03% | 100% | 99%
Class E | 0.05% | -0.01% | 0.00% | 100% | 99%
Overall | 0.04% | -0.01% | -0.01% | 99% | 100%
Class D | 0.02% | -0.07% | -0.06% | 100% | 99%
Class F | 0.01% | 0.02% | 0.04% | 99% | 100%
 |  |  | Random access |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | -0.08% | 0.03% | 100% | 101%
Class A2 | -0.03% | 0.05% | -0.02% | 100% | 100%
Class B | 0.02% | 0.09% | 0.25% | 100% | 100%
Class C | 0.04% | -0.11% | -0.11% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.02% | -0.01% | 0.06% | 100% | 100%
Class D | -0.02% | -0.23% | -0.06% | 101% | 100%
Class F | -0.01% | 0.09% | 0.09% | 101% | 100%
 |  |  | All Intra |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.01% | -0.19% | 0.15% | 98% | 100%
Class A2 | 0.00% | 0.04% | -0.05% | 99% | 100%
Class B | 0.00% | 0.00% | -0.07% | 100% | 100%
Class C | 0.02% | 0.05% | 0.07% | 100% | 99%
Class E | 0.00% | 0.00% | 0.11% | 100% | 99%
Overall | 0.00% | -0.01% | 0.03% | 99% | 100%
Class D | 0.01% | 0.03% | 0.02% | 100% | 100%
Class F | 0.00% | 0.03% | 0.13% | 99% | 100%
 |  |  | Random access |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.08% | 0.00% | 100% | 100%
Class A2 | -0.02% | -0.04% | -0.05% | 99% | 100%
Class B | 0.01% | 0.02% | 0.08% | 100% | 100%
Class C | 0.01% | 0.05% | -0.04% | 101% | 100%
Class E |  |  |  |  | 
Overall | 0.00% | -0.01% | 0.00% | 100% | 100%
Class D | 0.01% | -0.18% | 0.17% | 101% | 100%
Class F | -0.02% | 0.09% | 0.05% | 101% | 100%
test-sW5 (7-bit table)
test-sW6 (8-bit table)

## Slide 7: Conclusions
Proposed simplifications of MIP
  Use constant sW and fO
  Remove two tables for those.
  Change parameters for weight
Experiments
  Test-sW5 (with 7-bit table)
    0.04% and 0.02% for AI and RA case
  Test-sW6 (with 8-bit table)
    0.00% and 0.00% for AI and RA case
Recommendation
  This simplification is adopted in next VTM.
Thanks HHI for cross-check!