## Slide 1: JVET-Q0162 A memory issue on adaptive color transform
K. Kondo, M. Ikeda, T. Suzuki (Sony)
Notes: 1

## Slide 2: Summary
Introduce an issue about memory
Propose the solution
Experiment results
Conclusion

## Slide 3: A memory issue for ACT
Need buffering before inverse ACT
  ACT needs three components for each sample level.
  But, the inverse transform processes for the transform size.
  Buffering is required before the inverse ACT.
    VVC can use 64-points inverse transform.
    Thus, the memory size becomes 197 Kbits (16-bit x 3 components x 64 x 64).
Entropy decoding
IQ + IT
Inverse ACT
Memory
A pipeline process when ACT is used.
+
Prediction
Bitstream
Y/Cg/Co
G/B/R
Reconstruction

## Slide 4: A solution for memory issue
Restrict the larger inverse transform
  When ACT is used, the transform size is limited.
  Proposes to prohibit 64-points transform when ACT is used.
    HEVC can use 32-points, thus it aligns to HEVC.
  When sps_max_luma_transform_size_64_flag is equal to 0, sps_act_enabled_flag is inferred equal to 0.
seq_parameter_set_rbsp( ) { | Descriptor
sps_max_luma_transform_size_64_flag | u(1)
… | 
if( chroma_format_idc = = 3 ) { | 
if(!sps_max_luma_transform_size_64_flag) | 
sps_act_enabled_flag | u(1)
} | 
} | 

## Slide 5: Test results for Separate Tree OFF case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree0, ACT1
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.1% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.1% | 0.3% | 0.2%
RGB, Animation, 720p | 0.2% | 0.1% | 0.1%
RGB, camera captured, 1080p | 1.1% | 0.0% | 0.7%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.1% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.8% | -0.1% | 0.7%
Enc Time[%] | 99% |  | 
Dec Time[%] | 101% |  | 

## Slide 6: Test results for Separate Tree OFF case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree0, ACT1
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | 0.0% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.3% | 0.4% | 0.3%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 1.3% | 0.1% | 1.0%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.4% | 0.5% | 0.5%
YUV, Animation, 720p | 0.2% | 0.1% | -0.1%
YUV, camera captured, 1080p | 0.8% | -0.1% | 0.6%
Enc Time[%] | 104% |  | 
Dec Time[%] | 99% |  | 

## Slide 7: Test results for Separate Tree OFF case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree0, ACT1
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | -0.2%
RGB, mixed content, 1440p & 1080p | 0.8% | 0.6% | 0.6%
RGB, Animation, 720p | -0.3% | 0.1% | 0.2%
RGB, camera captured, 1080p | 1.7% | 0.0% | 0.6%
YUV, text & graphics with motion, 1080p & 720p | 0.4% | 0.4% | 0.5%
YUV, mixed content, 1440p & 1080p | 1.0% | 0.9% | 1.1%
YUV, Animation, 720p | 0.5% | 0.2% | 0.3%
YUV, camera captured, 1080p | 0.8% | 0.4% | 0.7%
Enc Time[%] | 106% |  | 
Dec Time[%] | 100% |  | 

## Slide 8: Test results for Separate-Tree ON case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree1, ACT1
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | 0.1% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.4% | 0.4% | 0.3%
RGB, Animation, 720p | -0.1% | 0.1% | 0.0%
RGB, camera captured, 1080p | 1.8% | 0.0% | 1.4%
YUV, text & graphics with motion, 1080p & 720p | 0.2% | 0.3% | 0.4%
YUV, mixed content, 1440p & 1080p | 0.4% | 0.7% | 0.5%
YUV, Animation, 720p | 0.3% | 0.3% | 0.4%
YUV, camera captured, 1080p | 0.3% | 0.0% | 0.3%
Enc Time[%] | 105% |  | 
Dec Time[%] | 99% |  | 

## Slide 9: Test results for Separate-Tree ON case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree1, ACT1
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.1% | -0.2%
RGB, mixed content, 1440p & 1080p | 0.7% | 0.5% | 0.2%
RGB, Animation, 720p | -0.1% | 0.1% | 0.3%
RGB, camera captured, 1080p | 1.6% | 0.0% | 0.6%
YUV, text & graphics with motion, 1080p & 720p | 0.3% | 0.5% | 0.3%
YUV, mixed content, 1440p & 1080p | 0.9% | 0.9% | 1.1%
YUV, Animation, 720p | 0.3% | 0.2% | 0.2%
YUV, camera captured, 1080p | 0.7% | 0.4% | 0.8%
Enc Time[%] | 105% |  | 
Dec Time[%] | 100% |  | 

## Slide 10: Test results for Separate Tree OFF case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree0, ACT0
Anchor: ACT OFF, Test: ACT ON with proposal
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -5.7% | -1.5% | -2.7%
RGB, mixed content, 1440p & 1080p | -12.3% | -4.9% | -5.0%
RGB, Animation, 720p | -11.5% | -4.3% | -2.2%
RGB, camera captured, 1080p | -15.1% | -1.9% | -3.1%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.1% | 0.1% | 0.1%
YUV, Animation, 720p | 0.1% | 0.1% | 0.1%
YUV, camera captured, 1080p | 0.9% | -0.1% | 0.7%
Enc Time[%] | 101% |  | 
Dec Time[%] | 100% |  | 

## Slide 11: Test results for Separate Tree OFF case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree0, ACT0
Anchor: ACT OFF, Test: ACT ON with proposal
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -8.8% | -3.3% | -4.8%
RGB, mixed content, 1440p & 1080p | -19.1% | -9.6% | -9.5%
RGB, Animation, 720p | -18.2% | -8.6% | -6.4%
RGB, camera captured, 1080p | -28.6% | -8.3% | -12.9%
YUV, text & graphics with motion, 1080p & 720p | 0.2% | 0.1% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.5% | 0.5% | 0.4%
YUV, Animation, 720p | 0.3% | 0.1% | 0.1%
YUV, camera captured, 1080p | 0.9% | 0.0% | 0.7%
Enc Time[%] | 108% |  | 
Dec Time[%] | 99% |  | 

## Slide 12: Test results for Separate Tree OFF case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree0, ACT0
Anchor: ACT OFF, Test: ACT ON with proposal
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -11.5% | -5.1% | -6.3%
RGB, mixed content, 1440p & 1080p | -26.2% | -12.7% | -12.3%
RGB, Animation, 720p | -27.0% | -8.5% | -6.6%
RGB, camera captured, 1080p | -37.6% | -10.8% | -17.6%
YUV, text & graphics with motion, 1080p & 720p | 0.5% | 0.4% | 0.6%
YUV, mixed content, 1440p & 1080p | 1.3% | 1.1% | 1.7%
YUV, Animation, 720p | 0.6% | 0.6% | 0.4%
YUV, camera captured, 1080p | 0.9% | 0.3% | 0.8%
Enc Time[%] | 108% |  | 
Dec Time[%] | 99% |  | 

## Slide 13: Test results for Separate-Tree ON case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree1, ACT0
Anchor: ACT OFF, Test: ACT ON with proposal
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -4.8% | -1.9% | -2.5%
RGB, mixed content, 1440p & 1080p | -7.5% | -3.9% | -3.8%
RGB, Animation, 720p | -11.4% | -4.6% | -4.4%
RGB, camera captured, 1080p | -25.4% | -7.8% | -11.8%
YUV, text & graphics with motion, 1080p & 720p | 0.3% | 0.4% | 0.5%
YUV, mixed content, 1440p & 1080p | 0.5% | 0.7% | 0.6%
YUV, Animation, 720p | 0.3% | 0.4% | 0.4%
YUV, camera captured, 1080p | 0.4% | -0.1% | 0.4%
Enc Time[%] | 109% |  | 
Dec Time[%] | 99% |  | 

## Slide 14: Test results for Separate-Tree ON case
VTM-7.1, IBC1, PLT1, BDPCM2, HashMe1, DualTree1, ACT0
Anchor: ACT OFF, Test: ACT ON with proposal
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -10.3% | -4.8% | -5.8%
RGB, mixed content, 1440p & 1080p | -17.7% | -9.1% | -9.0%
RGB, Animation, 720p | -25.5% | -8.1% | -6.1%
RGB, camera captured, 1080p | -37.2% | -10.7% | -17.5%
YUV, text & graphics with motion, 1080p & 720p | 0.3% | 0.8% | 0.6%
YUV, mixed content, 1440p & 1080p | 1.2% | 1.0% | 1.1%
YUV, Animation, 720p | 0.6% | 0.6% | 0.4%
YUV, camera captured, 1080p | 0.8% | 0.4% | 0.9%
Enc Time[%] | 108% |  | 
Dec Time[%] | 99% |  | 

## Slide 15: Average BD rate for RGB test sequence
 |  | Anchor: ACT ON |  |  | Anchor: ACT OFF |  | 
 |  | G | B | R | G | B | R
Separate tree OFF | AI | 0.3% | 0.1% | 0.2% | -11.1% | -3.1% | -3.2%
 | RA | 0.4% | 0.1% | 0.3% | -18.7% | -7.5% | -8.4%
 | LB | 0.5% | 0.2% | 0.3% | -25.6% | -9.3% | -10.7%
Separate tree ON | RA | 0.5% | 0.1% | 0.5% | -12.3% | -4.6% | -5.6%
 | LB | 0.5% | 0.1% | 0.2% | -22.7% | -8.2% | -9.6%

## Slide 16: Conclusions
Introduced a memory issue when ACT is used
Proposed a solution
  Prohibit 64-points transform size as align to HEVC
  The memory size can be reduced to 49 Kbits from 197 Kbits
Recommendation
  This solution is adopted in next VTM.
Thanks WILUS for cross-check!
seq_parameter_set_rbsp( ) { | Descriptor
sps_max_luma_transform_size_64_flag | u(1)
… | 
if( chroma_format_idc = = 3 ) { | 
if(!sps_max_luma_transform_size_64_flag) | 
sps_act_enabled_flag | u(1)
} | 
} |