## Slide 1: JVET-0166: On the adaptive color transform
Han Huang, Adarsh Krishnan Ramasubramonian, Chun-Chi Chen, Vadim Seregin, Ted Hsieh, Yung-Hsuan Chao, Wei-Jung Chien, Geert Van der Auwera, Marta Karczewicz

## Slide 2: Summary of proposal
Add ACT QP offset before clipping of QP to avoid QP out of range
Align the chroma QP in the deblocking stage and dequantization stage as adopted in JVET-P1001
CU-level switching of QP offset values according to the ACT CU-level flag
Clip the input and output of inverse ACT to 16 bits dynamic range
Signal ACT QP offset in PPS and slide header
Use a separate chroma ACT QP offset for JointCbCr mode = 2

## Slide 3: Text change
if( sps_act_enabled_flag ) { | 
pps_slice_act_qp_offset_present_flag | u(1)
pps_act_y_qp_offset_plus5 | se(v)
pps_act_cb_qp_offset_plus5 | se(v)
pps_act_cr_qp_offset_plus3 | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
pps_act_cbcr_qp_offset_plus5 | se(v)
} | 
Item 5: Signaling of ACT offset at PPS and slice header
Item 6: Use a separate chroma ACT QP offset for JointCbCr mode 2
if(pps_slice_act_qp_offset_present_flag && !( slice_type == I && qtbtt_dual_tree_intra_flag) ) { | 
slice_act_y_qp_offset | se(v)
slice_act_cb_qp_offset | se(v)
slice_act_cr_qp_offset | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
slice_act_cbcr_qp_offset | se(v)
} | 
PPS ACT offset:
Slice header ACT offset:

## Slide 4: Text change
Item 1-3: QP clipping, CU level switching of QP offset, alignment for DB
If cu_act_enabled_flag[xCb][yCb] is equal to 1, variable QpY is derived as follows:
QpY = ( ( qPY_PRED + CuQpDeltaVal + pps_act_y_qp_offset+ slice_ act_y_qp_offset + 64 + 2 * QpBdOffset ) % ( 64 + QpBdOffset ) ) – QpBdOffset
Otherwise, the variable QpY is derived as follows:
QpY = ( ( qPY_PRED + CuQpDeltaVal + 64 + 2 * QpBdOffset ) % ( 64 + QpBdOffset ) ) − QpBdOffset (1116)
If cu_act_enabled_flag[xCb][yCb] is equal to 1, The chroma quantization parameters for the Cb and Cr components, Qp′Cb and Qp′Cr, and joint Cb-Cr coding Qp′CbCr are derived as follows:
Qp′Cb = Clip3( −QpBdOffset, 63, qPCb + pps_act_cb_qp_offset + slice_ act_cb_qp_offset + CuQpOffsetCb ) + QpBdOffset (1122)
Qp′Cr = Clip3( −QpBdOffset, 63, qPCr + pps_ act_cr_qp_offset + slice_ act_cr_qp_offset + CuQpOffsetCr ) + QpBdOffset (1123)
Qp′CbCr = Clip3( −QpBdOffset, 63, qPCbCr + pps_act_cbcr_qp_offset + slice_act_cbcr_qp_offset +CuQpOffsetCbCr ) + QpBdOffset
Otherwise, the chroma quantization parameters for the Cb and Cr components, Qp′Cb and Qp′Cr, and joint Cb-Cr coding Qp′CbCr are derived as follows:
Qp′Cb = Clip3( −QpBdOffset, 63, qPCb + pps_cb_qp_offset + slice_cb_qp_offset + CuQpOffsetCb ) + QpBdOffset (1122)
Qp′Cr = Clip3( −QpBdOffset, 63, qPCr + pps_cr_qp_offset + slice_cr_qp_offset + CuQpOffsetCr ) + QpBdOffset (1123)
Qp′CbCr = Clip3( −QpBdOffset, 63, qPCbCr + pps_joint_cbcr_qp_offset + slice_joint_cbcr_qp_offset +CuQpOffsetCbCr ) + QpBdOffset (1124)
Luma QP
Chroma QP

## Slide 5: Text change
Item 4: clipping of input and output of ACT
The (nTbW)x(nTbH) arrays of residual samples rY, rCb and rCr are modified as follows:
rY[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rY[ x ][ y ])
rCb[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCb[ x ][ y ])
rCr[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCr[ x ][ y ])
tmp = rY[ x ][ y ] − rCb[ x ][ y ] (1191)
rY[ x ][ y ] = rY[ x ][ y ] + rCb[ x ][ y ] (1192)
rCb[ x ][ y ] = tmp − rCr[ x ][ y ] (1193)
rCr[ x ][ y ] = tmp + rCr[ x ][ y ] (1194)
rY[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rY[ x ][ y ])
rCb[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCb[ x ][ y ])
rCr[ x ][ y ] = Clip3( CoeffMin, CoeffMax, rCr[ x ][ y ])

## Slide 6: Test results
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.3% | -0.2%
RGB, mixed content, 1440p & 1080p | 0.0% | -0.7% | -0.5%
RGB, Animation, 720p | 0.0% | -1.5% | -1.0%
RGB, camera captured, 1080p | -0.1% | -0.5% | -0.4%
Enc Time[%] | 97% |  | 
Dec Time[%] | 104% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.4% | -0.3%
RGB, mixed content, 1440p & 1080p | -0.1% | -1.0% | -0.6%
RGB, Animation, 720p | -0.1% | -1.3% | -0.7%
RGB, camera captured, 1080p | 0.1% | -0.3% | -0.2%
Enc Time[%] | 97% |  | 
Dec Time[%] | 101% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.3% | -0.4%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.9% | -0.7%
RGB, Animation, 720p | -0.1% | -0.6% | -0.5%
RGB, camera captured, 1080p | -0.1% | 0.0% | -0.4%
Enc Time[%] | 99% |  | 
Dec Time[%] | 102% |  | 
Applying item 1-5
 | All Intra |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 95% |  | 
Dec Time[%] | 101% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | -0.2% | -0.3%
YUV444, mixed content, 1440p & 1080p | 0.0% | -0.1% | -0.1%
YUV444, Animation, 720p | 0.1% | 0.1% | -0.1%
YUV444, camera captured, 1080p | 0.1% | 0.0% | 0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 

## Slide 7: Test results
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.3% | -0.2%
RGB, mixed content, 1440p & 1080p | 0.0% | -0.7% | -0.5%
RGB, Animation, 720p | 0.0% | -1.5% | -1.0%
RGB, camera captured, 1080p | -0.1% | -0.5% | -0.4%
Enc Time[%] | 104% |  | 
Dec Time[%] | 94% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | -0.4% | -0.3%
RGB, mixed content, 1440p & 1080p | -0.1% | -1.0% | -0.6%
RGB, Animation, 720p | -0.1% | -1.4% | -0.7%
RGB, camera captured, 1080p | 0.0% | -0.3% | -0.2%
Enc Time[%] | 97% |  | 
Dec Time[%] | 91% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | -0.3% | -0.4%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.9% | -0.7%
RGB, Animation, 720p | -0.1% | -0.7% | -0.5%
RGB, camera captured, 1080p | 0.0% | 0.0% | -0.3%
Enc Time[%] | 98% |  | 
Dec Time[%] | 93% |  | 
Applying item 1-6
 | All Intra |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 93% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV444, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1%
YUV444, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 97% |  | 
Dec Time[%] | 91% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
YUV444, text & graphics with motion, 1080p & 720p | 0.0% | -0.1% | -0.1%
YUV444, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.1%
YUV444, Animation, 720p | 0.1% | 0.0% | 0.0%
YUV444, camera captured, 1080p | 0.1% | 0.0% | 0.1%
Enc Time[%] | 98% |  | 
Dec Time[%] | 91% |  |