## Slide 1: JVET-Q0209: [AHG9][AHG15]: On Chroma Qp offsets
Hendry, J. Zhao, S. Kim
LG ELECTRONICS

## Slide 2: Introduction
In VVC7, Chroma QP offsets at picture and CU level are allowed.
List of CU level chroma Qp offset values are signaled in PPS, and index is signaled in transform unit and pallette coding.
This proposal is regarding
(1Make the condition for signaling the chroma index consistent in palette coding syntax table and transform unit syntax table,
(2) clean up of picture-level and CU-level chroma QP offset signaling in PPS by merging them into one list

## Slide 3: Background
CU Chroma QP offsets are referred in transform_unit and palette coding
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
… | 
if( ( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ ( chromaAvailable && ( tu_cbf_cb[ xC ][ yC ] ¦ ¦ tu_cbf_cr[ xC ][ yC ] ) ) ) && treeType != DUAL_TREE_LUMA ) { | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && chroma_qp_offset_list_len_minus1 > 0 ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
} | 
… | 
} | 
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) { | Descriptor
… | 
if( treeType != DUAL_TREE_LUMA && palette_escape_val_present_flag ) | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded ) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
… | 
} | 

## Slide 4: Proposal Aspect #1
In palette coding, no need to signal cu_chroma_qp_offset_idx if cu_chroma_qp_offset_flag is true and there is only 1 entry in chroma_qp_offset_list
This condition is consistent with the condition in transform_unit (The red text is addition)
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) { | Descriptor
… | 
if( treeType != DUAL_TREE_LUMA && palette_escape_val_present_flag ) | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded ) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && chroma_qp_offset_list_len_minus1 > 0) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
… | 
} | 

## Slide 5: Background
In PPS, a set of chroma QP offsets are signaled for picture level; then a loop to signal a list of CU level chroma QP offsets
pic_parameter_set_rbsp( ) { | Descriptor
… | 
pps_cb_qp_offset | se(v)
pps_cr_qp_offset | se(v)
pps_joint_cbcr_qp_offset_present_flag | u(1)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
pps_joint_cbcr_qp_offset_value | se(v)
pps_slice_chroma_qp_offsets_present_flag | u(1)
pps_cu_chroma_qp_offset_list_enabled_flag | u(1)
if( pps_cu_chroma_qp_offset_list_enabled_flag ) { | 
chroma_qp_offset_list_len_minus1 | ue(v)
for( i = 0; i <= chroma_qp_offset_list_len_minus1; i++ ) { | 
cb_qp_offset_list[ i ] | se(v)
cr_qp_offset_list[ i ] | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
joint_cbcr_qp_offset_list[ i ] | se(v)
} | 
} | 
… | 
} | 

## Slide 6: Proposal Aspect #2 : Introduction
This aspect is text cleanup by combining syntax elements
Picture-level chroma Qp offsets and CU-level chroma Qp offset list are signalled separately in the PPS. At the block level when they are used, they are always used together.
Thus, it makes more sense if these signalling be simplified by merging them.
The chroma quantization parameters for the Cb and Cr components, Qp′Cb and Qp′Cr, and joint Cb-Cr coding Qp′CbCr are derived as follows:
Qp′Cb = Clip3( −QpBdOffset, 63, qPCb + pps_cb_qp_offset + slice_cb_qp_offset + CuQpOffsetCb ) + QpBdOffset (1122)
Qp′Cr = Clip3( −QpBdOffset, 63, qPCr + pps_cr_qp_offset + slice_cr_qp_offset + CuQpOffsetCr ) + QpBdOffset (1123)
Qp′CbCr = Clip3( −QpBdOffset, 63, qPCbCr + pps_joint_cbcr_qp_offset + slice_joint_cbcr_qp_offset +CuQpOffsetCbCr ) + QpBdOffset (1124)

## Slide 7: Proposed modified syntax
pic_parameter_set_rbsp( ) { | Descriptor
... | 
pps_joint_cbcr_qp_offset_present_flag | u(1)
pps_chroma_qp_offset_list_len_minus1 | ue(v)
for( i = 0; i <= pps_chroma_qp_offset_list_len_minus1; i++ ) { | 
pps_cb_qp_offset_list[ i ] | se(v)
pps_cr_qp_offset_list[ i ] | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
pps_joint_cbcr_qp_offset_list[ i ] | se(v)
} | 
pps_slice_chroma_qp_offsets_present_flag | u(1)
... | 
} | 

## Slide 8: Comparison with existing
pic_parameter_set_rbsp( ) {
...
pps_cb_qp_offset
pps_cr_qp_offset
pps_joint_cbcr_qp_offset_present_flag
if( pps_joint_cbcr_qp_offset_present_flag )
pps_joint_cbcr_qp_offset_value
pps_slice_chroma_qp_offsets_present_flag
pps_cu_chroma_qp_offset_list_enabled_flag
if( pps_cu_chroma_qp_offset_list_enabled_flag ) {
chroma_qp_offset_list_len_minus1
for( i = 0; i <= chroma_qp_offset_list_len_minus1; i++ ) {
cb_qp_offset_list[ i ]
cr_qp_offset_list[ i ]
if( pps_joint_cbcr_qp_offset_present_flag )
joint_cbcr_qp_offset_list[ i ]
}
}
...
}
pic_parameter_set_rbsp( ) {
...
pps_joint_cbcr_qp_offset_present_flag
pps_chroma_qp_offset_list_len_minus1
for( i = 0; i <= pps_chroma_qp_offset_list_len_minus1; i++ ) {
pps_cb_qp_offset_list[ i ]
pps_cr_qp_offset_list[ i ]
if( pps_joint_cbcr_qp_offset_present_flag )
pps_joint_cbcr_qp_offset_list[ i ]
}
pps_slice_chroma_qp_offsets_present_flag
...
}
pps_cb_qp_offset_list[ 0 ] = pps_cb_qp_offset
pps_cb_qp_offset_list[ 1 ] = pps_cb_qp_offset + cb_qp_offset_list[ 0 ]
pps_cb_qp_offset_list[ 2 ] = pps_cb_qp_offset + cb_qp_offset_list[ 1 ]
...

## Slide 9: Aspect# 2: Proposed Changes
Propose to combine the signalling of picture level chroma QP offset (pps_cb_qp_offset, pps_cr_qp_offset, and pps_joint_cbcr_qp_offset) with the list of CU level chroma QP offsets (cb_qp_offset_list[ ], cr_qp_offset_list[ ], and joint_cbcr_qp_offset_list[ ])
Increase the chroma QP list size by 1, the first entry of the list is the picture level chroma QP offsets, the rest entries are the sum of CU level chroma QP offset with the picture level
No need to signal pps_cu_chroma_qp_offset_list_enabled_flag any more, pps_chroma_qp_offset_list_len_minus1 > 0 means there is CU level chroma QP offset is present.
Text are cleaner and # of syntax elements are reduced.
In the case of CU level chroma Qp offsets are in use, no need to add the CU level chroma QP offset with picture level chroma QP offset any more.

## Slide 10: Aspect #2 Syntax Table (cond)
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) { | Descriptor
… | 
if( treeType != DUAL_TREE_LUMA && palette_escape_val_present_flag ) | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded ) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && pps_chroma_qp_offset_list_len_minus1 > 0 1 ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
… | 
transform_unit( x0, y0, tbWidth, tbHeight, treeType, subTuIndex, chType ) { | Descriptor
… | 
if( ( CbWidth[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ CbHeight[ chType ][ x0 ][ y0 ] > 64 ¦ ¦ ( chromaAvailable && ( tu_cbf_cb[ xC ][ yC ] ¦ ¦ tu_cbf_cr[ xC ][ yC ] ) ) ) && treeType != DUAL_TREE_LUMA ) { | 
if( cu_chroma_qp_offset_enabled_flag && !IsCuChromaQpOffsetCoded) { | 
cu_chroma_qp_offset_flag | ae(v)
if( cu_chroma_qp_offset_flag && pps_chroma_qp_offset_list_len_minus1 > 1 ) | 
cu_chroma_qp_offset_idx | ae(v)
} | 
} | 
… | 

## Slide 11: Conclusion
Propose two aspects regarding chroma QP offsets.
  remove unnecessary signaling of chroma Qp offsets in transform unit and make it consistent with the signalling in palette coding syntax table,
  clean up of picture and CU level chroma QP signaling in PPS by merging them into one list.
Propose to adopt these cleanups to VVC draft