## Slide 1: JVET-Q0254 [AHG9]: Override mechanism for ALF related syntax elements in slice header
Anand Meher Kotra, Semih Esenlik, Biao Wang, Han Gao, Elena Alshina

## Slide 2: Introduction
Picture header is introduced in JVET-P2001-VE to mainly reduce the parsing overhead of slice header
ALF related syntax elements (ALF data) can be signalled either in the picture header or slice header but not both.

## Slide 3: Drawback of current picture header design for ALF
Slice 1.. Slice N-2 share the same ALF information as the picture header.
Slice 1
Slice 2
Slice 3
Slice N-2
…
Slice N-1
Slice N
Picture header
Defines one common ALF data where all slice headers can inherit data from
Since Slice N-1.. Slice N contain different ALF data
Fig. 1 Each slice header has to still transmit the redundant ALF data, even if the ALF data is the same for most of the slices in a given picture.
For a use case where multiple slices are present in a picture
  Most of the slices share the same ALF data
  Only one or few slices have a small difference in one of the ALF syntax elements
Current proposal proposes a override mechanism to further reduce the parsing overhead of slice header

## Slide 4
7.3.2.4 Picture header RBSP syntax
pic_parameter_set_rbsp( ) { | Descriptor
….
7.3.7.1 General slice header syntax
….
….
Syntax as per JVET-P2001-VE
….
if( sps_alf_enabled_flag ) { | 
pic_alf_enabled_present_flag | u(1)
if( pic_alf_enabled_present_flag ) { | 
pic_alf_enabled_flag | u(1)
if( pic_alf_enabled_flag ) { | 
pic_num_alf_aps_ids_luma | u(3)
for( i = 0; i < pic_num_alf_aps_ids_luma; i++ ) | 
pic_alf_aps_id_luma[ i ] | u(3)
if( ChromaArrayType != 0 ) | 
pic_alf_chroma_idc | u(2)
if( pic_alf_chroma_idc ) | 
pic_alf_aps_id_chroma | u(3)
} | 
} | 
} | 
slice_header( ) { | Descriptor
if( sps_alf_enabled_flag && !pic_alf_enabled_present_flag ) { | 
slice_alf_enabled_flag | u(1)
if( slice_alf_enabled_flag ) { | 
slice_num_alf_aps_ids_luma | u(3)
for( i = 0; i < slice_num_alf_aps_ids_luma; i++ ) | 
slice_alf_aps_id_luma[ i ] | u(3)
if( ChromaArrayType != 0 ) | 
slice_alf_chroma_idc | u(2)
if( slice_alf_chroma_idc ) | 
slice_alf_aps_id_chroma | u(3)
} | 
} | 

## Slide 5: ALF CTU syntax
….
coding_tree_unit( ) { | Descriptor
xCtb = CtbAddrX << CtbLog2SizeY | 
yCtb = CtbAddrY << CtbLog2SizeY | 
if( slice_sao_luma_flag ¦ ¦ slice_sao_chroma_flag ) | 
sao( CtbAddrX, CtbAddrY ) | 
if( slice_alf_enabled_flag ){ | 
alf_ctb_flag[ 0 ][ CtbAddrX ][ CtbAddrY ] | ae(v)
if( alf_ctb_flag[ 0 ][ CtbAddrX ][ CtbAddrY ] ) { | 
if( slice_num_alf_aps_ids_luma > 0 ) | 
alf_use_aps_flag | ae(v)
if( alf_use_aps_flag ) { | 
if( slice_num_alf_aps_ids_luma > 1 ) | 
alf_luma_prev_filter_idx | ae(v)
} else | 
alf_luma_fixed_filter_idx | ae(v)
} | 
if( slice_alf_chroma_idc = = 1 ¦ ¦ slice_alf_chroma_idc = = 3 ) { | 
alf_ctb_flag[ 1 ][ CtbAddrX ][ CtbAddrY ] | ae(v)
if( alf_ctb_flag[ 1 ][ CtbAddrX ][ CtbAddrY ] && aps_alf_chroma_num_alt_filters_minus1 > 0 ) | 
alf_ctb_filter_alt_idx[ 0 ][ CtbAddrX ][ CtbAddrY ] | ae(v)
} | 
if( slice_alf_chroma_idc = = 2 ¦ ¦ slice_alf_chroma_idc = = 3 ) { | 
alf_ctb_flag[ 2 ][ CtbAddrX ][ CtbAddrY ] | ae(v)
if( alf_ctb_flag[ 2 ][ CtbAddrX ][ CtbAddrX ] && aps_alf_chroma_num_alt_filters_minus1 > 0 ) | 
alf_ctb_filter_alt_idx[ 1 ][ CtbAddrX ][ CtbAddrX ] | ae(v)
} | 
} | 
coding_tree_unit( ) | alf_ctb_flag[ ][ ][ ] | FL | cMax = 1
 | alf_use_aps_flag | FL | cMax = 1
 | alf_luma_fixed_filter_idx | TB | cMax = 15
 | alf_luma_prev_filter_idx | TB | cMax = slice_num_alf_aps_ids_luma − 1
 | alf_ctb_filter_alt_idx[ ][ ][ ] | TR | cMax = alf_chroma_num_alt_filters_minus1, cRiceParam = 0

## Slide 6: ALF syntax design in VVC
Up to 8 different ALF parameter sets (ALF data) can be sent in 8 different APS (adaptation parameter sets)
Each Luma CTB can choose upto 8 different APS Ids when the slice containing the CTUS indicate it.
ALF data in the slice header can be upto 34 bits in the worst case
If CCALF tool gets adopted, then it might add few more syntax elements to the slice header.

## Slide 7: Solution
Picture header (PH) defines a initial ALF parameter set (ALF data)
A new syntax element slice_alf_override_flag is used as follows
  All slices which use the same ALF data as the picture header can re-use the data from PH (slice_alf_override_flag is set to 0)
  Only the slices which have different ALF data when compared to the PH override the ALF parameters and therefore define their own ALF parameters. (slice_alf_override_flag is set to 1)

## Slide 8: Solution
7.3.2.4 Picture header RBSP syntax
pic_parameter_set_rbsp( ) { | Descriptor
….
7.3.7.1 General slice header syntax
….
….
….
if( sps_alf_enabled_flag ) { | 
pic_alf_override_enabled_present_flag | u(1)
if( pic_alf_enabled_present_flag ) { | 
pic_alf_enabled_flag | u(1)
if( pic_alf_enabled_flag ) { | 
pic_num_alf_aps_ids_luma | u(3)
for( i = 0; i < pic_num_alf_aps_ids_luma; i++ ) | 
pic_alf_aps_id_luma[ i ] | u(3)
if( ChromaArrayType != 0 ) | 
pic_alf_chroma_idc | u(2)
if( pic_alf_chroma_idc ) | 
pic_alf_aps_id_chroma | u(3)
} | 
} | 
} | 
slice_header( ) { | Descriptor
…… | 
if( sps_alf_enabled_flag && !pic_alf_override_enabled_present_flag ) { | 
slice_alf_override_flag | u(1)
if(slice_alf_override_flag) { | 
slice_alf_enabled_flag | u(1)
if( slice_alf_enabled_flag ) { | 
slice_num_alf_aps_ids_luma | u(3)
for( i = 0; i < slice_num_alf_aps_ids_luma; i++ ) | 
slice_alf_aps_id_luma[ i ] | u(3)
if( ChromaArrayType != 0 ) | 
slice_alf_chroma_idc | u(2)
if( slice_alf_chroma_idc ) | 
slice_alf_aps_id_chroma | u(3)
} | 
} | 
…….. | 

## Slide 9: Solution (continued)
pic_alf_override_enabled_flag equal to 1 specifies the presence of slice_alf_ovderride_flag in the slice header referrring to the PH. Pic_alf_override_enabled_flag equal to 0 specifies the absence of slice_alf_ovderride_flag in the slice header referring to the PH. When not present, the value of pic_alf_override_enabled_flag is inferred to be equal to 0.
slice_alf_override_flag equal to 1 specifies that the ALF parameters are present in the slice header. slice_alf_override_flag equal to 0 specifies that ALF parameters are not present in the slice header. When not present, the value of slice_alf_override_flag is inferred to be equal to 0.

## Slide 10: Feedback from BOG conducted on 7th Jan
Simplify the “if” condition in slice header syntax
Re-name the pic_alf_enabled_flag ?
  After carefully checking the sematics of pic_alf_enabled_flag, it seems we need not rename the flag
  pic_alf_enabled_flag equal to 1 specifies that adaptive loop filter is enabled for all slices associated with the PH and may be applied to Y, Cb, or Cr colour component in the slices. pic_alf_enabled_flag equal to 0 specifies that adaptive loop filter may be disabled for one, or more, or all slices associated with the PH. When not present, pic_alf_enabled_flag is inferred to be equal to 0.
slice_header( ) { | Descriptor
…… | 
if( sps_alf_enabled_flag && !pic_alf_override_enabled_present_flag ) { | 
slice_alf_override_flag | u(1)
if(slice_alf_override_flag) { | 
slice_alf_enabled_flag | u(1)
if( slice_alf_enabled_flag ) { | 
slice_num_alf_aps_ids_luma | u(3)
for( i = 0; i < slice_num_alf_aps_ids_luma; i++ ) | 
slice_alf_aps_id_luma[ i ] | u(3)
if( ChromaArrayType != 0 ) | 
slice_alf_chroma_idc | u(2)
if( slice_alf_chroma_idc ) | 
slice_alf_aps_id_chroma | u(3)
} | 
} | 
…….. | 

## Slide 11: Different scenarios
Typical case where all slices share the same ALF Information
  ALF is completely switched “off” for current picture
    pic_alf_override_enabled_flag is set to 0
    pic_alf_enabled_flag is set to 0
  ALF is switched “on” for current picture
    pic_alf_override_enabled_flag is set to 0
    pic_alf_enabled_flag is set to 1
Case where slices have different ALF data
  pic_alf_override_enabled_flag is set to 1
  pic_alf_enabled_flag can be set to 0
  slice_alf_override_flag when set to 1 will enable slice to transmit its own ALF info
  slice_alf_override_flag when set to 0 will enable slice to inherit information from picture header