## Slide 1
JVET-Q0294
CE3-related: CTU level local lossless coding of VVC
2020/1/9

## Slide 2
Proposed method
Propose a CTU level lossless flag for local lossless coding
  Motivation:
    Finer granularity of lossless coding
    Current VVC design supports CTB level control of ALF and SAO
coding_tree_unit( ) { | Descriptor
xCtb = CtbAddrX << CtbLog2SizeY | 
yCtb = CtbAddrY << CtbLog2SizeY | 
ctu_lossless_flag[ CtbAddrX ][ CtbAddrY ] | u(1)
……. | 
} | 
Coding tools | VTM-7.0 | Proposed CTU level control
LMCS | Disable in SPS level | Disable if ctu_lossless_flag == 1
DF | Disable in SPS level | Disable if ctu_lossless_flag == 1
SAO | Disable in SPS level | Disable if ctu_lossless_flag == 1
ALF | Disable in SPS level | Disable if ctu_lossless_flag == 1
JointCbCr | Disable in SPS level | Disable if ctu_lossless_flag == 1
SBT | Disable in SPS level | Disable if ctu_lossless_flag == 1
ISP | Disable in SPS level | Disable if ctu_lossless_flag == 1
MTS | Disable in SPS level | Disable if ctu_lossless_flag == 1
LFNST | Disable in SPS level | Disable if ctu_lossless_flag == 1
transform_skip_flag | Signal each TB | if ctu_lossless_flag == 1, transform_skip_flag is inferred to be 1.

## Slide 3
Proposed method
To increase the performance of lossless CTU, we also propose CTU level residual coding flag.
coding_tree_unit( ) { | Descriptor
xCtb = CtbAddrX << CtbLog2SizeY | 
yCtb = CtbAddrY << CtbLog2SizeY | 
ctu_lossless_flag[ CtbAddrX ][ CtbAddrY ] | u(1)
if (ctu_lossless_flag[ CtbAddrX ][ CtbAddrY ]) | 
ctu_rrc_flag[ CtbAddrX ][ CtbAddrY ] | u(1)
……. | 
} | 

## Slide 4
Simulation results
Following tests are conducted
  Test 1: VTM-7.0 TSRC
  Test 2: TSRC proposed in JVET-Q0269.
  Test 3:
    Camera capture content are coded using RRC.
    Class F & TGM sequences are coded in TSRC with rice parameter derivation proposed in JVET-Q0269.
  Test 4: Test 3 + Luma BDPCM on

## Slide 5
Summary results
 | AI | RA | LB
Test 1 | -0.01% | -0.01% | -0.01%
Test 2 | -4.33% | -2.61% | -1.99%
Test 3 | -5.24% | -5.59% | -4.98%
Test 4 | -6.77% | -5.97% | -5.55%
 | AI | RA | LB
Test 1 | -0.01% | 0.09% | -0.09%
Test 2 | -5.20% | -6.61% | -6.80%
Test 3 | -5.20% | -6.61% | -6.80%
Test 4 | -7.01% | -7.44% | -7.39%
Overall
TGM

## Slide 6
Conclusions
Supports local lossless coding
CTU level control
Minimal changes on current VVC design for local lossless

## Slide 7: Backup

## Slide 8
Test 1
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | Ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-7.0 | test 1 |  | VTM-7.0 | test 1 |  | VTM-7.0 | test 1 | 
Class A1 | 2.2 | 2.2 | -0.01% | 2.2 | 2.2 | -0.01% |  |  | 
Class A2 | 1.6 | 1.6 | -0.01% | 1.7 | 1.7 | -0.01% |  |  | 
Class B | 2.2 | 2.2 | -0.01% | 2.3 | 2.3 | -0.01% | 2.3 | 2.3 | -0.01%
Class C | 1.9 | 1.9 | -0.01% | 2.4 | 2.4 | -0.01% | 2.4 | 2.4 | -0.01%
Class D | 1.9 | 1.9 | -0.01% | 2.8 | 2.8 | -0.02% | 2.7 | 2.7 | -0.03%
Class E | 2.8 | 2.8 | -0.01% |  |  |  | 3.1 | 3.1 | -0.01%
Class F | 5.3 | 5.3 | -0.02% | 33.7 | 33.7 | 0.01% | 50.7 | 50.7 | 0.02%
TGM | 11.8 | 11.8 | -0.01% | 107.1 | 107.0 | 0.09% | 124.9 | 125.1 | -0.09%
Overall | 2.1 | 2.1 | -0.01% | 2.2 | 2.2 | -0.01% | 2.6 | 2.6 | -0.01%
Enc Time[%] | 101% |  |  | 102% |  |  | 102% |  | 
Dec Time[%] | 88% |  |  | 92% |  |  | 93% |  | 
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | Ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-7.0 | test 2 |  | VTM-7.0 | test 2 |  | VTM-7.0 | test 2 | 
Class A1 | 2.2 | 2.3 | -3.50% | 2.2 | 2.3 | -3.34% |  |  | 
Class A2 | 1.6 | 1.7 | -7.56% | 1.7 | 1.8 | -5.10% |  |  | 
Class B | 2.2 | 2.2 | -2.97% | 2.3 | 2.4 | -1.02% | 2.3 | 2.4 | -1.01%
Class C | 1.9 | 2.0 | -4.25% | 2.4 | 2.5 | -2.19% | 2.4 | 2.5 | -2.05%
Class D | 1.9 | 2.0 | -4.90% | 2.8 | 2.8 | -2.40% | 2.7 | 2.8 | -2.23%
Class E | 2.8 | 2.9 | -4.29% |  |  |  | 3.1 | 3.2 | -3.55%
Class F | 5.3 | 5.5 | -3.84% | 33.7 | 34.9 | -3.04% | 50.7 | 52.2 | -2.81%
TGM | 11.8 | 12.5 | -5.20% | 107.1 | 116.4 | -6.61% | 124.9 | 136.8 | -6.80%
Overall | 2.1 | 2.2 | -4.33% | 2.2 | 2.3 | -2.61% | 2.6 | 2.6 | -1.99%
Enc Time[%] | 97% |  |  | 99% |  |  | 101% |  | 
Dec Time[%] | 90% |  |  | 94% |  |  | 98% |  | 
Test 2
Simulation results

## Slide 9
Test 3
Test 4
Simulation results
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | Ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-7.0 | test 3 |  | VTM-7.0 | test 3 |  | VTM-7.0 | test 3 | 
Class A1 | 2.2 | 2.4 | -5.42% | 2.2 | 2.4 | -6.26% |  |  | 
Class A2 | 1.6 | 1.7 | -8.86% | 1.7 | 1.9 | -8.13% |  |  | 
Class B | 2.2 | 2.3 | -4.02% | 2.3 | 2.4 | -3.84% | 2.3 | 2.4 | -3.85%
Class C | 1.9 | 2.0 | -4.98% | 2.4 | 2.6 | -5.37% | 2.4 | 2.6 | -5.30%
Class D | 1.9 | 2.0 | -4.64% | 2.8 | 2.9 | -5.29% | 2.7 | 2.9 | -5.27%
Class E | 2.8 | 2.9 | -3.83% |  |  |  | 3.1 | 3.3 | -6.43%
Class F | 5.3 | 5.5 | -3.84% | 33.7 | 34.9 | -3.04% | 50.7 | 52.2 | -2.81%
TGM | 11.8 | 12.5 | -5.20% | 107.1 | 116.4 | -6.61% | 124.9 | 136.8 | -6.80%
Overall | 2.1 | 2.2 | -5.24% | 2.2 | 2.3 | -5.59% | 2.6 | 2.7 | -4.98%
Enc Time[%] | 95% |  |  | 100% |  |  | 98% |  | 
Dec Time[%] | 89% |  |  | 92% |  |  | 98% |  | 
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | ratio |  | bit-rate savings | Ratio |  | bit-rate savings | ratio |  | bit-rate savings
 | VTM-7.0 | test 3 |  | VTM-7.0 | test 3 |  | VTM-7.0 | test 3 | 
Class A1 | 2.2 | 2.4 | -5.82% | 2.2 | 2.4 | -6.52% |  |  | 
Class A2 | 1.6 | 1.8 | -10.00% | 1.7 | 1.9 | -8.40% |  |  | 
Class B | 2.2 | 2.3 | -5.59% | 2.3 | 2.5 | -4.30% | 2.3 | 2.4 | -4.34%
Class C | 1.9 | 2.1 | -6.42% | 2.4 | 2.6 | -5.80% | 2.4 | 2.6 | -5.75%
Class D | 1.9 | 2.1 | -7.51% | 2.8 | 2.9 | -5.80% | 2.7 | 2.9 | -5.66%
Class E | 2.8 | 3.0 | -6.94% |  |  |  | 3.1 | 3.4 | -7.30%
Class F | 5.3 | 5.8 | -7.10% | 33.7 | 35.7 | -4.41% | 50.7 | 53.0 | -4.02%
TGM | 11.8 | 12.8 | -7.01% | 107.1 | 117.5 | -7.44% | 124.9 | 137.6 | -7.39%
Overall | 2.1 | 2.3 | -6.77% | 2.2 | 2.4 | -5.97% | 2.6 | 2.7 | -5.55%
Enc Time[%] | 107% |  |  | 104% |  |  | 103% |  | 
Dec Time[%] | 83% |  |  | 91% |  |  | 98% |  |