## Slide 1: JVET-Q0304 Non-CE5: Non-Linear Cross Component Adaptive Loop Filter
Fujitsu
17th Meeting: Brussels, BE, 7–17 January 2020

## Slide 2: Cross Component Adaptive Loop Filter
,
  which is the center of
  is input luma samples
Si
)

## Slide 3: Non-Linear Cross Component Adaptive Loop Filter
Reformulated CCALF
  ,
    Sum of filter coefficients is 0
  Introduce non linearity using a clipping function
  ,
    is the clipping function
    are clipping parameters
BitDepth | clipIdx |  |  | 
 | 0 | 1 | 2 | 3
8 | 255 | 50 | 10 | 2
9 | 511 | 100 | 20 | 4
10 | 1023 | 201 | 39 | 8
11 | 2047 | 402 | 79 | 15
12 | 4095 | 803 | 158 | 31
13 | 8191 | 1607 | 315 | 62
14 | 16383 | 3214 | 630 | 124
15 | 32767 | 6427 | 1261 | 247
16 | 65535 | 12855 | 2521 | 495
Notes: 1. Given condition sum of C are zero. Expresion 1 can be reformulated as expression 2 with 7 coeff without coding efficiency impact.
  2. Based on expression (2) Use a clipping function to reduce the impact of neighbor sample values when they are too different with the current sample value
Function b and b are input and clipping range
  Derived in bellowing table depending on BitDepth of luma and clipIdx in the range of 0 to 3. The encoder performs the optimization to find the best 𝑘(𝑥_0,𝑦_0) per filter coefficient

## Slide 4: signaling
ccalf_cb_clip_idx & ccalf_cr_clip_idx
  One clipping parameter per filter coefficient
ccalf_cb_clip_flag & ccalf_cr_clip_flag
  A flag indicating whether Non-linear CCALF is performed
  If the flag is false, the clipping parameters are not signaled
alf_data( ) { | Descriptor
… | 
if ( alf_cross_component_cb_filter_signal_flag ) { | 
alf_cross_component_cb_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cb_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 7; j++ ) | 
alf_cross_component_cb_coeff_plus32[ k ][ j ] | u(6)
ccalf_cb_clip_flag[k] | u(1)
if( ccalf_cb_clip_flag[k] ) { | 
for( j = 0; j < 7; j++ ) | 
ccalf_cb_clip_idx[ k ][ j ] | u(2)
} | 
} | 
} | 
if ( alf_cross_component_cr_ filter_signal_flag ) { | 
alf_cross_component_cr_filters_signalled_minus1 | ue(v)
for( k = 0; k < (alf_cross_component_cr_filters_signalled_minus1+1); k++ ) { | 
for ( j = 0; j < 7; j++ ) | 
alf_cross_component_cr_coeff_plus32[ k ][ j ] | u(6)
ccalf_cr_clip_flag[k] | u(1)
if( ccalf_cr_clip_flag[k] ) { | 
for( j = 0; j < 7; j++ ) | 
ccalf_cr_clip_idx[ k ][ j ] | u(2)
} | 
} | 
} | 
} | 
Notes: "Clipping parameters" signaling same as NL-ALF

## Slide 5: Results
Result over CE5 anchor
  0.08 on AI
  0.11 on RA
  0.16 on LB
  Encoding time is not reliable
 | All Intra Main10 |  |  |  |  | 
 | Over CE5 anchor |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.01% | -0.15% | -0.36% | -0.04% | 92% | 102%
Class A2 | 0.01% | -0.87% | -1.17% | -0.20% | 87% | 102%
Class B | 0.01% | -0.61% | -0.37% | -0.09% | 90% | 102%
Class C | 0.00% | -0.16% | -0.20% | -0.03% | 95% | 101%
Class E | 0.00% | -0.14% | -0.20% | -0.03% | 88% | 101%
Overall | 0.01% | -0.40% | -0.44% | -0.08% | 91% | 102%
Class D | 0.00% | -0.07% | -0.07% | -0.01% | 81% | 98%
Class F | 0.03% | -0.45% | -0.35% | -0.06% | 90% | 101%
 | Random access Main10 |  |  |  |  | 
 | Over CE5 anchor |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.02% | -0.31% | -0.59% | -0.07% | 102% | 100%
Class A2 | 0.01% | -0.71% | -0.53% | -0.11% | 100% | 101%
Class B | 0.01% | -0.84% | -0.86% | -0.16% | 115% | 101%
Class C | -0.01% | -0.35% | -0.17% | -0.06% | 99% | 102%
Class E |  |  |  |  |  | 
Overall | 0.01% | -0.58% | -0.56% | -0.11% | 105% | 101%
Class D | -0.02% | -0.06% | 0.03% | -0.02% | 112% | 100%
Class F | 0.01% | -0.62% | -0.52% | -0.11% | 112% | 100%
 | Low delay B Main10 |  |  |  |  | 
 | Over CE5 anchor |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | 0.03% | -1.46% | -1.07% | -0.23% | 100% | 100%
Class C | -0.07% | -0.28% | -0.25% | -0.11% | 111% | 100%
Class E | 0.00% | -0.68% | -0.47% | -0.11% | 100% | 100%
Overall | -0.01% | -0.87% | -0.65% | -0.16% | 104% | 100%
Class D | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
Class F | #VALUE! | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 6: Conclusion
Non-Linear Cross Component Adaptive Loop Filter
  Using a simple clipping function to reduce the impact of neighbor sample values
  Coding gain of 0.08%, 0.11%, and 0.16% for AI, RA and LDB using AHG13 YUV metric
Suggest adopt this contribution for CCALF
Thanks for Sharp’s cross-checking