## Slide 1
JVET-Q0330 On block partitioning at picture boundary
2020/1/11

## Slide 2
In VVC draft 7, a block that exceed the picture boundary is forced to be split until all the samples are located inside the picture boundary
For a block exceeding the picture boundary, split_cu_flag is inferred to be 1
However, there are two cases that none of splitting method is allowed
Introduction

## Slide 3
When min QT size is set to 128 and size of a block is 128, none of splitting method is allowed for the block
Problem statement 1
QT splitting
If one or more of the following conditions are true, allowSplitQt is set equal to FALSE:
  treeType is equal to SINGLE_TREE or DUAL_TREE_LUMA and cbSize is less than or equal to MinQtSizeY
BT_Ver splitting
Otherwise, if all of the following conditions are true, allowBtSplit is set equal to FALSE
  btSplit is equal to SPLIT_BT_VER
  cbHeight is greater than 64
  x0 + cbWidth is greater than pic_width_in_luma_samples
BT_Hor splitting
Otherwise, if all of the following conditions are true, allowBtSplit is set equal to FALSE
  btSplit is equal to SPLIT_BT_HOR
  cbWidth is greater than 64
  y0 + cbHeight is greater than pic_height_in_luma_samples

## Slide 4
When MTT depth is set to 0 and size of a block is equal to min QT size, none of splitting method is allowed
Problem statement 2
QT splitting
If one or more of the following conditions are true, allowSplitQt is set equal to FALSE:
  treeType is equal to SINGLE_TREE or DUAL_TREE_LUMA and cbSize is less than or equal to MinQtSizeY
BT_Ver or BT_Hor splitting
If one or more of the following conditions are true, allowBtSplit is set equal to FALSE:
    mttDepth is greater than or equal to maxMttDepth
Example:
Min QT size = 64
MTT depth = 0
No splitting method is allowed for the red blocks

## Slide 5
Use QT split when a block exceeds the picture boundary and none of splitting method is allowed
Proposed method
split_qt_flag specifies whether a coding unit is split into coding units with half horizontal and vertical size.
When split_qt_flag is not present, the following applies:
If all of the following conditions are true, split_qt_flag is inferred to be equal to 1:
  split_cu_flag is equal to 1
  allowSplitQt, allowSplitBtHor, allowSplitBtVer, allowSplitTtHor and allowSplitTtVer are eqaul to FALSE.
Otherwise, iIf allowSplitQt is equal to TRUE, the value of split_qt_flag is inferred to be equal to 1.
Otherwise, the value of split_qt_flag is inferred to be equal to 0.