## Slide 1: JVET-Q0338 CE4-related: Harmonized conditions for CIIP and GEO
N. Park, J. Nam, H. Jang, J. Lim, S. Kim

## Slide 2: Introduction
In GEO mode, following 3 constraints are applied.
  GEO mode is disabled when block width or height is less than 8 by the common base.
  GEO mode is disabled when block width or height is larger than 64 by CE4-2.1.
  GEO mode is disabled when block size is 64x8 or 8x64 by the JVET-Q0309 (JVET-Q0123)
These constraints contributes to the number of the parsing conditions for CIIP and GEO becomes larger.

## Slide 3: Introduction
merge_data( x0, y0, cbWidth, cbHeight, chType ) { | Descriptor
…… | 
if( ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 && ( (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0) ¦ ¦ ( sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && cbWidth>=8 && cbHeight >=8 && slice_type = = B ) ) ) | 
regular_merge_flag[ x0 ][ y0 ] | ae(v)
if( regular_merge_flag[ x0 ][ y0 ] = = 1 ) { | 
if( sps_mmvd_enabled_flag ) | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
…… | 
} else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( sps_ciip_enabled_flag && sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && slice_type = = B && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth >= 8 && cbHeight >= 8 ) | 
ciip_flag[ x0 ][ y0 ] | ae(v)
…… | 
In GEO common base + CE4-2.1
  To parse the regular merge, CIIP and GEO, 1 multiplication, 6 “AND” and 7 “COMPARISION” are required.

## Slide 4: Proposed methods
Different constrained block size for CIIP and GEO makes the parsing condition complicated.
In this proposal, the block size constraint for CIIP and GEO on parsing conditions are unified.
 | GEO | CIIP
VTM7.0 | cbWidth >= 8 && cbHeight >= 8 | ( cbWidth * cbHeight ) >= 64 cbWidth < 128 && cbHeight < 128
Proposed Method I | cbWidth >= 8 && cbHeight >= 8 cbWidth < 128 && cbHeight < 128 | cbWidth >= 8 && cbHeight >= 8 cbWidth < 128 && cbHeight < 128
Green marks was adopted by CE4-2.1
Yellow marks was proposed in this proposal

## Slide 5: Proposed methods
In Method 1, 1 multiplication, 6 “AND” and 7 “COMPARISION” are reduced to 3“AND” and 4 “COMPARISION”.
The parsing condition of the “regular_merge_flag” | if( cbWidth>=8 && cbHeight >=8 && cbWidth < 128 && cbHeight < 128 && ( (sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0) ¦ ¦ ( sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && cbWidth>=8 && cbHeight >=8 && slice_type = = B ) ) ) regular_merge_flag[ x0 ][ y0 ]
The parsing condition of the “ciip_flag” | if( regular_merge_flag[ x0 ][ y0 ] = = 1 ) { …… } else { if( sps_ciip_enabled_flag && sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && slice_type = = B && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth >= 8 && cbHeight >= 8 ) ciip_flag[ x0 ][ y0 ] }

## Slide 6: Proposed methods
merge_data( x0, y0, cbWidth, cbHeight, chType ) { | Descriptor
…… | 
if ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 && ( sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 ) ¦ ¦ ( sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && cbWidth>=8 && cbHeight >=8 && cbWidth+cbHeight !=72 && slice_type = = B ) ) | 
regular_merge_flag[ x0 ][ y0 ] | ae(v)
if( regular_merge_flag[ x0 ][ y0 ] = = 1 ) { | 
if( sps_mmvd_enabled_flag ) | 
mmvd_merge_flag[ x0 ][ y0 ] | ae(v)
…… | 
} else if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
if( sps_ciip_enabled_flag && sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && slice_type = = B && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth >= 8 && cbHeight >= 8 && cbWidth+cbHeight !=72 ) | 
ciip_flag[ x0 ][ y0 ] | ae(v)
…… | 
In the GEO common base + CE4-2.1 + JVET-Q0309(JVET-Q0123)
  1 multiplication, 2 adds, 8 “AND” and 9 “COMPARISION” are required.

## Slide 7: Proposed methods
Different constrained block size for CIIP and GEO makes the parsing condition complicated.
In this proposal, the block size constraint for CIIP and GEO on parsing conditions are unified.
 | GEO | CIIP
VTM7.0 | cbWidth >= 8 && cbHeight >= 8 | ( cbWidth * cbHeight ) >= 64 cbWidth < 128 && cbHeight < 128
Proposed Method II | cbWidth >= 8 && cbHeight >= 8 cbWidth < 128 && cbHeight < 128 cbWidth+cbHeight !=72 | cbWidth >= 8 && cbHeight >= 8 cbWidth < 128 && cbHeight < 128 cbWidth+cbHeight !=72
Green marks was adopted by CE4-2.1
Red color was adopted by JVET-Q0309
Yellow marks was proposed in this proposal

## Slide 8: Proposed methods
In Method 2, 1 multiplication, 2 adds, 8 “AND” and 9 “COMPARISION” are reduced to 1 add, 4 “AND” and 5 “COMPARISION”.
The parsing condition of the “regular_merge_flag” | If (cbWidth>=8 && cbHeight >=8 && cbWidth+cbHeight !=72 ( cbWidth * cbHeight ) >= 64 && cbWidth < 128 && cbHeight < 128 && ( sps_ciip_enabled_flag && cu_skip_flag[ x0 ][ y0 ] = = 0 ) ¦ ¦ ( sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && cbWidth>=8 && cbHeight >=8 && cbWidth+cbHeight !=72 && slice_type = = B ) ) regular_merge_flag[ x0 ][ y0 ]
The parsing condition of the “ciip_flag” | if( regular_merge_flag[ x0 ][ y0 ] = = 1 ) { …… } else { if( sps_ciip_enabled_flag && sps_geo_enabled_flag && MaxNumGeoMergeCand > 1 && slice_type = = B && cu_skip_flag[ x0 ][ y0 ] = = 0 && cbWidth >= 8 && cbHeight >= 8 && cbWidth+cbHeight !=72 ) ciip_flag[ x0 ][ y0 ] }

## Slide 9: Proposed methods
By the 4xN, Nx4 block restriction, conditions on sample prediction process of the CIIP are removed.
When ciip_flag[ xCb ][ yCb ] is equal to 1, the array predSamples of prediction samples is modified as follows: If cIdx is equal to 0, the following applies: 8.4.5.2.5 General intra sample prediction process 8.5.6.7 Weighted sample prediction process Otherwise, if cIdx is equal to 1 and cbWidth / SubWidthC is greater than or equal to 4, the following applies: 8.4.5.2.5 General intra sample prediction process 8.5.6.7 Weighted sample prediction process Otherwise, if cIdx is equal to 2 and cbWidth / SubWidthC is greater than or equal to 4, the following applies: 8.4.5.2.5 General intra sample prediction process 8.5.6.7 Weighted sample prediction process

## Slide 10: Proposed methods
Complexity analysis
  For parser
  For decoding process
    “cbWidth / SubWidthC is greater than or equal to 4” conditions in both methods are removed.
 | Conditions | Proposed Method 1 | Proposed Method 2
GEO common base + CE4-2.1 | 1 multiplication 6 “AND” 7 “COMPARISION” | 3 “AND” 4 “COMPARISION” | 
GEO common base + CE4-2.1 + JVET-Q0309 | 1 multiplication 2 adds 8 “AND” 9 “COMPARISION” |  | 1 add 4 “AND” 5 “COMPARISION”

## Slide 11: Simulation results
Simulation results (anchor : CE4-2.1)
Simulation results (anchor : CE4-2.1 + 64x8, 8x64 restriction)
 | Over VTM7.0 with CE4-2.1 |  |  |  |  |  |  |  |  | 
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.04% | 0.00% | 100% | 99% |  |  |  |  | 
Class A2 | 0.03% | 0.04% | 0.02% | 100% | 99% |  |  |  |  | 
Class B | 0.00% | -0.04% | 0.04% | 100% | 98% | 0.04% | -0.19% | 0.02% | 99% | 99%
Class C | 0.07% | 0.02% | 0.00% | 100% | 99% | 0.08% | -0.09% | 0.00% | 99% | 99%
Class E |  |  |  |  |  | 0.08% | 0.40% | 0.21% | 100% | 102%
Overall | 0.02% | -0.01% | 0.02% | 100% | 99% | 0.06% | -0.01% | 0.06% | 100% | 100%
Class D | 0.03% | -0.01% | 0.14% | 99% | 99% | 0.03% | 0.71% | 0.06% | 99% | 96%
Class F | 0.02% | 0.00% | -0.02% | 100% | 99% | 0.03% | -0.60% | -0.54% | 100% | 98%
 | Over VTM7.0 with CE4-2.1 |  |  |  |  |  |  |  |  | 
 | Random access Main10 |  |  |  |  | Low delay B Main10 |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 |  |  |  |  |  |  |  |  |  | 
Class A2 |  |  |  |  |  |  |  |  |  | 
Class B | 0.00% | 0.05% | 0.11% | 100% | 100% |  |  |  |  | 
Class C | 0.07% | 0.03% | 0.01% | 99% | 100% | 0.05% | 0.08% | 0.15% | 99% | 100%
Class E |  |  |  |  |  | -0.04% | 0.04% | -0.11% | 99% | 99%
Overall |  |  |  |  |  |  |  |  |  | 
Class D | 0.03% | 0.05% | 0.11% | 100% | 101% | 0.09% | -0.26% | -0.37% | 99% | 100%
Class F | 0.07% | 0.02% | 0.06% | 100% | 101% |  |  |  |  | 

## Slide 12: Conclusion
In this contribution, harmonized conditions for CIIP and GEO mode are proposed.
The simulation results reportedly show minor changes.
It is recommended to consider this method in the next VTM.
Thanks to Bytedance (JVET-Q0575) for crosscheck