## Slide 1
CE3-related: Fixed rice parameters in transform residual coding
JVET-Q0347
Y. Chen, F. Le Léannec, F. Galpin, T. Poirier

## Slide 2: JVET-Q0347: CE3-related: Fixed rice parameters in transform residual coding
Motivation
  High-throughput CABAC mode proposed during last meeting (JVET-P0300)
  Meeting notes: ”There could also be other throughput issues even with bypass coding, e.g. to determine Rice parameters.”
  This contribution proposes fixed Rice Param for RRC as for TSRC for further increased throughput

## Slide 3: JVET-Q0347: CE3-related: Fixed rice parameters in transform residual coding
In VTM 7.0, per-sample adaptive codewords (Golomb Rice) is used for the coding of the level remainder abs_remainder and dec_abs_level in regular transform residual coding (RRC)
  Rice parameter is determined based on the sum of absolute levels (locSumAbs) of the 5 neighboring transform coefficients, and the corresponding base level
Proposed methods to replace per-sample adaptive codewords with fixed codewords
  abs_remainder: rice parameter is fixed as 0
  dec_abs_level: rice parameter is fixed as 1
  GOAL: increase the throughput, in particular in the case of high throughput scenario
locSumAbs | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
RiceParam | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2
locSumAbs | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31
RiceParam | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3

## Slide 4: JVET-Q0347: standard QPs
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.05% | -0.06% | 0.20% | 99% | 100%
Class A2 | 0.07% | 0.17% | 0.09% | 99% | 100%
Class B | 0.06% | 0.09% | -0.03% | 98% | 99%
Class C | 0.08% | 0.04% | 0.04% | 97% | 99%
Class E | 0.05% | 0.00% | 0.06% | 99% | 100%
Overall | 0.07% | 0.05% | 0.06% | 98% | 99%
Class D | 0.12% | 0.20% | 0.17% | 98% | 98%
Class F | 0.10% | 0.01% | 0.20% | 98% | 98%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.06% | -0.08% | 0.09% | 102% | 105%
Class A2 | 0.02% | 0.12% | 0.19% | 102% | 103%
Class B | 0.05% | 0.11% | 0.09% | 99% | 105%
Class C | 0.09% | -0.05% | -0.03% | 99% | 101%
Class E |  |  |  |  | 
Overall | 0.06% | 0.03% | 0.08% | 100% | 103%
Class D | 0.09% | -0.07% | 0.30% | 100% | 102%
Class F | 0.11% | 0.23% | 0.14% | 100% | 104%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.25% | 0.16% | 99% | 106%
Class C | 0.04% | -0.27% | -0.02% | 99% | 96%
Class E | -0.06% | -0.11% | 0.31% | 99% | 95%
Overall | 0.00% | -0.22% | 0.14% | 99% | 100%
Class D | 0.00% | -0.08% | -0.60% | 99% | 100%
Class F | -0.04% | -0.39% | 0.51% | 99% | 97%

## Slide 5: JVET-Q0347: low QPs
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.45% | 0.66% | 0.63% | 96% | 100%
Class A2 | 1.80% | 2.11% | 2.13% | 96% | 103%
Class B | 1.57% | 1.70% | 1.77% | 95% | 104%
Class C | 2.72% | 2.90% | 3.01% | 93% | 106%
Class E | 1.30% | 1.47% | 1.53% | 96% | 102%
Overall | 1.63% | 1.82% | 1.88% | 95% | 103%
Class D | 3.07% | 3.16% | 3.19% | 92% | 105%
Class F | 1.00% | 1.22% | 1.26% | 97% | 102%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.49% | 0.64% | 0.62% | 97% | 100%
Class C | 1.12% | 1.45% | 1.47% | 96% | 100%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 1.29% | 1.69% | 1.48% | 96% | 101%
Class F | 0.54% | 0.90% | 0.87% | 98% | 102%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.38% | 0.49% | 0.48% | 97% | 101%
Class C | 0.92% | 1.26% | 1.33% | 97% | 103%
Class E | 0.10% | 0.14% | 0.10% | 98% | 100%
Overall | 0.49% | 0.66% | 0.67% | 97% | 101%
Class D | 0.97% | 1.20% | 1.07% | 97% | 100%
Class F | 0.55% | 0.58% | 0.56% | 98% | 100%

## Slide 6: JVET-Q0347 + JVET-P0300(High Throughput mode): standard QPs
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 7.08% | 4.34% | 4.65% | 106% | 96%
Class A2 | 5.77% | 3.86% | 6.67% | 95% | 94%
Class B | 3.29% | 3.71% | 3.13% | 96% | 93%
Class C | 2.57% | 3.49% | 3.60% | 91% | 92%
Class E | 2.44% | 3.68% | 3.46% | 92% | 95%
Overall | 4.03% | 3.79% | 4.13% | 95% | 94%
Class D | 2.17% | 3.06% | 3.40% | 89% | 92%
Class F | 6.10% | 7.10% | 6.82% | 92% | 94%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 7.18% | 10.43% | 8.77% | 97% | 104%
Class A2 | 4.40% | 5.55% | 7.04% | 94% | 105%
Class B | 4.58% | 5.64% | 3.56% | 96% | 105%
Class C | 3.70% | 5.34% | 3.87% | 94% | 99%
Class E |  |  |  |  | 
Overall | 4.83% | 6.50% | 5.38% | 95% | 103%
Class D | 3.40% | 4.53% | 3.72% | 94% | 99%
Class F | 7.07% | 8.92% | 8.39% | 96% | 103%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 4.50% | 5.42% | -0.73% | 95% | 98%
Class C | 3.12% | 5.46% | 1.13% | 94% | 94%
Class E | 2.63% | 2.02% | -0.20% | 96% | 94%
Overall | 3.57% | 4.59% | 0.03% | 95% | 95%
Class D | 3.19% | 3.23% | -0.05% | 94% | 97%
Class F | 6.44% | 9.42% | 7.74% | 95% | 95%

## Slide 7: Reference JVET-P0300(High Throughput mode): standard QPs
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 6.99% | 4.22% | 4.55% | 109% | 92%
Class A2 | 5.68% | 3.73% | 6.48% | 95% | 90%
Class B | 3.22% | 3.60% | 3.04% | 132% | 106%
Class C | 2.48% | 3.42% | 3.55% | 128% | 104%
Class E | 2.38% | 3.57% | 3.39% | 132% | 106%
Overall | 3.95% | 3.68% | 4.04% | 120% | 100%
Class D | 2.05% | 3.05% | 3.23% | 129% | 105%
Class F | 6.02% | 7.04% | 6.79% | 120% | 105%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 7.10% | 10.22% | 8.65% | 97% | 122%
Class A2 | 4.35% | 5.61% | 7.00% | 98% | 116%
Class B | 4.57% | 5.53% | 3.63% | 97% | 117%
Class C | 3.60% | 5.35% | 3.79% | 113% | 114%
Class E |  |  |  |  | 
Overall | 4.77% | 6.44% | 5.35% | 101% | 117%
Class D | 3.29% | 4.24% | 3.56% | 118% | 109%
Class F | 6.96% | 8.63% | 8.28% | 117% | 116%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 4.48% | 5.54% | -0.59% | 95% | 97%
Class C | 3.07% | 5.41% | 0.95% | 95% | 93%
Class E | 2.65% | 2.45% | -0.05% | 96% | 93%
Overall | 3.55% | 4.72% | 0.06% | 95% | 95%
Class D | 3.07% | 3.16% | 0.20% | 95% | 97%
Class F | 6.60% | 8.92% | 7.69% | 96% | 96%

## Slide 8: Conclusion
In regular residual coding (RRC), it is proposed to use fixed rice parameters
  abs_remainder: rice parameter is fixed as 0
  dec_abs_level: rice parameter is fixed as 1
Per-sample codeword determination and look-up table for rice parameter derivation can be removed with few losses
Unify the rice parameter decision between RRC and TSRC (fixed rice parameters)
It can be combined with the “High throughput CABAC mode for VVC” proposed in JVET-P0300
  Improve the throughput for the use cases of high bitrate and low delay conditions

## Slide 9
Thank HHI for cross-checking!

## Slide 10: JVET-Q0347 + JVET-P0300(High Throughput mode): low QPs
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 8.95% | 7.14% | 8.11% | 103% | 91%
Class A2 | 7.46% | 7.78% | 7.97% | 92% | 87%
Class B | 8.27% | 8.45% | 9.59% | 97% | 96%
Class C | 6.83% | 7.00% | 7.61% | 88% | 97%
Class E | 6.84% | 7.29% | 9.07% | 91% | 95%
Overall | 7.69% | 7.60% | 8.55% | 94% | 94%
Class D | 6.17% | 6.06% | 6.49% | 87% | 97%
Class F | 8.27% | 6.62% | 7.17% | 94% | 97%
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 8.61% | 11.62% | 10.60% | 102% | 90%
Class C | 7.06% | 10.43% | 8.40% | 92% | 101%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 6.27% | 9.94% | 7.52% | 91% | 94%
Class F | 10.15% | 9.26% | 8.24% | 94% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 8.29% | 10.70% | 10.15% | 104% | 89%
Class C | 6.98% | 10.28% | 8.53% | 95% | 98%
Class E | 6.88% | 8.01% | 7.27% | 94% | 92%
Overall | 7.50% | 9.89% | 8.89% | 99% | 93%
Class D | 5.84% | 9.18% | 7.35% | 92% | 96%
Class F | 7.77% | 10.13% | 8.10% | 94% | 97%

## Slide 11: Reference JVET-P0300(High Throughput mode): low QPs
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 8.32% | 6.47% | 7.34% | 108% | 90%
Class A2 | 5.31% | 5.46% | 5.59% | 96% | 84%
Class B | 6.58% | 6.70% | 7.74% | 101% | 91%
Class C | 3.73% | 3.82% | 4.31% | 97% | 92%
Class E | 5.40% | 5.74% | 7.47% | 96% | 95%
Overall | 5.83% | 5.65% | 6.51% | 100% | 91%
Class D | 2.83% | 2.65% | 3.10% | 96% | 95%
Class F | 6.77% | 5.25% | 5.70% | 99% | 97%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 7.87% | 10.08% | 9.61% | 109% | 88%
Class C | 5.88% | 8.87% | 7.09% | 95% | 91%
Class E | 6.75% | 7.90% | 7.00% | 97% | 88%
Overall | 6.93% | 9.13% | 8.12% | 101% | 89%
Class D | 4.79% | 8.04% | 6.13% | 95% | 95%
Class F | 7.14% | 9.35% | 7.46% | 96% | 97%