## Slide 1: JVET-Q0350 (Non-CE: Enable CIIP for 4x8/8x4 block without SCIPU violation)
Hyeongmun Jang,
Junghak Nam, Naeri Park, Seung-hwan Kim, Jaehyun Lim
Notes: This is presentation for P0577, APS support for initial palette predictor entry.

## Slide 2: Summary
Propose to allow CIIP for 4x8/8x4 blocks without SCIPU violation.
Experiment result shows extra BD-rate saving without enc/dec complexity increment.
  0.02% and 0.03% BD-rate saving for RA and LDB respectively.
  BD-rate saving is shown relatively high for low resolution

## Slide 3: Motivation
4x8/8x4 CIIP prediction give extra BD-rate saving
In VVC draft6, If 4x8/8x4 CIIP is allowed,
  Corresponding chroma block size is 4x2 and 2x4.
  Due to the SCIPU constraint, it is not supported for small block CIIP.
In VVC draft7, If the corresponding chroma block violates SCIPU constraint,
  Chroma intra prediction is bypassed for CIIP decoding processing.
  Only inter prediction block is used for CIIP chroma component.
  But the constraint is not fully covered about SCIPU restriction for CIIP.
  Only 4x2 block is not covered.

## Slide 4: Proposed method
Support CIIP for 4x8/8x4 block.
  Remove minimum block size restriction for CIIP
  Describe SCIPU restriction to be fully covered including 4x2 block for CIIP chroma component

## Slide 5: Experimental result
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.05% | -0.03% | 100% | 99%
Class A2 | -0.01% | 0.01% | 0.02% | 100% | 100%
Class B | -0.02% | 0.10% | 0.15% | 100% | 98%
Class C | -0.06% | -0.08% | -0.03% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | 0.01% | 0.04% | 100% | 99%
Class D | -0.09% | -0.02% | -0.23% | 100% | 100%
Class F | -0.03% | 0.03% | -0.01% | 100% | 100%
Class SCC | -0.04% | -0.02% | -0.03% | 100% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.06% | -0.13% | 101% | 100%
Class C | -0.02% | -0.27% | -0.16% | 101% | 99%
Class E | -0.09% | 0.52% | 0.14% | 100% | 99%
Overall | -0.03% | 0.01% | -0.07% | 100% | 100%
Class D | -0.10% | -0.04% | -0.24% | 100% | 99%
Class F | 0.02% | -0.25% | 0.32% | 100% | 98%
Class SCC | -0.04% | -0.09% | -0.12% | 101% | 98%