## Slide 1: JVET-Q0350 (Non-CE: Enable CIIP for 4x8/8x4 block without SCIPU violation)
Hyeongmun Jang,
Junghak Nam, Naeri Park, Seung-hwan Kim, Jaehyun Lim
Notes: This is presentation for P0577, APS support for initial palette predictor entry.

## Slide 2: Summary
Propose to allow CIIP for 4x8/8x4 blocks.
Experiment result shows extra BD-rate saving
  0.02% and 0.03% BD-rate saving for RA and LDB respectively.
  BD-rate saving is shown relatively high for low resolution

## Slide 3: Motivation
4x8/8x4 CIIP prediction give extra BD-rate saving
  Coding gain from CIIP show relatively low in low resolution sequences.
  Average coding performance decrement by coding performance in low resolution
  Due to the CIIP “restriction on small block size” and “light” encoder design for CIIP.
  For now, any specific reason for CIIP block size restriction would not be catch
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.23% | 0.07% | 0.00% | 99% | 101%
Class A2 | 0.21% | -0.03% | 0.04% | 97% | 104%
Class B | 0.34% | 0.04% | -0.04% | 98% | 101%
Class C | 0.30% | -0.04% | 0.07% | 98% | 99%
Class E |  |  |  |  | 
Overall | 0.28% | 0.01% | 0.01% | 98% | 101%
Class D | 0.18% | -0.02% | -0.11% | 98% | 99%
Class F | 0.22% | 0.09% | 0.14% | 99% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.53% | 0.51% | 0.61% | 97% | 96%
Class C | 0.38% | 0.18% | 0.57% | 97% | 98%
Class E | 0.16% | 0.76% | 0.14% | 97% | 97%
Overall | 0.39% | 0.46% | 0.48% | 97% | 97%
Class D | 0.26% | 0.02% | 0.42% | 97% | 101%
Class F | 0.72% | 0.14% | 1.22% | 98% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.05% | -0.03% | 100% | 99%
Class A2 | -0.01% | 0.01% | 0.02% | 100% | 100%
Class B | -0.02% | 0.10% | 0.15% | 100% | 98%
Class C | -0.06% | -0.08% | -0.03% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | 0.01% | 0.04% | 100% | 99%
Class D | -0.09% | -0.02% | -0.23% | 100% | 100%
Class F | -0.03% | 0.03% | -0.01% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.06% | -0.13% | 101% | 100%
Class C | -0.02% | -0.27% | -0.16% | 101% | 99%
Class E | -0.09% | 0.52% | 0.14% | 100% | 99%
Overall | -0.03% | 0.01% | -0.07% | 100% | 100%
Class D | -0.10% | -0.04% | -0.24% | 100% | 99%
Class F | 0.02% | -0.25% | 0.32% | 100% | 98%
AhG13 CIIP tool off
Proposed benefit

## Slide 4: Proposed method
Support CIIP for 4x8/8x4 block.
  Remove minimum block size restriction for CIIP

## Slide 5: Experimental result
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.05% | -0.03% | 100% | 99%
Class A2 | -0.01% | 0.01% | 0.02% | 100% | 100%
Class B | -0.02% | 0.10% | 0.15% | 100% | 98%
Class C | -0.06% | -0.08% | -0.03% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.02% | 0.01% | 0.04% | 100% | 99%
Class D | -0.09% | -0.02% | -0.23% | 100% | 100%
Class F | -0.03% | 0.03% | -0.01% | 100% | 100%
Class SCC | -0.04% | -0.02% | -0.03% | 100% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.06% | -0.13% | 101% | 100%
Class C | -0.02% | -0.27% | -0.16% | 101% | 99%
Class E | -0.09% | 0.52% | 0.14% | 100% | 99%
Overall | -0.03% | 0.01% | -0.07% | 100% | 100%
Class D | -0.10% | -0.04% | -0.24% | 100% | 99%
Class F | 0.02% | -0.25% | 0.32% | 100% | 98%
Class SCC | -0.04% | -0.09% | -0.12% | 101% | 98%

## Slide 6: Proposed method decoding process
In VVC draft7, If the corresponding chroma block violates SCIPU constraint,
  Chroma intra prediction is bypassed for CIIP decoding processing.
  e.g., chroma block width < 4
  CIIP is allowed if chroma block < 16
Propose
  Chroma intra prediction is bypassed when Chroma block < 16