## Slide 1: JVET-Q0351 (Report on experimental result for fixing BDPCM Chroma mismatch)
Hyeongmun Jang,
Hendry, Junghak Nam, Seethal Paluri, Seung-hwan Kim, Jaehyun Lim
Notes: This is presentation for P0577, APS support for initial palette predictor entry.

## Slide 2: Summary
Report experiment result with fixing mistmatch between SW and SPEC regarding Chroma BDPCM.
Notes:   this proposal follows same sprit of HEVC’s scc extension.

## Slide 3: Problem statement
Context.
  In VVC draft7, separate contexts are used for BDPCM luma and chroma.
  In SW, BDPCM luma anc chroma share same context.
Syntax signaling order for single tree case.
  In VVC draft7, the BDPCM chroma syntax is transmitted after intra luma prediction mode syntax.
  In SW, the BDPCM chroma syntax is transmitted before intra luma prediction mode.
Notes:   this proposal follows same sprit of HEVC’s scc extension.

## Slide 4: Report
The experimental result for aligning SW to SPEC.
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
444 color format | -0.25% | -0.21% | -0.25% | 101% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
444 color format | -0.07% | 0.01% | -0.05% | 100% | 101%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
444 color format | -0.11% | -0.04% | 0.05% | 100% | 99%

## Slide 5: Individual experiment result
Individual experimental result (using separate context between luma & chroma for BDPCM)
  Address same issue which is reported JVET-Q0110 aspect2 (already adopted)
 | All Intra Main10 |  |  |  | 
 | Over VTM-7.0 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
444 color format | -0.02% | -0.07% | -0.05% | 100% | 99%
 | Random access Main10 |  |  |  | 
 | Over VTM-7.0 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
444 color format | 0.02% | 0.05% | 0.04% | 99% | 98%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 4:4:4 |  |  |  | 
 | Y | U | V | EncT | DecT
444 color format | -0.01% | -0.04% | 0.05% | 100% | 100%

## Slide 6: Individual experiment result
All Intra Main10 |  |  |  | 
Over VTM-7.0 4:4:4 |  |  |  | 
Y | U | V | EncT | DecT
-0.18% | -0.21% | -0.24% | 101% | 98%
Random access Main10 |  |  |  | 
Over VTM-7.0 4:4:4 |  |  |  | 
Y | U | V | EncT | DecT
-0.05% | -0.01% | -0.04% | 100% | 101%
Low delay B Main10 |  |  |  | 
Over VTM-7.0 4:4:4 |  |  |  | 
Y | U | V | EncT | DecT
-0.12% | 0.05% | 0.11% | 100% | 100%
Individual experimental result (fix parsing order for BDPCM chroma)