## Slide 1: JVET-Q0361 Cleanup of chroma BDPCM constraint
Fujitsu
17th JVET meeting, Brussels , 2020/1/7-17

## Slide 2: Introduction
Chroma BDPCM and PLT are merely enabled for 4:4:4 sequences.
For PLT, the chroma size is expressed using the chroma scaling factors.
For Chroma BDPCM, the luma block size is used in the constraint check.
...... | 
if( cbWidth <= MaxTsSize && cbHeight <= MaxTsSize && sps_bdpcm_chroma_enabled_flag ) { | 
intra_bdpcm_chroma_flag | ae(v)
if( intra_bdpcm_chroma_flag ) | 
intra_bdpcm_chroma_dir_flag | ae(v)
}...... | 
7.3.9.5 Coding unit syntax
…… | 
if( ( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_CHROMA ) && ChromaArrayType != 0 ) { | 
if( pred_mode_plt_flag && treeType = = DUAL_TREE_CHROMA ) | 
palette_coding( x0, y0, cbWidth / SubWidthC, cbHeight / SubHeightC, treeType ) | 
}…… | 

## Slide 3: Specification change
To add the chroma scaling factors in the condition for chroma BDPCM
7.3.9.5 Coding unit syntax | 
...... | 
if( cbWidth / SubWidthC <= MaxTsSize && cbHeight/ SubHeightC <= MaxTsSize && sps_bdpcm_chroma_enabled_flag ) { | 
intra_bdpcm_chroma_flag | ae(v)
if( intra_bdpcm_chroma_flag ) | 
intra_bdpcm_chroma_dir_flag | ae(v)
}...... | 

## Slide 4
Notes: 以上で発表を終わります。
ご清聴ありがとうございました。