## Slide 1: JVET-Q0369 Restricting MIP for ACT coded CUs
Fujitsu
17th JVET meeting, Brussels , 2020/1/7-17

## Slide 2: Summary
Two modifications are proposed:
  Aspect 1: to fix a bug in the software by skipping BDPCM signaling for Chroma when ACT is used
  Aspect 2: to disallow MIP for ACT

## Slide 3: On Aspect 1
Problem
  In spec, chroma BDPCM is not signalled when ACT is used
  In VTM7.1, chroma BDPCM will always be signalled no matter if ACT is used
Solution
  Align SW with the Draft 7

## Slide 4: On Aspect 2
Introduction
  In the single tree, MIP flag is signaled if the luma intra prediction mode is not PLT and BDPCM.
…… | descriptor
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA ¦ ¦ CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_PLT ) { | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( pred_mode_plt_flag ) | 
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) | 
else { | 
if( sps_bdpcm_enabled_flag && cbWidth <= MaxTsSize && cbHeight <= MaxTsSize ) | 
intra_bdpcm_luma_flag | ae(v)
if( intra_bdpcm_luma_flag ) | 
intra_bdpcm_luma_dir_flag | ae(v)
else { | 
if( sps_mip_enabled_flag ) | 
intra_mip_flag[ x0 ][ y0 ] | ae(v)
if( intra_mip_flag[ x0 ][ y0 ] ) { | 
intra_mip_transposed[ x0 ][ y0 ] | ae(v)
intra_mip_mode[ x0 ][ y0 ] | ae(v)
} else { | 
…… | 
} | 
} | 
} | 
7.3.9.5 Coding unit syntax

## Slide 5: On Aspect 2
  The hit rate of MIP is very small when ACT is applied
    Statistics of MIP hit rate with MIP flag(0 or 1) signaled
      from VTM7.1 with AI configuration
      Separate-tree is OFF
      IBC, PLT, luma BDPCM, chroma BDPCM, inter HashME and ACT enabled
 | ACT = 1 |  |  | ACT = 0 |  | 
 | MIP = 1 | MIP = 0 | Ratio of CU with MIP flag(0 or 1) signaled | MIP = 1 | MIP = 0 | Ratio of CU with MIP flag (0 or 1) signaled
RGB, text & graphics with motion, 1080p & 720p | 0.59% | 99.41% | 51.34% | 0.66% | 99.34% | 48.66%
RGB, mixed content, 1440p & 1080p | 0.43% | 99.57% | 84.35% | 0.39% | 99.61% | 15.65%
RGB, Animation, 720p | 1.51% | 98.49% | 89.95% | 1.73% | 98.27% | 10.05%
RGB, camera captured, 1080p | 2.65% | 97.35% | 90.83% | 4.53% | 95.47% | 9.17%
YUV, text & graphics with motion, 1080p & 720p | 3.72% | 96.28% | 0.07% | 4.30% | 95.70% | 99.93%
YUV, mixed content, 1440p & 1080p | 7.95% | 92.05% | 0.05% | 10.52% | 89.48% | 99.95%
YUV, Animation, 720p | 14.03% | 85.97% | 0.02% | 7.41% | 92.59% | 99.98%
YUV, camera captured, 1080p | 24.38% | 75.63% | 0.01% | 22.75% | 77.25% | 99.99%
Notes:       For RGB sequences, when ACT is applied, the ratio of CU with MIP flag signaled is much more than 50%, but the hit rate of MIP among them is less than 3%.
      For YUV sequences, when ACT is applied, although the hits of MIP is higher (3%~25%) , the ratio of CU with MIP flag signaled is very small (<1%).
      When ACT is not applied, MIP is applied by a large number of intra CUs for YUV sequences.

## Slide 6: On Aspect 2
Proposed method
  To disallow MIP for ACT to enhance the throughput
…… | 
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && sps_act_enabled_flag && treeType = = SINGLE_TREE ) | 
cu_act_enabled_flag | ae(v)
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA ¦ ¦ CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_PLT ) { | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( pred_mode_plt_flag ) | 
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) | 
else { | 
if( sps_bdpcm_enabled_flag && cbWidth <= MaxTsSize && cbHeight <= MaxTsSize ) | 
intra_bdpcm_luma_flag | ae(v)
if( intra_bdpcm_luma_flag ) | 
intra_bdpcm_luma_dir_flag | ae(v)
else { | 
if( sps_mip_enabled_flag && !cu_act_enable_flag ) | 
intra_mip_flag[ x0 ][ y0 ] | ae(v)
if( intra_mip_flag[ x0 ][ y0 ] ) { | 
intra_mip_transposed[ x0 ][ y0 ] | ae(v)
intra_mip_mode[ x0 ][ y0 ] | ae(v)
}…… | 
…… | 
7.3.9.5 Coding unit syntax

## Slide 7: Simulation results
    Anchor: VTM-7.1
Thank NHK for crosschecking!
Aspect 1+2 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.06% | -0.02% | 0.03%
RGB, mixed content, 1440p & 1080p | -0.04% | -0.04% | -0.01%
RGB, Animation, 720p | -0.08% | 0.05% | -0.01%
RGB, camera captured, 1080p | 0.02% | -0.06% | -0.03%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.00% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.00% | 0.06% | 0.03%
YUV, Animation, 720p | -0.01% | -0.02% | 0.01%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.01%
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 
Aspect 1+2 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.04% | 0.00% | 0.02%
RGB, mixed content, 1440p & 1080p | -0.01% | -0.05% | -0.05%
RGB, Animation, 720p | -0.10% | 0.00% | -0.02%
RGB, camera captured, 1080p | 0.15% | 0.02% | 0.05%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | -0.01% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.05% | 0.10% | 0.10%
YUV, Animation, 720p | -0.02% | 0.01% | 0.03%
YUV, camera captured, 1080p | 0.02% | 0.04% | -0.06%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Aspect 1 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.04% | -0.03% | -0.02%
RGB, mixed content, 1440p & 1080p | -0.06% | -0.04% | -0.03%
RGB, Animation, 720p | -0.01% | 0.02% | -0.04%
RGB, camera captured, 1080p | -0.02% | -0.02% | -0.01%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | -0.01% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.00% | 0.02% | 0.02%
YUV, Animation, 720p | 0.00% | 0.00% | 0.00%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Aspect 1 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.00% | -0.01% | -0.02%
RGB, mixed content, 1440p & 1080p | -0.02% | -0.02% | -0.03%
RGB, Animation, 720p | -0.04% | 0.00% | -0.02%
RGB, camera captured, 1080p | 0.04% | 0.00% | 0.06%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.01% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.02% | 0.01% | 0.02%
YUV, Animation, 720p | 0.00% | 0.00% | -0.02%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 

## Slide 8
Notes: 以上で発表を終わります。
ご清聴ありがとうございました。