## Slide 1: JVET-Q0369 Restricting MIP for ACT coded CUs
Fujitsu
17th JVET meeting, Brussels , 2020/1/7-17

## Slide 2: Summary
Two modifications are proposed:
  Aspect 1: to fix a bug in the software by skipping BDPCM signaling for Chroma when ACT is used
  Aspect 2: to disallow MIP for ACT

## Slide 3: On Aspect 1
Problem
  In spec, chroma BDPCM is not signalled when ACT is used
  In VTM7.1, chroma BDPCM will always be signalled no matter if ACT is used
Solution
  Align SW with the Draft 7

## Slide 4: On Aspect 2
Introduction
  In the single tree, MIP flag is signaled if the luma intra prediction mode is not PLT and BDPCM.
…… | descriptor
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA ¦ ¦ CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_PLT ) { | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( pred_mode_plt_flag ) | 
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) | 
else { | 
if( sps_bdpcm_enabled_flag && cbWidth <= MaxTsSize && cbHeight <= MaxTsSize ) | 
intra_bdpcm_luma_flag | ae(v)
if( intra_bdpcm_luma_flag ) | 
intra_bdpcm_luma_dir_flag | ae(v)
else { | 
if( sps_mip_enabled_flag ) | 
intra_mip_flag[ x0 ][ y0 ] | ae(v)
if( intra_mip_flag[ x0 ][ y0 ] ) { | 
intra_mip_transposed[ x0 ][ y0 ] | ae(v)
intra_mip_mode[ x0 ][ y0 ] | ae(v)
} else { | 
…… | 
} | 
} | 
} | 
7.3.9.5 Coding unit syntax

## Slide 5: On Aspect 2
  The hit rate of MIP is very small when ACT is applied
    Statistics of MIP hit rate with MIP flag(0 or 1) signaled
      from VTM7.1 with AI configuration
      Separate-tree is OFF
      IBC, PLT, luma BDPCM, chroma BDPCM, inter HashME and ACT enabled
 | ACT = 1 |  |  | ACT = 0 |  | 
 | MIP = 1 | MIP = 0 | Ratio of CU with MIP flag(0 or 1) signaled | MIP = 1 | MIP = 0 | Ratio of CU with MIP flag (0 or 1) signaled
RGB, text & graphics with motion, 1080p & 720p | 0.59% | 99.41% | 51.34% | 0.66% | 99.34% | 48.66%
RGB, mixed content, 1440p & 1080p | 0.43% | 99.57% | 84.35% | 0.39% | 99.61% | 15.65%
RGB, Animation, 720p | 1.51% | 98.49% | 89.95% | 1.73% | 98.27% | 10.05%
RGB, camera captured, 1080p | 2.65% | 97.35% | 90.83% | 4.53% | 95.47% | 9.17%
YUV, text & graphics with motion, 1080p & 720p | 3.72% | 96.28% | 0.07% | 4.30% | 95.70% | 99.93%
YUV, mixed content, 1440p & 1080p | 7.95% | 92.05% | 0.05% | 10.52% | 89.48% | 99.95%
YUV, Animation, 720p | 14.03% | 85.97% | 0.02% | 7.41% | 92.59% | 99.98%
YUV, camera captured, 1080p | 24.38% | 75.63% | 0.01% | 22.75% | 77.25% | 99.99%
Notes:       Made the statistics of the cases that MIP flag is signaled for an intra CU
      For RGB sequences, the ratio of CU with ACT applied much more than 50% among them.
      In the cases that ACT is applied, the hit rate of MIP is less than 3%.
      For YUV sequences, the ratio of CU with ACT is applied is quite small although the hits of MIP is higher.

## Slide 6: On Aspect 2
Proposed method
  To disallow MIP for ACT to enhance the throughput
…… | 
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA && sps_act_enabled_flag && treeType = = SINGLE_TREE ) | 
cu_act_enabled_flag | ae(v)
if( CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_INTRA ¦ ¦ CuPredMode[ chType ][ x0 ][ y0 ] = = MODE_PLT ) { | 
if( treeType = = SINGLE_TREE ¦ ¦ treeType = = DUAL_TREE_LUMA ) { | 
if( pred_mode_plt_flag ) | 
palette_coding( x0, y0, cbWidth, cbHeight, treeType ) | 
else { | 
if( sps_bdpcm_enabled_flag && cbWidth <= MaxTsSize && cbHeight <= MaxTsSize ) | 
intra_bdpcm_luma_flag | ae(v)
if( intra_bdpcm_luma_flag ) | 
intra_bdpcm_luma_dir_flag | ae(v)
else { | 
if( sps_mip_enabled_flag && !cu_act_enable_flag ) | 
intra_mip_flag[ x0 ][ y0 ] | ae(v)
if( intra_mip_flag[ x0 ][ y0 ] ) { | 
intra_mip_transposed[ x0 ][ y0 ] | ae(v)
intra_mip_mode[ x0 ][ y0 ] | ae(v)
}…… | 
…… | 
7.3.9.5 Coding unit syntax

## Slide 7: Simulation results over VTM.7.1
Thanks NHK for crosschecking!
Aspect 1+2 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.06% | -0.02% | 0.03%
RGB, mixed content, 1440p & 1080p | -0.04% | -0.04% | -0.01%
RGB, Animation, 720p | -0.08% | 0.05% | -0.01%
RGB, camera captured, 1080p | 0.02% | -0.06% | -0.03%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.00% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.00% | 0.06% | 0.03%
YUV, Animation, 720p | -0.01% | -0.02% | 0.01%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.01%
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 
Aspect 1+2 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.04% | 0.00% | 0.02%
RGB, mixed content, 1440p & 1080p | -0.01% | -0.05% | -0.05%
RGB, Animation, 720p | -0.10% | 0.00% | -0.02%
RGB, camera captured, 1080p | 0.15% | 0.02% | 0.05%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | -0.01% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.05% | 0.10% | 0.10%
YUV, Animation, 720p | -0.02% | 0.01% | 0.03%
YUV, camera captured, 1080p | 0.02% | 0.04% | -0.06%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Aspect 1 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.04% | -0.03% | -0.02%
RGB, mixed content, 1440p & 1080p | -0.06% | -0.04% | -0.03%
RGB, Animation, 720p | -0.01% | 0.02% | -0.04%
RGB, camera captured, 1080p | -0.02% | -0.02% | -0.01%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | -0.01% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.00% | 0.02% | 0.02%
YUV, Animation, 720p | 0.00% | 0.00% | 0.00%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Aspect 1 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.00% | -0.01% | -0.02%
RGB, mixed content, 1440p & 1080p | -0.02% | -0.02% | -0.03%
RGB, Animation, 720p | -0.04% | 0.00% | -0.02%
RGB, camera captured, 1080p | 0.04% | 0.00% | 0.06%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.01% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.02% | 0.01% | 0.02%
YUV, Animation, 720p | 0.00% | 0.00% | -0.02%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.00%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
    Aspect 1
    RGB: {-0.03%, -0.02%, -0.03%} for AI
    RGB: {-0.01%, -0.01%, 0.00%} for RA
    YUV: {0.00%, 0.00%, 0.01%} for AI
    YUV: {0.00%, 0.00%, 0.00%} for RA
    Aspect 1+2
    RGB: {-0.04%, -0.02%, 0.00%} for AI
    RGB: {0.02%, 0.00 %, 0.01 %}for RA
    YUV: {0.02%, -0.01%, 0.00%}for AI
    YUV: {0.01%, 0.03%, 0.02%}for RA

## Slide 8: Simulation results over Aspect 1
Aspect 1+2 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.02% | 0.01% | 0.05%
RGB, mixed content, 1440p & 1080p | 0.02% | 0.00% | 0.03%
RGB, Animation, 720p | -0.07% | 0.02% | 0.04%
RGB, camera captured, 1080p | 0.04% | -0.04% | -0.02%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | 0.00% | 0.00%
YUV, mixed content, 1440p & 1080p | 0.01% | 0.04% | 0.01%
YUV, Animation, 720p | -0.01% | -0.02% | 0.01%
YUV, camera captured, 1080p | 0.00% | 0.00% | 0.01%
Enc Time[%] | 98% |  | 
Dec Time[%] | 100% |  | 
Aspect 1+2 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.05% | 0.01% | 0.05%
RGB, mixed content, 1440p & 1080p | 0.01% | -0.03% | -0.02%
RGB, Animation, 720p | -0.07% | -0.01% | 0.01%
RGB, camera captured, 1080p | 0.11% | 0.02% | -0.02%
YUV, text & graphics with motion, 1080p & 720p | 0.00% | -0.02% | -0.01%
YUV, mixed content, 1440p & 1080p | 0.04% | 0.09% | 0.08%
YUV, Animation, 720p | -0.02% | 0.01% | 0.06%
YUV, camera captured, 1080p | 0.02% | 0.04% | -0.06%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
    Aspect 1+2
    RGB: {-0.01%, 0.00%, 0.02%} for AI
    RGB: {0.02%, 0.00 %, 0.01 %}for RA
    YUV: {0.00%, 0.00%, 0.00%}for AI
    YUV: {0.01%, 0.03%, 0.02%}for RA
Thanks NHK for crosschecking!