## Slide 1: AHG15: Clean up for signaling quantization matrix
Ling Li, H. Zhang, X. Li, S. Liu

## Slide 2: Existing in VVC
Use 1D quantization matrix
Signal QM from id 0 to 27
No default QM
id=0 is the first id in base size 2x2
id=2 is the first id in base size 4x4
id=8 is the first id in base size 8x8
For id equals to 0, 2, 8, id_delta is not signaled
id | 0~1 | 2~7 | 8~27
 | Base size 2x2 | Base size 4x4 | Base size 8x8
Figure is from adopted JVET-P1034-v1
1
1
0
id_delta
id_delta
copy_flag
res DPCM
direct DPCM
pred_flag
0

## Slide 3: Proposed Method
Only for id equals to 0, 2, 8
Proposed method VVC
It is noticed that, QMs rarely have all value as 16
To simplify the process, it is proposed not to signal copy_flag when id equals to 0, 2, 8.
1
1
0
infer id_delta as 0
infer id_delta as 0
copy_flag
res DPCM
direct DPCM
pred_flag
0
1
infer id_delta as 0
res DPCM
direct DPCM
pred_flag
0

## Slide 4: Test sets
Use QM test sets provided in JVET-P0110
For id=0,2,8, only 1 QM has all 16 value

## Slide 5: Thank You

## Slide 6: Existing in VVC
Grey rows for when id=0, 2, 8
copy_flag | pred_flag | id_delta | ScalingMatrixPred | ScalingMatrixDCPred | 
0 | 0 | Inferred 0 | 8 | 8 | direct DPCM
0 | 1 | Inferred/Parsed 0 | 16 | 16 | Residual DPCM
0 | 1 | Not 0 | ScalingMatrixRec[ refId ] | ScalingMatrixDCPred | Residual DPCM
1 | 0 | Inferred/Parsed 0 | 16 | 16 | -
1 | 0 | Not 0 | ScalingMatrixRec[ refId ] | ScalingMatrixDCPred | -