## Slide 1: CE3-related: Modified Rice Parameter Derivation for TS Blocks
JVET-Q0439
Advanced Technology Team
European Professional Engineering
Sony Europe BV.
Karl Sharman / Steve Keating
Sony Corp.

## Slide 2: Introduction
In CE3-1.1c the Rice parameter for TS blocks is derived from the sum of two previous coefficients:

## Slide 3: Proposal
Performance can be improved by using 2*MAX instead of the sum:
Some additional gain can be obtained by using two previous coefficients in the top row and left column, e.g.:
A negligible additional gain can be obtained by leaving the default of 1 for the top left sample (instead of changing to 0, as in CE3-1.1c)
CE3-1.1c
Proposal

## Slide 4: Results
Lossless low QP CTC
Proposal
CE3-1.1c

## Slide 5: Conclusion
By changing an adder to a max function the performance of CE3-1.1c can be improved
Using two coefficients in the top row and left column gives some additional gain
Leaving the default as 1 gives a minor additional gain.

## Slide 6: Additional results
Breakdown of lossless results (all intra)
Method: | CE3-1.1c | + Changing sum to 2*Max | + Changing to using two samples on top row and left column | + Using default of 1 for top left position
Class A1 | -4.45% | -5.16% | -5.54% | -5.59%
Class A2 | -8.73% | -9.88% | -10.51% | -10.72%
Class B | -3.72% | -4.04% | -4.18% | -4.18%
Class C | -4.93% | -5.18% | -5.30% | -5.29%
Class E | -4.60% | -4.34% | -4.28% | -4.23%
Overall | -5.09% | -5.50% | -5.73% | -5.76%
Class D | -5.54% | -5.88% | -6.00% | -6.01%
Class F | -5.14% | -5.30% | -5.30% | -5.30%
Class TGM | -8.12% | -8.82% | -9.01% | -9.13%