## Slide 1: JVET-Q0455: On CU-level BDOF enable condition
Shuai Wan, Yi Xue , Junyan Huo,
Yanzhuo Ma，Fuzheng Yang,
Yuanfang Yu, Yang Liu
January. 2020

## Slide 2: Proposed Modification
BDOF off, when
(sign(mvL0[ xSbIdx ][ ySbIdx ][0]) * sign(mvL1[ xSbIdx ][ ySbIdx ][0]) >0)
& (sign(mvL0[ xSbIdx ][ ySbIdx ][1]) * sign(mvL1[ xSbIdx ][ ySbIdx ][1]) >0)
Reference picture in L0
Reference picture in L1
Current picture
MV0
MV1
BDOF off

## Slide 3: Proposed Modification
  MotionModelIdc[ xCb ][ yCb ] is equal to 0.
  merge_subblock_flag[ xCb ][ yCb ] is equal to 0.
  sym_mvd_flag[ xCb ][ yCb ] is equal to 0.
  ciip_flag[ xCb ][ yCb ] is equal to 0.
  BcwIdx[ xCb ][ yCb ] is equal to 0.
  luma_weight_l0_flag[ refIdxL0 ] and luma_weight_l1_flag[ refIdxL1 ] are both equal to 0.
  cbWidth is greater than or equal to 8.
  cbHeight is greater than or equal to 8.
  cbHeight * cbWidth is greater than or equal to 128.
  RefPicIsScaled[ 0 ][ refIdxL0 ] is equal to 0 and RefPicIsScaled[ 1 ][ refIdxL1 ] is equal to 0.
  cIdx is equal to 0.
Otherwise, bdofFlag is set equal to FALSE.
sign(mvL0[ xSbIdx ][ ySbIdx ][0]) * sign(mvL1[ xSbIdx ][ ySbIdx ][0]) is not larger than 0 or sign(mvL0[ xSbIdx ][ ySbIdx ][1]) * sign(mvL1[ xSbIdx ][ ySbIdx ][1]) is not larger than 0.
If all of the following conditions are true, bdofFlag is set equal to TRUE.
  pic_disable_bdof_flag is equal to 0.
  predFlagL0[ xSbIdx ][ ySbIdx ] and predFlagL1[ xSbIdx ][ ySbIdx ] are both equal to 1.
  DiffPicOrderCnt( currPic, RefPicList[ 0 ][ refIdxL0 ] ) is equal to DiffPicOrderCnt( RefPicList[ 1 ][ refIdxL1 ], currPic).
  RefPicList[ 0 ][ refIdxL0 ] is a short-term reference picture and RefPicList[ 1 ][ refIdxL1 ] is a short-term reference picture.
Suggested changes to working draft

## Slide 4: Experimental results
 |  |  | Random Access |  | 
 |  |  | Over VTM-7.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.02% | -0.01% | 99.6% | 99.6%
Class A2 | 0.00% | 0.00% | -0.01% | 100.6% | 100.0%
Class B | 0.00% | 0.02% | 0.03% | 99.8% | 100.0%
Class C | 0.01% | -0.03% | 0.02% | 100.0% | 99.8%
Class E |  |  |  |  | 
Overall | 0.00% | -0.01% | 0.01% | 100.0% | 99.9%
Class D | 0.00% | -0.01% | 0.01% | 99.8% | 98.8%
Class F | -0.01% | -0.02% | -0.04% | 99.6% | 99.6%
BDOF is off in the LDB configuration.

## Slide 5: Conclusion
BDOF enable restriction by utilizing the sign of forward and backward motion vectors.
A small reduced decoding time.
No coding efficiency loss.
Recommend to adopt into VVC.
Thanks crosschecking by Alibaba

## Slide 6
Thank you