## Slide 1: Non-CE3 Inter BDPCM for lossless video coding
Gosala Kulupana, and Saverio Blasi
17th Meeting: Brussels, BE, 7–17 Jan. 2020
JVET-Q0460

## Slide 2
General idea
This contribution proposes to apply BDPCM on inter-predicted residuals for lossless coding (similar to HEVC-Rext).
Identically to intra BDPCM, the proposed inter BDPCM works on quantized residuals.
Therefore, the tool re-uses entirely the residual prediction operations used in the intra BDPCM pipeline.
Shares the same BDPCM flag used in intra blocks to signal usage of BDPCM for inter-coded blocks. In case BDPCM is used, an additional flag is used to signal the BDPCM prediction direction.

## Slide 3
Performance results
 | Random Access |  |  | Low Delay B |  | 
 | Compression Ratio |  | Bit-rate savings | Compression Ratio |  | bit-rate savings
 | VTM-7.0 with intra BDPCM=0 | inter BDPCM |  | VTM-7.0 with intra BDPCM=0 | inter BDPCM | 
Class A1 | 2.2 | 2.2 | -0.22% |  |  | 
Class A2 | 1.7 | 1.7 | -1.96% |  |  | 
Class B | 2.3 | 2.4 | -0.88% | 2.3 | 2.4 | -1.04%
Class C | 2.4 | 2.5 | -0.87% | 2.4 | 2.4 | -1.00%
Class D | 2.8 | 2.8 | -1.27% | 2.7 | 2.8 | -1.52%
Class E |  |  |  | 3.1 | 3.2 | -1.82%
Class F | 33.7 | 34.4 | -1.96% | 50.7 | 51.7 | -2.30%
TGM | 107.1 | 107.7 | -0.83% | 124.9 | 126.2 | -1.19%
Overall | 2.2 | 2.2 | -0.96% | 2.6 | 2.6 | -1.22%
Enc Time[%] | 110% |  |  | 112% |  | 
Dec Time[%] | 98% |  |  | 97% |  | 
Table 1 - Performance of inter BDPCM compared to VTM-7.0.

## Slide 4
Performance results
 | Random Access |  |  | Low Delay B |  | 
 | Compression Ratio |  | Bit-rate savings | Compression Ratio |  | bit-rate savings
 | VTM-7.0 | inter and intra BDPCM |  | VTM-7.0 | inter and intra BDPCM | 
Class A1 | 2.2 | 2.3 | -0.54% |  |  | 
Class A2 | 1.7 | 1.7 | -2.09% |  |  | 
Class B | 2.3 | 2.4 | -1.13% | 2.3 | 2.4 | -1.28%
Class C | 2.4 | 2.5 | -1.19% | 2.4 | 2.5 | -1.30%
Class D | 2.8 | 2.8 | -1.61% | 2.7 | 2.8 | -1.70%
Class E |  |  |  | 3.1 | 3.2 | -2.50%
Class F | 34.6 | 35.1 | -1.73% | 51.6 | 52.4 | -2.06%
TGM | 108.1 | 108.7 | -0.73% | 126.2 | 127.4 | -1.16%
Overall | 2.2 | 2.2 | -1.22% | 2.6 | 2.6 | -1.59%
Enc Time[%] | 114% |  |  | 114% |  | 
Dec Time[%] | 98% |  |  | 98% |  | 
Table 2 - Performance of inter and intra BDPCM compared to VTM-7.0.

## Slide 5
Performance results
 | Random Access |  |  | Low Delay B |  | 
 | Compression Ratio |  | Bit-rate savings | Compression Ratio |  | bit-rate savings
 | VTM-7.0 with intra BDPCM = 1 | inter and intra BDPCM |  | VTM-7.0 with intra BDPCM = 1 | inter and intra BDPCM | 
Class A1 | 2.3 | 2.3 | -0.15% |  |  | 
Class A2 | 1.7 | 1.7 | -1.75% |  |  | 
Class B | 2.4 | 2.4 | -0.59% | 2.4 | 2.4 | -0.70%
Class C | 2.4 | 2.5 | -0.68% | 2.4 | 2.5 | -0.76%
Class D | 2.8 | 2.8 | -1.04% | 2.8 | 2.8 | -1.25%
Class E |  |  |  | 3.2 | 3.2 | -1.27%
Class F | 34.6 | 35.1 | -1.73% | 51.6 | 52.4 | -2.06%
TGM | 108.1 | 108.7 | -0.73% | 126.2 | 127.4 | -1.16%
Overall | 2.2 | 2.2 | -0.76% | 2.6 | 2.6 | -0.86%
Enc Time[%] | 111% |  |  | 110% |  | 
Dec Time[%] | 99% |  |  | 99% |  | 
Table 3 - Performance of inter and intra BDPCM compared to VTM-7.0 with intra BDPCM always set.

## Slide 6
Conclusion
Inter BDPCM is proposed for lossless video coding
-0.96% bit rate saving is obtained for 110% encoder run-time compared to VTM-7.0 lossless anchor.
-1.22% bit rate saving is obtained when both inter and intra BDPCM is used, for 114% encoder run-time compared to VTM-7.0 lossless anchor.

## Slide 7: Thank you
www.bbc.co.uk/rd
gosala.kulupana@bbc.co.uk
Email: