## Slide 1: JVET-Q0506 Interaction between ACT and cross-component coding tools
H. Zhang, X. Li, L. Li, G. Li, S. Liu
2020/1

## Slide 2: Introduction
Coding tool Inter-component residuals
  ACT performs the color space conversion (YCgCo) in the residue domain.
  JCCR follows ACT, and jointly encode the two converted chroma channel residuals.
Overlap Problem
  JCCR has limited performance when ACT is on.
  Increase residual reconstruction delay if both of JCCR and ACT are used.

## Slide 3: Proposed Method
Not to enable JCCR for the ACT coded CUs.

## Slide 4: Simulation Results
Anchor: VTM-7.1

## Slide 5: Conclusion
Overlap exists between JCCR and ACT
Proposed performance impact on time/bdrate
  YUV,
    AI 2% dec. 1% enc. time saving with 0.00%/0.01%/0.00%.
    RA 1% dec. time saving with 0.03%/0.03%/0.02%.
  RGB,
    AI 6% enc. 2% dec. time saving with 0.11%0.15%/0.08%.
    RA 5% enc. 1% dec. time saving with 0.19%/0.18%/0.04%.
Increase residual reconstruction delay if both of JCCR and ACT are used.
Thanks to ByteDance for crosschecking!

## Slide 6
Thank you!

## Slide 7: Supplement data

## Slide 8: Noted
The second version of this document updated the quality data of sequence “Kimono1_1920x1080_24_10bit_444” that 600 frames have been encoded (instead of 300 frames in the data in first version) and increased the precision of encoding and decoding time.
Q0305 test 1 more sequence, “ChineseEditing_1920x1080_60_444” for RGB and YUV. Therefore, the results of categories “RGB, text & graphics with motion, 1080p & 720p” and “YUV, text & graphics with motion, 1080p & 720p” has a very little different with us.