## Slide 1
JVET-Q0123
Ce4-related: Modifications for GEO
Li Jingya, Lim Chong Soon

## Slide 2
Introduction
Geometrical partitioning (GEO)
JVET-J1030/JVET-K0146 which applied to both AMVP and merge mode.
JVET-O0489, GEO was proposed for merge mode with 140 supported partitioning modes and 19 supported block size (8x8 to 128x128).
JVET-P0884/0885, efforts were made to remove multiplication of weight mask calculation and number of modes was reduced to 82.
JVET-Q0059, number of modes is further reduced to 64.
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
Wedge mode (in other standard) | 144 | 16 | 8
GEO (JVET-O0489, Gothenburg) | 2,660 | 140 | 19
GEO (JVET-P0884/JVET-Q0079, CE4 common base, Geneva) | 1,558 | 82 | 19
GEO (JVET-Q0059, CE4-1, Brussels) | 1,216 | 64 | 19

## Slide 3
Proposal
Scalable geo by signaling number of valid modes in SPS
Encoder is allowed to choose either 16 valid geo modes or 64 valid geo modes.
A flag is signaled in SPS level to switch between 16 and 64 modes.
If 16 mode is selected, only the first 16 modes of GEO mode table are valid.
If 64 mode is selected, all 64 modes of GEO mode table are valid.
(This affects coding of merge_geo_parititon_idx with cmax set to 16 and 64 respectively)
 | Total # of cases | # modes per block size | # of supported block sizes
TPM | 50 | 2 | 25
GEO (JVET-Q0059, CE4-1) | 1,216 | 64 | 19
Proposal (64 mode) | Same as above | Same as above | Same as above
Proposal (16 mode) | 304 | 16 | 19

## Slide 4
Simulation results
Anchor: VTM7.0
Test: Left - scalable coding with 16 valid modes; Right – scalable coding with 64 valid modes. (implemented over CE4-1, GEO mode table is reordered according to statistics)
 | Random Access Main 10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.09% | 0.00% | 102% | 101%
Class A2 | -0.06% | 0.04% | 0.05% | 101% | 100%
Class B | -0.06% | 0.03% | -0.04% | 101% | 101%
Class C | -0.21% | -0.34% | -0.28% | 101% | 100%
Class E |  |  |  |  | 
Overall | -0.09% | -0.09% | -0.08% | 101% | 100%
Class D | -0.16% | -0.32% | -0.25% | 101% | 100%
Class F | -0.22% | -0.21% | -0.19% | 100% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-7.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.16% | -0.28% | -0.17% | 101% | 100%
Class C | -0.25% | -0.42% | -0.09% | 101% | 99%
Class E | -0.52% | 0.22% | -0.38% | 99% | 99%
Overall | -0.28% | -0.20% | -0.20% | 100% | 99%
Class D | -0.33% | 0.12% | -0.53% | 100% | 100%
Class F | -0.34% | -0.49% | 0.01% | 100% | 100%
Random Access Main 10 |  |  |  | 
Over VTM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.13% | -0.20% | -0.18% | 103% | 101%
-0.19% | -0.14% | -0.02% | 103% | 100%
-0.14% | -0.11% | -0.09% | 102% | 100%
-0.61% | -0.97% | -0.86% | 102% | 100%
-0.28% | -0.36% | -0.30% | 102% | 100%
-0.41% | -0.64% | -0.52% | 102% | 100%
-0.33% | -0.34% | -0.35% | 101% | 100%
Low delay B Main10 |  |  |  | 
Over VTM-7.0 |  |  |  | 
Y | U | V | EncT | DecT
-0.32% | -0.44% | -0.26% | 103% | 100%
-0.81% | -1.15% | -0.96% | 103% | 99%
-1.18% | -0.21% | -0.77% | 101% | 99%
-0.70% | -0.62% | -0.62% | 102% | 99%
-0.68% | -0.56% | -0.76% | 102% | 99%
-0.53% | -0.75% | 0.05% | 102% | 99%

## Slide 5
Simulation results (additional information)
8 valid modes 32 valid modes 48 valid modes
 | Random Access Main 10 |  | 
 | Over VTM-7.0 |  | 
 | Y | U | V
Class A1 | 0.09% | 0.18% | 0.21%
Class A2 | 0.03% | 0.17% | 0.23%
Class B | 0.06% | 0.21% | 0.13%
Class C | 0.06% | 0.15% | 0.13%
Class E |  |  | 
Overall | 0.06% | 0.18% | 0.16%
Class D | -0.03% | -0.01% | 0.00%
Class F | -0.11% | -0.03% | -0.08%
 | Low delay B Main10 |  | 
 | Over VTM-7.0 |  | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | 0.09% | -0.09% | 0.26%
Class C | 0.18% | 0.09% | 0.40%
Class E | -0.14% | 0.57% | 0.08%
Overall | 0.06% | 0.14% | 0.26%
Class D | 0.00% | 0.32% | 0.48%
Class F | -0.03% | -0.47% | 0.43%
Random Access Main 10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.10% | -0.19% | -0.07%
-0.13% | -0.12% | 0.02%
-0.12% | -0.08% | -0.11%
-0.41% | -0.60% | -0.53%
-0.19% | -0.25% | -0.19%
-0.31% | -0.46% | -0.52%
-0.29% | -0.32% | -0.27%
Low delay B Main10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.29% | -0.34% | -0.17%
-0.59% | -0.80% | -0.48%
-0.84% | -0.24% | -0.49%
-0.53% | -0.47% | -0.35%
-0.54% | -0.46% | -0.64%
-0.41% | -1.17% | -0.22%
Random Access Main 10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.11% | -0.15% | -0.18%
-0.17% | -0.07% | 0.02%
-0.15% | -0.11% | -0.10%
-0.55% | -0.79% | -0.74%
-0.25% | -0.29% | -0.27%
-0.41% | -0.53% | -0.60%
-0.33% | -0.36% | -0.29%
Low delay B Main10 |  | 
Over VTM-7.0 |  | 
Y | U | V
-0.37% | -0.54% | -0.43%
-0.76% | -1.14% | -0.81%
-0.93% | -0.30% | -1.11%
-0.64% | -0.68% | -0.73%
-0.64% | -0.42% | -0.44%
-0.51% | -1.04% | -0.09%

## Slide 6
Mode number-BD curve (LDB) (additional information)
Chart: # of modes - coding impact curve (LDB)
| 8 | 16 | 32 | 48 | 64
 | 0.0006 | -0.0028 | -0.0053 | -0.0064 | -0.007

## Slide 7
Other tests (additional information)
Encoder uses only first 16 modes (cmax of merge_geo_parititon_idx = 64, w/o mode table reordering, implemented on CE4-1)
RA (YCbCr): 0.19%, 0.30%, 0.30%
LDB(YCbCr): 0.44%, 0.62%, 0.69%
Encoder uses only first 16 modes (cmax of merge_geo_parititon_idx = 16, w/o mode table reordering, implemented on CE4-1)
RA (YCbCr): 0.04%, 0.06%, 0.14%
LDB(YCbCr): 0.07%, 0.31%, 0.47%
Encoder uses only first 16 modes (cmax of merge_geo_parititon_idx = 16, with mode table reordering, implemented on CE4-1)
RA (YCbCr): -0.09%, -0.09%, -0.08%
LDB(YCbCr): -0.28%, -0.20%, -0.20%
It can be observed that both signaling max value of cmax of merge_geo_partition_idx and geo mode table reordering contribute to coding efficiency.

## Slide 8
8
Conclusion
This contribution proposes scalable number of modes of GEO to address the issue regarding hardware validation checks for encoder. A SPS switch is used to switch between 16 and 64 modes.
16 modes (anchor VTM7.0): -0.09% (RA) and -0.28% (LDB)
  64 modes (anchor VTM7.0): -0.28% (RA) and -0.70% (LDB)

## Slide 9
9
Thank Bytedance for cross-check