## Slide 1
JVET-P0510
ACT colour conversion for both lossless and lossy coding
Xiaoyu Xiu, Yi-Wen Chen, Tsung-chuan Ma, Hong-Jheng Jhu, Xianglin Wang (Kwai)
Jie Zhao, Hendry, Seethal Paluri, Seung Hwan Kim (LGE)
Weijia Zhu, Jizheng Xu, Li, Zhang (Bytedance)

## Slide 2
Summary of proposal
Proposal
  It is proposed to use reversible YCgCo colour transform (a.k.a. YCgCo-R) for both lossy and lossless coding.
  It is proposed to signal ACT QP offsets in bitstream, instead of using fixed ACT QP offsets.
  ACT QP clipping to valid QP range of TS and non-TS modes (as proposed in JVET-Q0511)
  Performance
  For lossless coding, bitrate differences of -2.35% for AI, -4.86% for RA and -6.04% for LD for RGB test sequences.
  For lossy coding, average {G, B, R} BD-rate differences of {-0.16%, -0.08%, -0.10%} for AI, {-0.02%, 0.01%, -0.09%} for RA, and {-0.29%,0.01%, -0.31%} for LD for RGB test sequences.

## Slide 3
YCgCo-R conversion
Color space conversion in VVC draft 7
  The YCgCo conversion is irreversible
  QP adjustments are (-5, -5, -3)
Proposal
  Use YCgCo-R conversion for both lossy and lossless coding
  QP adjustments become (-5, 1, 3)
  Clip the QP values of ACT to valid dynamic range of non-TS and TS
  Enable chroma TS for ACT (encoder-only)

## Slide 4
ACT QP offset signaling
It is proposed to signal the ACT QP offset in PPS
  It is needed to support the lossless coding of the ACT mode
  It provides more flexibilities to encoder for adjusting the QPs applied to ACT CUs
pic_parameter_set_rbsp( ) { | Descriptor
…… | 
pps_act_qp_offsets_present_flag | u(1)
if (pps_act_qp_offsets_present_flag) { | 
pps_act_y_qp_offset_plus5 | se(v)
pps_act_cb_qp_offset_minus1 | se(v)
pps_act_cr_qp_offset_minus3 | se(v)
if( pps_joint_cbcr_qp_offset_present_flag ) | 
pps_act_cbcr_qp_offset_minus1 | se(v)
} | 
… | 
} | 

## Slide 5
ACT QP Clipping
It is proposed to clip the QP values of ACT to valid QP range (JVET-Q0511)
  TS mode
  Non-TS mode

## Slide 6
Lossless results

## Slide 7
Lossy results
YCgCo-R + chroma transform skip

## Slide 8
Lossy results
YCgCo-R only