## Slide 1: JVET-Q0511: On ACT QP clipping
LG ELECTRONICS
Kwai
Bytedance

## Slide 2: Introduction
In October meeting, Adaptive Colour Transform (ACT) was adopted for 444 content to reduce redundancy among colour components .
Since ACT forward transform is not normalized, predefined ACT QP offsets (-5, -5 or -3) are applied to the QP for transform coefficient scaling process to compensate the dynamic range change between colour components
In VVC 7, the QP modified by ACT QP offsets may result in out of bound QP, this proposal proposes a bug fix.

## Slide 3: Background
In VVC7, the quantization parameter qP for Scaling process for transform coefficients is modified by ACT QP offsets as follows:
– If transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0, the following applies:
qP = qP + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset : 0 ) (1133)
– Otherwise (transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1), the following applies:
qP = Max( QpPrimeTsMin, qP ) + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset : 0 ) (1136)
Note: actQpOffset is -5 or -3 depending on component.

## Slide 4: Problem statement
qP = qP + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset: 0 )
qP = Max( QpPrimeTsMin, qP ) + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset : 0 ) (1136)
Problem: The modified qP can become out of range:
For low QP, it may become negative.
In Transform skip mode, it may become lower than the QpPrimeTsMin which is the minimum allowed QP for transform skip mode.
In the case that other actQPOffset values are used, the modified QP may go out of range at upper bound as well.

## Slide 5: Proposed
Propose to clip the modified Qp used for the scaling process.
8.7.3 Scaling process for transform coefficients
…
The quantization parameter qP is modified as follows:
If transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 0, the following applies:
qP = qP + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset : 0 )
qP = Clip3(0, 63+ QpBdOffset, qP + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset : 0 ) )
Otherwise (transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1), the following applies:
qP = Max( QpPrimeTsMin, qP ) + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpoffset : 0 )
qP = Clip3( QpPrimeTsMin, 63+ QpBdOffset, qP + ( cu_act_enabled_flag[ xTbY ][ yTbY ] ? actQpOffset : 0 ) )

## Slide 6: Results ( Low QP Dual Tree Off)
 |  |  | All Intra Main10 |  | 
 | Over VTM7.1 ACT ON |  |  |  | 
 | Y | U | V | EncT | DecT
RGB, TGM 1080p | -0.61% | -0.41% | -0.41% | 100% | 100%
RGB, TGM 720p | -0.26% | -0.19% | -0.18% | 100% | 100%
RGB, Animation | 0.00% | 0.00% | 0.01% | 100% | 99%
RGB, Mixed content | -0.32% | -0.24% | -0.19% | 100% | 100%
RGB, Camera-Captured content | 0.00% | 0.00% | 0.00% | 101% | 100%
YUV, TGM 1080p | 0.00% | 0.00% | 0.00% | 101% | 100%
YUV, TGM 720p | 0.00% | 0.00% | 0.00% | 100% | 100%
YUV, Animation | 0.00% | 0.00% | 0.00% | 100% | 100%
YUV, Mixed content | 0.00% | 0.00% | 0.00% | 100% | 100%
YUV, Camera-Captured content | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall (RGB) | -0.32% | -0.22% | -0.21% | 100% | 100%
Overall (YUV) | 0.00% | 0.00% | 0.00% | 100% | 100%
Tested on RGB and YUV444 sequences at low QP (2,7,12,17), dualItree Off, ACT on.
The bug fix has small gain of -0.32%, -0.1%, -0.07% in AI,RA, LD for RGB sequences due to clipping to QpPrimeTsMin.

## Slide 7: Results ( Low QP Dual Tree Off)
RA and LD results
 |  |  | Random access Main10 |  | 
 | Over VTM7.1 ACT ON |  |  |  | 
 | Y | U | V | EncT | DecT
RGB, TGM 1080p | -0.17% | -0.01% | -0.02% | 100% | 100%
RGB, TGM 720p | -0.05% | -0.09% | 0.00% | 101% | 100%
RGB, Animation | 0.00% | -0.05% | -0.07% | 100% | 99%
RGB, Mixed content | -0.17% | -0.01% | -0.04% | 100% | 100%
RGB, Camera-Captured | 0.00% | 0.00% | 0.00% | 100% | 100%
YUV, TGM 1080p | 0.00% | 0.02% | -0.01% | 100% | 100%
YUV, TGM 720p | 0.00% | -0.02% | 0.00% | 100% | 100%
YUV, Animation | 0.00% | 0.00% | -0.01% | 100% | 100%
YUV, Mixed content | 0.01% | 0.01% | 0.01% | 100% | 100%
YUV, Camera-Captured | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall (RGB) | -0.10% | -0.03% | -0.02% | 100% | 100%
Overall (YUV) | 0.00% | 0.00% | 0.00% | 100% | 100%
 |  | Low delay B Main10 |  | 
Over VTM7.1 ACT ON |  |  |  | 
Y | U | V | EncT | DecT
-0.21% | -0.15% | -0.11% | 100% | 100%
-0.04% | -0.07% | -0.09% | 99% | 99%
0.05% | -0.03% | -0.04% | 100% | 100%
-0.03% | 0.07% | 0.06% | 100% | 100%
0.00% | 0.00% | 0.00% | 100% | 100%
-0.02% | -0.01% | 0.00% | 100% | 100%
-0.03% | -0.03% | -0.01% | 101% | 101%
-0.01% | 0.01% | -0.01% | 100% | 100%
-0.01% | 0.04% | 0.01% | 101% | 100%
0.00% | 0.00% | 0.00% | 101% | 100%
-0.07% | -0.05% | -0.05% | 100% | 100%
-0.01% | 0.00% | 0.00% | 100% | 100%

## Slide 8: Conclusion
Propose to fix the bug that can result the QP for scaling process going out of bound.
Propose to adopt this bug fix into WD and VTM.
Thanks for Sony for cross-checking (JVET-Q0620).