## Slide 1
JVET-P0517
On RPR down-sampling filters for affine mode
Xiaoyu Xiu, Yi-Wen Chen, Tsung-chuan Ma, Hong-Jheng Jhu, Xianglin Wang

## Slide 2: Summary of proposal
Down-sampling filters are proposed for affine mode in RPR
  6-tap luma down-sampling filters are derived from the existing 8-tap luma down-sampling filters for non-affine mode.
  4-tap chroma down-sampling filters for non-affine mode are reused.
 | PSNR1 |  | PSNR2 | 
 | 2X | 1.5X | 2X | 1.5X
CTC sequences | -0.19% | -0.14% | -0.16% | -0.12%
Affine sequences | -1.88% | -1.06% | -1.57% | -0.84%

## Slide 3: Down-sampling filters in RPR
Additional down-sampling filters are only applied to the motion compensation of non-affine mode
  2X: 8/4-tap: cosine windowed sinc filters
  1.5X: 8/4-tap Lanczos filters
  The 6-tap/4-tap MCIF filters are applied to the motion compensation of non-affine mode
  Nearly all-pass filters
  Strong aliasing artifacts

## Slide 4: Proposal
Down-sampling filters to replace the MCIF filters for affine mode
  Same filter length and precision as existing affine MCIF filters
  Luma down-sampling filters are derived from the existing luma down-sampling filters for non-affine mode
  Chroma down-sampling filters for non-affine mode are reused

## Slide 5: Proposal
Luma down-sampling filters for affine mode
Fractional sample | interpolation filter coefficients |  |  |  |  |  |  | 
 | P0 | P1 | P2 | P3 | P4 | P5 | P6 | P7
0 | −4 | 2 | 20 | 28 | 20 | 2 | −4 | 0
1 | −4 | 0 | 19 | 29 | 21 | 5 | −4 | −2
2 | −4 | −1 | 18 | 29 | 22 | 6 | −4 | −2
3 | −4 | −1 | 16 | 29 | 23 | 7 | −4 | −2
4 | −4 | −1 | 16 | 28 | 24 | 7 | −4 | −2
5 | −4 | −1 | 14 | 28 | 25 | 8 | −4 | −2
6 | −3 | −3 | 14 | 27 | 26 | 9 | −3 | −3
7 | −3 | −1 | 12 | 28 | 25 | 10 | −4 | −3
8 | −3 | −3 | 11 | 27 | 27 | 11 | −3 | −3
9 | −3 | −4 | 10 | 25 | 28 | 12 | −1 | −3
10 | −3 | −3 | 9 | 26 | 27 | 14 | −3 | −3
11 | −2 | −4 | 8 | 25 | 28 | 14 | −1 | −4
12 | −2 | −4 | 7 | 24 | 28 | 16 | −1 | −4
13 | −2 | −4 | 7 | 23 | 29 | 16 | −1 | −4
14 | −2 | −4 | 6 | 22 | 29 | 18 | −1 | −4
15 | −2 | −4 | 5 | 21 | 29 | 19 | 0 | −4
Fractional sample | interpolation filter coefficients |  |  |  |  | 
 | P0 | P1 | P2 | P3 | P4 | P5
0 | -2 | 20 | 28 | 20 | 2 | −4
1 | -4 | 19 | 29 | 21 | 5 | −6
2 | −5 | 18 | 29 | 22 | 6 | −6
3 | −5 | 16 | 29 | 23 | 7 | −6
4 | −5 | 16 | 28 | 24 | 7 | −6
5 | −5 | 14 | 28 | 25 | 8 | −6
6 | −6 | 14 | 27 | 26 | 9 | −6
7 | −4 | 12 | 28 | 25 | 10 | −7
8 | −6 | 11 | 27 | 27 | 11 | −6
9 | −7 | 10 | 25 | 28 | 12 | −4
10 | −6 | 9 | 26 | 27 | 14 | −6
11 | −6 | 8 | 25 | 28 | 14 | −5
12 | −6 | 7 | 24 | 28 | 16 | −5
13 | −6 | 7 | 23 | 29 | 16 | −5
14 | −6 | 6 | 22 | 29 | 18 | −5
15 | −6 | 5 | 21 | 29 | 19 | -4
2X down-sampling filters

## Slide 6: Proposal
Fractional sample | interpolation filter coefficients |  |  |  |  | 
 | P0 | P1 | P2 | P3 | P4 | P5
0 | −4 | 17 | 42 | 17 | −5 | −1
1 | −5 | 15 | 41 | 19 | −5 | −1
2 | −5 | 13 | 40 | 21 | −4 | −1
3 | −5 | 11 | 39 | 24 | −4 | −1
4 | −5 | 9 | 38 | 26 | −3 | −1
5 | −5 | 7 | 38 | 28 | −2 | −2
6 | −4 | 5 | 36 | 30 | −1 | −2
7 | −3 | 3 | 35 | 32 | 0 | −3
8 | −3 | 2 | 33 | 33 | 2 | −3
9 | −3 | 0 | 32 | 35 | 3 | −3
10 | −2 | −1 | 30 | 36 | 5 | −4
11 | −2 | −2 | 28 | 38 | 7 | −5
12 | −1 | −3 | 26 | 38 | 9 | −5
13 | −1 | −4 | 24 | 39 | 11 | −5
14 | −1 | −4 | 21 | 40 | 13 | −5
15 | −1 | −5 | 19 | 41 | 15 | −5
Fractional sample | interpolation filter coefficients |  |  |  |  |  |  | 
 | P0 | P1 | P2 | P3 | P4 | P5 | P6 | P7
0 | −1 | −5 | 17 | 42 | 17 | −5 | −1 | 0
1 | 0 | −5 | 15 | 41 | 19 | −5 | −1 | 0
2 | 0 | −5 | 13 | 40 | 21 | −4 | −1 | 0
3 | 0 | −5 | 11 | 39 | 24 | −4 | −2 | 1
4 | 0 | −5 | 9 | 38 | 26 | −3 | −2 | 1
5 | 0 | −5 | 7 | 38 | 28 | −2 | −3 | 1
6 | 1 | −5 | 5 | 36 | 30 | −1 | −3 | 1
7 | 1 | −4 | 3 | 35 | 32 | 0 | −4 | 1
8 | 1 | −4 | 2 | 33 | 33 | 2 | −4 | 1
9 | 1 | −4 | 0 | 32 | 35 | 3 | −4 | 1
10 | 1 | −3 | −1 | 30 | 36 | 5 | −5 | 1
11 | 1 | −3 | −2 | 28 | 38 | 7 | −5 | 0
12 | 1 | −2 | −3 | 26 | 38 | 9 | −5 | 0
13 | 1 | −2 | −4 | 24 | 39 | 11 | −5 | 0
14 | 0 | −1 | −4 | 21 | 40 | 13 | −5 | 0
15 | 0 | −1 | −5 | 19 | 41 | 15 | −5 | 0
Luma down-sampling filters for affine mode
1.5X down-sampling filters

## Slide 7: Proposal
2X
Fractional sample | interpolation filter coefficients |  |  | 
 | P0 | P1 | P2 | P3
0 | 17 | 30 | 17 | 0
1 | 17 | 30 | 18 | −1
2 | 16 | 30 | 18 | 0
3 | 16 | 30 | 18 | 0
4 | 15 | 30 | 18 | 1
5 | 14 | 30 | 18 | 2
6 | 13 | 29 | 19 | 3
7 | 13 | 29 | 19 | 3
8 | 12 | 29 | 20 | 3
9 | 11 | 28 | 21 | 4
10 | 10 | 28 | 22 | 4
11 | 10 | 27 | 22 | 5
12 | 9 | 27 | 23 | 5
13 | 9 | 26 | 24 | 5
14 | 8 | 26 | 24 | 6
15 | 7 | 26 | 25 | 6
16 | 7 | 25 | 25 | 7
17 | 6 | 25 | 26 | 7
18 | 6 | 24 | 26 | 8
19 | 5 | 24 | 26 | 9
20 | 5 | 23 | 27 | 9
21 | 5 | 22 | 27 | 10
22 | 4 | 22 | 28 | 10
23 | 4 | 21 | 28 | 11
24 | 3 | 20 | 29 | 12
25 | 3 | 19 | 29 | 13
26 | 3 | 19 | 29 | 13
27 | 2 | 18 | 30 | 14
28 | 1 | 18 | 30 | 15
29 | 0 | 18 | 30 | 16
30 | 0 | 18 | 30 | 16
31 | −1 | 18 | 30 | 17
Fractional sample | interpolation filter coefficients |  |  | 
 | P0 | P1 | P2 | P3
0 | 12 | 40 | 12 | 0
1 | 11 | 40 | 13 | 0
2 | 10 | 40 | 15 | −1
3 | 9 | 40 | 16 | −1
4 | 8 | 40 | 17 | −1
5 | 8 | 39 | 18 | −1
6 | 7 | 39 | 19 | −1
7 | 6 | 38 | 21 | −1
8 | 5 | 38 | 22 | −1
9 | 4 | 38 | 23 | −1
10 | 4 | 37 | 24 | −1
11 | 3 | 36 | 25 | 0
12 | 3 | 35 | 26 | 0
13 | 2 | 34 | 28 | 0
14 | 2 | 33 | 29 | 0
15 | 1 | 33 | 30 | 0
16 | 1 | 31 | 31 | 1
17 | 0 | 30 | 33 | 1
18 | 0 | 29 | 33 | 2
19 | 0 | 28 | 34 | 2
20 | 0 | 26 | 35 | 3
21 | 0 | 25 | 36 | 3
22 | −1 | 24 | 37 | 4
23 | −1 | 23 | 38 | 4
24 | −1 | 22 | 38 | 5
25 | −1 | 21 | 38 | 6
26 | −1 | 19 | 39 | 7
27 | −1 | 18 | 39 | 8
28 | −1 | 17 | 40 | 8
29 | −1 | 16 | 40 | 9
30 | −1 | 15 | 40 | 10
31 | 0 | 13 | 40 | 11
1.5X
  Chroma down-sampling filters for non-affine mode are reused

## Slide 8: Simulations (CTC)
PSNR1
PSNR2
For ParkScene and BQSquare, the gains are 1.11% and 1.24%

## Slide 9: Simulations (Affine sequences)
PSNR1
PSNR2
 |  | Low delay B Main10 | 
 |  | Over VTM-7.0 | 
 | Y | U | V
BlueSkyPart | -0.40% | -0.05% | -0.29%
JetParts | -1.49% | -2.39% | -0.76%
ShieldsPart | -1.26% | -1.03% | -1.54%
SpincalendarPart | -4.82% | -2.92% | -5.25%
StationKtaPart | -1.47% | -0.65% | -1.35%
TratorPart | -1.86% | -0.99% | -0.70%
Overall | -1.88% | -1.34% | -1.65%
 |  | Low delay B Main10 | 
 |  | Over VTM-7.0 | 
 | Y | U | V
BlueSkyPart | -0.34% | -0.12% | -0.27%
JetParts | -2.44% | -2.49% | -1.09%
ShieldsPart | -0.93% | -0.74% | -1.16%
SpincalendarPart | -2.80% | -3.43% | -4.35%
StationKtaPart | -1.37% | -0.62% | -1.22%
TratorPart | -1.55% | -1.08% | -0.90%
Overall | -1.57% | -1.41% | -1.50%