## Slide 1
CE5-related:
CCALF coefficient derivation using combined neighbors
JVET-Q0559
Krit Panusopone, Seungwook Hong, Limin Wang, Jani Lainema

## Slide 2: CCALF (Cross-Component Adaptive Loop Filter)
Second ALF option for chroma component
Derive chroma correction based on luma pixels in the neighborhood
CCALF usage and filter choice (if needed) signaled at CTU level
Filter coefficient signaled in APS
CE5 common base, based on JVET-P1008
  4 filter choices
  3x4 filter shape
  8 coefficients
  6 bit accuracy

## Slide 3: CE5 common base filtering
Each CCALF coefficient corresponds to a luma sample
Every sample contributes equally to CCALF
sum = filterCoeff[0] * srcCross[offset2 + jj2];
sum += filterCoeff[1] * srcCross[offset0 + jj2 - 1];
sum += filterCoeff[2] * srcCross[offset0 + jj2];
sum += filterCoeff[3] * srcCross[offset0 + jj2 + 1];
sum += filterCoeff[4] * srcCross[offset1 + jj2 - 1];
sum += filterCoeff[5] * srcCross[offset1 + jj2];
sum += filterCoeff[6] * srcCross[offset1 + jj2 + 1];
sum += filterCoeff[7] * srcCross[offset3 + jj2];

## Slide 4: Proposed method 1
sum = filterCoeff[0] * srcCross[offset2 + jj2];
sum += filterCoeff[1] * ((srcCross[offset0+jj2-1]+srcCross[offset1+jj2-1] + 1)>>1);
sum += filterCoeff[2] * srcCross[offset0 + jj2];
sum += filterCoeff[3] * srcCross[offset1 + jj2];
sum += filterCoeff[4] * ((srcCross[offset0+jj2+1]+srcCross[offset1+jj2+1] + 1)>>1);
sum += filterCoeff[5] * srcCross[offset3 + jj2];
4x3 filter shape, 6 coefficients
Left most pair samples
Right most pair samples

## Slide 5: Proposed method 2
sum = filterCoeff[0] * srcCross[offset2 + jj2];
sum += filterCoeff[1] * ((srcCross[offset0+jj2-2]+srcCross[offset1+jj2-2] + 1)>>1);
sum += filterCoeff[2] * ((srcCross[offset0+jj2-1]+srcCross[offset1+jj2-1] + 1)>>1);
sum += filterCoeff[3] * srcCross[offset0 + jj2];
sum += filterCoeff[4] * srcCross[offset1 + jj2];
sum += filterCoeff[5] * ((srcCross[offset0+jj2+1]+srcCross[offset1+jj2+1] + 1)>>1);
sum += filterCoeff[6] * ((srcCross[offset0+jj2+2]+srcCross[offset1+jj2+2] + 1)>>1);
sum += filterCoeff[7] * srcCross[offset3 + jj2];
5x3 filter shape, 8 coefficients
Left most pair samples
Right most pair samples
Second-to-left most pair samples
Second-to-right most pair samples

## Slide 6: Simulation Results
Method 1: 4x3 filter shape, 6 coefficients
 |  |  |  |  | Over CE5 common base |  |  |  | 
 | All Intra (0.02% combined BD-rate) |  |  | Random access (0.00% combined BD-rate) |  |  | Low delay B (-0.02% combined BD-rate) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | -0.01% | 0.05% | 0.08% | 0.01% | -0.15% | 0.08% |  |  | 
Class A2 | 0.00% | -0.01% | -0.17% | 0.00% | 0.19% | 0.22% |  |  | 
Class B | -0.01% | 0.18% | 0.09% | 0.00% | 0.11% | -0.07% | 0.00% | -0.08% | -0.17%
Class C | -0.03% | 0.06% | 0.04% | -0.02% | -0.07% | -0.10% | 0.03% | 0.13% | -0.15%
Class E | -0.03% | 1.01% | 0.16% |  |  |  | -0.05% | 0.05% | -0.29%
Overall | -0.02% | 0.24% | 0.05% | -0.01% | 0.02% | 0.01% | 0.00% | 0.02% | -0.19%
Class D | -0.01% | -0.05% | -0.18% | -0.03% | -0.12% | 0.01% | -0.01% | -0.28% | -0.78%
Class F | -0.03% | 0.06% | 0.05% | -0.02% | 0.10% | -0.05% | 0.04% | -0.04% | 0.33%

## Slide 7: Simulation Results
Method 2: 5x3 filter shape, 8 coefficients
 |  |  |  |  | Over CE5 common base |  |  |  | 
 | All Intra (-0.12% combined BD-rate) |  |  | Random access (-0.16% combined BD-rate) |  |  | Low delay B (-0.29% combined BD-rate) |  | 
 | Y | U | V | Y | U | V | Y | U | V
Class A1 | 0.02% | -0.27% | -1.09% | 0.03% | -0.73% | -1.04% |  |  | 
Class A2 | 0.00% | -1.01% | -1.05% | -0.02% | -0.81% | -0.64% |  |  | 
Class B | 0.00% | -0.68% | -1.03% | 0.02% | -0.73% | -1.29% | -0.01% | -1.78% | -1.23%
Class C | 0.01% | -0.48% | -0.63% | -0.02% | -0.43% | -0.62% | 0.01% | -1.42% | -1.09%
Class E | 0.02% | 0.50% | -0.63% |  |  |  | -0.03% | -0.39% | -2.62%
Overall | 0.01% | -0.42% | -0.89% | 0.00% | -0.67% | -0.93% | -0.01% | -1.31% | -1.53%
Class D | 0.01% | -0.69% | -0.74% | -0.03% | -0.38% | -0.92% | -0.04% | -1.44% | -1.62%
Class F | 0.01% | -0.77% | -0.61% | 0.01% | -0.63% | -0.66% | 0.06% | -1.30% | -0.57%

## Slide 8: Conclusions
Combine less correlated neighbor for CCALF operations
Simple average between a pair of luma samples
Minor changes in covariance calculation and filter block functions
Method 1 uses 6 coefficients, compared to 8 in CE5 common base
  Similar coding efficiency; 0.02%, 0.00%, -0.02% for AI, RA, LB against CE5 common base
Method 2 uses 8 coefficients, same as in CE5 common base
  Combined BD-rate gains of -0.12%,-0.16%, -0.29% for AI, RA, LB against CE5 common base