## Slide 1
JVET-R0096
AHG9: On signaling of chroma residual scaling
2020/4/11

## Slide 2
Problem statement
In current VVC draft, if a picture contains multiple slices, the chroma residual scaling cannot be independently controlled for individual slices.
In this simple example, the current VVC draft does NOT allow following combination:
Slice 1: Luma mapping ON and Chroma residual scaling OFF
Slice 2: Luma mapping ON and Chroma residual scaling ON

## Slide 3
Proposed method : Method 1
Move chroma residual scale flag from PH to SH
if( sps_lmcs_enabled_flag ) { | 
ph_lmcs_enabled_flag | u(1)
if( ph_lmcs_enabled_flag ) { | 
ph_lmcs_aps_id | u(2)
if( ChromaArrayType != 0 ) | 
ph_chroma_residual_scale_flag | u(1)
} | 
} | 
if( ph_lmcs_enabled_flag ){ | 
slice_lmcs_enabled_flag | u(1)
if(slice_lmcs_enabled_flag && ChromaArrayType != 0 ) | 
slice_chroma_residual_scale_enabled_flag | u(1)
} | 
PH
SH

## Slide 4
Proposed method : Method 2
Chroma residual scaling can be controlled both in picture level and in slice level.
if( sps_lmcs_enabled_flag ) { | 
ph_lmcs_enabled_flag | u(1)
if( ph_lmcs_enabled_flag ) { | 
ph_lmcs_aps_id | u(2)
if( ChromaArrayType != 0 ) | 
ph_chroma_residual_scale_flag | u(1)
} | 
} | 
if( ph_lmcs_enabled_flag ){ | 
slice_lmcs_enabled_flag | u(1)
if(slice_lmcs_enabled_flag && ph_chroma_residual_scale_flag ) | 
slice_chroma_residual_scale_enabled_flag | u(1)
} | 
PH
SH

## Slide 6
Backup: Consistency with other loop filters
if( sps_alf_enabled_flag && !alf_info_in_ph_flag ) {
slice_alf_enabled_flag
if( slice_alf_enabled_flag ) {
slice_num_alf_aps_ids_luma
for( i = 0; i < slice_num_alf_aps_ids_luma; i++ )
slice_alf_aps_id_luma[ i ]
if( ChromaArrayType != 0 )
slice_alf_chroma_idc
if( slice_alf_chroma_idc )
slice_alf_aps_id_chroma
if( sps_ccalf_enabled_flag ) {
slice_cc_alf_cb_enabled_flag
if( slice_cc_alf_cb_enabled_flag )
slice_cc_alf_cb_aps_id
slice_cc_alf_cr_enabled_flag
if( slice_cc_alf_cr_enabled_flag )
slice_cc_alf_cr_aps_id
}
}
if( sps_sao_enabled_flag && !sao_info_in_ph_flag ) {
slice_sao_luma_flag
if( ChromaArrayType != 0 )
slice_sao_chroma_flag
}
if( deblocking_filter_override_enabled_flag && !dbf_info_in_ph_flag ) | 
slice_deblocking_filter_override_flag | u(1)
if( slice_deblocking_filter_override_flag ) { | 
slice_deblocking_filter_disabled_flag | u(1)
if( !slice_deblocking_filter_disabled_flag ) { | 
slice_beta_offset_div2 | se(v)
slice_tc_offset_div2 | se(v)
slice_cb_beta_offset_div2 | se(v)
slice_cb_tc_offset_div2 | se(v)
slice_cr_beta_offset_div2 | se(v)
slice_cr_tc_offset_div2 | se(v)
} | 
} | 
ALF
SAO
Deblocking