## Slide 1: JVET-R0208: AHG16: Rounding correction for ALF virtual boundary processing Anand Meher Kotra, S. Esenlik, B. Wang, H. Gao, E. Alshina

## Slide 2: Introduction
ALF essentially acts as a 1D filter for the case shown in Fig. below and this *may* generate visual artifacts when there are structural edges passing through the ALF virtual boundary (VB)
JVET-Q0150 (solution 2) was adopted in the Brussels meeting to address the above problem
  solves the problem by attenuating the ALF filter by increasing the quantization of the correction value during filtering

## Slide 3: JVET-Q0150 Spec. text changes
Condition | alfShiftY | y1 | y2 | y3
( y = = CtbSizeY − 5 ¦ ¦ y = = CtbSizeY − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 10 | 0 | 0 | 0
( y = = CtbSizeY − 6 ¦ ¦ y = = CtbSizeY − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 1 | 1 | 1
( y = = CtbSizeY − 7 ¦ ¦ y = = CtbSizeY − 2 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 1 | 2 | 2
otherwise | 7 | 1 | 2 | 3
sum = curr + ( ( sum + 64 ) >> alfShiftY )
ALF Luma filter changes:
ALF Chroma filter changes:
Condition | alfShiftC | y1 | y2
( y = = ctbHeightC − 2 ¦ ¦ y = = ctbHeightC − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 10 | 0 | 0
( y = = ctbHeightC − 1 ¦ ¦ y = = ctbHeightC − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 1 | 1
Otherwise | 7 | 1 | 2
sum = curr + ( ( sum + 64 ) >> alfShiftC )

## Slide 4: Problem
The rounding value in the following equations, is not changed, even if the quantization value is increased
We identified two more proposals targeting the same problem
  JVET-R0231 (Method 1)
  JVET-R0291 (proposal (a))
sum = curr + ( ( sum + 64 ) >> alfShiftY )
sum = curr + ( ( sum + 64 ) >> alfShiftC )

## Slide 5: Solution (Fix the rounding correction)
sum = curr + ( ( sum + 64 roundY ) >> alfShiftY ) (1467)
sum = curr + ( ( sum + 64 roundC ) >> alfShiftC ) (1508)
Specification text changes and software are attached along with the contribution
Condition | alfShiftY | roundY | y1 | y2 | y3
( y = = CtbSizeY − 5 ¦ ¦ y = = CtbSizeY − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 10 | 512 | 0 | 0 | 0
( y = = CtbSizeY − 6 ¦ ¦ y = = CtbSizeY − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 64 | 1 | 1 | 1
( y = = CtbSizeY − 7 ¦ ¦ y = = CtbSizeY − 2 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 64 | 1 | 2 | 2
otherwise | 7 | 64 | 1 | 2 | 3
Condition | alfShiftC | roundC | y1 | y2
( y = = ctbHeightC − 2 ¦ ¦ y = = ctbHeightC − 3 ) && ( applyAlfLineBufBoundary = = 1 ) | 10 | 512 | 0 | 0
( y = = ctbHeightC − 1 ¦ ¦ y = = ctbHeightC − 4 ) && ( applyAlfLineBufBoundary = = 1 ) | 7 | 64 | 1 | 1
Otherwise | 7 | 64 | 1 | 2

## Slide 6: Simulation Results
 | All Intra Main10 |  |  |  | 
 | Over VTM 8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.02% | 100% | 99%
Class A2 | 0.00% | 0.01% | 0.01% | 100% | 99%
Class B | 0.00% | 0.01% | 0.01% | 100% | 100%
Class C | 0.00% | 0.01% | 0.01% | 100% | 99%
Class E | 0.00% | 0.01% | 0.02% | 99% | 99%
Overall | 0.00% | 0.01% | 0.01% | 100% | 99%
Class D | 0.00% | 0.00% | 0.00% | 100% | 99%
Class F | 0.00% | 0.01% | 0.01% | 100% | 99%
 | Random Access Main 10 |  |  |  | 
 | Over VTM 8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.14% | -0.06% | 100% | 100%
Class A2 | 0.00% | 0.05% | 0.13% | 100% | 100%
Class B | 0.02% | -0.02% | -0.02% | 100% | 100%
Class C | 0.01% | 0.05% | -0.02% | 100% | 99%
Class E |  |  |  |  | 
Overall | 0.01% | -0.01% | 0.00% | 100% | 100%
Class D | 0.00% | 0.06% | -0.12% | 100% | 99%
Class F | 0.00% | -0.04% | -0.04% | 100% | 99%
 | Low delay B Main10 |  |  |  | 
 | Over VTM 8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.15% | 0.12% | 101% | 103%
Class C | 0.00% | -0.21% | -0.15% | 100% | 100%
Class E | 0.06% | 0.11% | -0.29% | 100% | 102%
Overall | 0.01% | 0.02% | -0.07% | 100% | 102%
Class D | 0.00% | -0.68% | -0.45% | 99% | 100%
Class F | -0.03% | 0.23% | -0.18% | 100% | 101%
 | Low delay P Main10 |  |  |  | 
 | Over VTM 8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.05% | 0.16% | 100% | 104%
Class C | 0.01% | -0.14% | -0.33% | 100% | 103%
Class E | 0.01% | -0.72% | -0.37% | 100% | 102%
Overall | 0.01% | -0.25% | -0.14% | 100% | 103%
Class D | -0.03% | 0.10% | -0.51% | 99% | 100%
Class F | 0.01% | -0.11% | -0.65% | 100% | 102%