## Slide 1: JVET-R0212 GPM with reduced modes
Christopher Hollmann, Du Liu,
Ruoyang Yu, Jacob Ström
Ericsson Research
Christopher Hollmann
Ericsson Research
2020-04-09

## Slide 2: Introduction
GPM adopted at last meeting with 64 modes
20 angles with 2-4 distances:
  Angles 0, 5, 10 and 15: only distance 1 and 3 (8 total)
  Angles 11…14 and 16…19: only distance 1, 2 and 3 (24 total)
  Angles 1…4 and 6…9: distances 0-3 (32 total)
14 different block sizes allowed
  MxN with N = {8, 16, 32, 64} and M = {8, 16, 32, 64}
  Exception: 8x64 and 64x8 are not allowed
Possible combinations (required for verification testing): 14 * 64 = 896
0
1
2
3
4
5
6
7
8
9
10
11
19
18
17
16
15
14
13
12

## Slide 3: Method 1: 50 modes
Remove angles 4, 6, 14 and 16 (-14 modes)
New angle distribution:
  Angles 0, 5, 10 and 15: only distance 1 and 3 (8 total)
  Angles 11…13 and 17…19: only distance 1, 2 and 3 (18 total)
  Angles 1…3 and 7…9: distances 0-3 (24 total)
Combinations:
  14 * 50 = 700 (-22%)
0
1
2
3
4
5
6
7
8
9
10
11
19
18
17
16
15
14
13
12

## Slide 4: Method 2: 38 modes
Remove angles 4, 6, 14 and 16 (-14 modes)
Remove distance 2 from all angles (-12 modes)
New angle distribution:
  Angles 0, 5, 10 and 15: only distance 1 and 3 (8 total)
  Angles 11…13 and 17…19: only distance 1 and 3 (12 total)
  Angles 1…3 and 7…9: distances 0, 1 and 3 (18 total)
Combinations:
  14 * 38 = 532 (-40%)
0
1
2
3
4
5
6
7
8
9
10
11
19
18
17
16
15
14
13
12

## Slide 5: Method 3: 32 modes
Remove angles 4, 6, 14 and 16 (-14 modes)
Remove distance 2 from all angles (-12 modes)
Remove distance 0 from all angles (-6 modes)
New angle distribution:
  Angles 0, 5, 10 and 15: only distance 1 and 3 (8 total)
  Angles 11…13 and 17…19: only distance 1 and 3 (12 total)
  Angles 1…3 and 7…9: distances 1 and 3 (12 total)
Combinations:
  14 * 32 = 448 (-50%)
0
1
2
3
4
5
6
7
8
9
10
11
19
18
17
16
15
14
13
12

## Slide 6: Compression performance
​ | GPM Modes​ | BDR RA​ | BDR LD​ | Combinations​
VTM-8.0​ | 64​ | 0.00%​ | 0.00%​ | 896​
VTM-8.0 w/o GPM​¹ | 0​ | 0.66%​ | 1.50%​ | 0 (-100%)
Method 1​ | 50​ | 0.03%​ | 0.00%​ | 700 (-22%)
Method 2​ | 38​ | 0.05%​ | 0.01%​ | 532 (-40%)
Method 3​ | 32​ | 0.07%​ | 0.06%​ | 448 (-50%)
¹ Taken from AHG13 tests

## Slide 7: Conclusion
3 different methods to reduce the number of modes in GPM
Reduction of combinations required for verification testing by up to 50%
Proposal: Adopt the most suitable trade-off into VVC
Thanks to Bytedance for crosschecking!

## Slide 9: Method 1 – detailed results
 | Random Access |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.07% | -0.01% | 100% | 100%
Class A2 | 0.04% | 0.08% | 0.18% | 100% | 99%
Class B | 0.02% | -0.05% | 0.00% | 99% | 100%
Class C | 0.06% | 0.21% | 0.13% | 97% | 98%
Class E |  |  |  |  | 
Overall | 0.03% | 0.04% | 0.07% | 99% | 99%
Class D | 0.02% | 0.13% | 0.02% | 97% | 100%
Class F | 0.02% | 0.02% | -0.03% | 98% | 100%
 | Low delay B |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | 0.23% | -0.04% | 98% | 100%
Class C | -0.03% | -0.08% | 0.02% | 99% | 97%
Class E | 0.05% | 0.36% | -0.18% | 98% | 101%
Overall | 0.00% | 0.16% | -0.05% | 98% | 99%
Class D | -0.03% | -0.47% | 0.03% | 96% | 99%
Class F | 0.06% | 0.63% | -0.15% | 99% | 102%

## Slide 10: Method 2 – detailed results
 | Random Access |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.03% | -0.03% | 99% | 100%
Class A2 | 0.05% | 0.08% | 0.18% | 99% | 99%
Class B | 0.03% | -0.07% | -0.02% | 98% | 100%
Class C | 0.10% | 0.20% | 0.09% | 96% | 99%
Class E |  |  |  |  | 
Overall | 0.05% | 0.05% | 0.05% | 98% | 100%
Class D | 0.04% | 0.14% | -0.05% | 95% | 100%
Class F | 0.02% | 0.05% | -0.05% | 96% | 101%
 | Low delay B |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | 0.02% | -0.04% | 98% | 99%
Class C | -0.01% | -0.10% | 0.05% | 98% | 100%
Class E | 0.06% | 0.22% | 0.15% | 97% | 102%
Overall | 0.01% | 0.03% | 0.04% | 98% | 100%
Class D | -0.02% | -0.34% | 0.02% | 95% | 101%
Class F | -0.06% | 0.54% | 0.44% | 96% | 99%

## Slide 11: Method 3 – detailed results
 | Random Access |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | 0.04% | 0.06% | 107% | 100%
Class A2 | 0.06% | 0.02% | 0.19% | 106% | 102%
Class B | 0.05% | 0.07% | 0.05% | 109% | 102%
Class C | 0.11% | 0.30% | 0.25% | 106% | 101%
Class E |  |  |  |  | 
Overall | 0.07% | 0.11% | 0.13% | 107% | 101%
Class D | 0.02% | 0.23% | 0.02% | 99% | 101%
Class F | 0.03% | 0.06% | 0.00% | 103% | 97%
 | Low delay B |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.01% | 0.21% | -0.03% | 106% | 101%
Class C | 0.02% | -0.04% | 0.08% | 106% | 100%
Class E | 0.18% | 0.73% | -0.38% | 107% | 102%
Overall | 0.06% | 0.26% | -0.08% | 106% | 101%
Class D | 0.03% | -0.52% | -0.01% | 107% | 100%
Class F | 0.00% | 0.25% | -0.24% | 109% | 102%