## Slide 1: JVET-R0230: AHG2: Syntax clean-up for cross component adaptive loop filter
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2
 | Filters in an APS | APS id in SH/PH
Chroma ALF in VTM8 | Up to 8 chroma ALF filters | One chroma APS id
CCALF in VTM8 | Up to 4 Cb CCALF filters + Up to 4 Cr CCALF filters | One Cb CCALF APS id + One Cr CCALF APS id
Proposed CCALF | Up to 8 CCALF filters | One CCALF APS id

## Slide 3: Results
Thank Alibaba for cross-checking
 | All Intra Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | -0.09% | -0.04% | 101% | 100%
Class A2 | 0.04% | -0.05% | -0.78% | 101% | 97%
Class B | 0.03% | -0.46% | 0.06% | 101% | 99%
Class C | 0.02% | -0.08% | -0.19% | 100% | 99%
Class E | 0.01% | -0.03% | -0.21% | 100% | 95%
Overall | 0.03% | -0.17% | -0.20% | 100% | 98%
Class D | 0.01% | -0.02% | -0.16% | 101% | 96%
Class F | 0.01% | -0.08% | -0.03% | 101% | 100%
 | Random access Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | -0.03% | 0.16% | 101% | 100%
Class A2 | 0.02% | -0.07% | -0.19% | 101% | 100%
Class B | 0.02% | -0.19% | 0.31% | 102% | 100%
Class C | 0.00% | -0.07% | -0.13% | 101% | 101%
Class E |  |  |  |  | 
Overall | 0.01% | -0.10% | 0.06% | 101% | 100%
Class D | 0.00% | -0.11% | 0.00% | 101% | 101%
Class F | 0.03% | 0.02% | -0.14% | 101% | 100%
 | Low delay B Main10 |  |  |  | 
 | Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.11% | 0.02% | 100% | 98%
Class C | -0.08% | -0.39% | 0.09% | 101% | 103%
Class E | -0.03% | 0.06% | -0.33% | 101% | 105%
Overall | -0.04% | -0.16% | -0.04% | 101% | 101%
Class D | -0.06% | -0.09% | -0.45% | 101% | 104%
Class F | 0.00% | 0.34% | 0.29% | 100% | 99%